## Slide 1
Unregistered Distribution Generation Data Collection and Maintenance
Joel Koepke
April 2026

## Slide 2: NPRR1265 Language to be Unboxed on June 1 – Section 2

## Slide 3: NPRR1265 Language to be Unboxed on June 1 – Section 3.2.5.1
3.2.5.1 describes the process to collect UDG information from DSPs, pass to TSPs, and provide to ERCOT

## Slide 4: Additional UDG Attributes for CIM Loads
Transformers between the transmission system and distribution system are modeled as individual load points
These “CIM loads” will be given new attributes quantifying the UDG characteristics of the connected distribution system
Transmission
Distribution
Example UDG attributes for loads in the model
Transformers represented as load points
In the field
In the model

## Slide 5: UDG Data for Operations and Planning Use Cases
The ERCOT Network Operations Model (NOM) will be extended to hold Unregistered Distribution Generation (UDG) data
The NOM, containing the new UDG data, will be used in operations and as the starting point for each planning build cycle
Energy Management System
Market Management System
Forecasting
SSWG Case Building
RPG and LTSA Activities
UDG Data
UDG Data
UDG Data
UDG Data submitted within the NOM can be incorporated into the planning case builds where needed

## Slide 6: UDG in Planning Models and Studies
UDG will be included in the Planning cases as discrete generators and not embedded in the load forecast.
A script will synchronize the UDG information in NMMS with MOD like we do for SODG.
They will be aggregated by fuel type on a bus.
The bus will be in the 800,000 range.
Dispatching
  Wind and Solar UDG will be dispatched at the same value of transmission wind and solar
  All other UDG will be offline
UDGs will be modeled at unity PF.

## Slide 7: Timeline: NPRR1265 Unboxing and Data Collection
Complete – ERCOT posts draft pre-populated UDG template to MIS
Complete – UDG Workshop #3
June 1 – Unbox NPRR1265 items
  Includes 3.2.5.1 Unregistered Distributed Generator Reporting Requirements
Protocol-Driven Dates
  By Jan. 15, 2027 – ERCOT posts pre-populated UDG template to ERCOT MIS
  By Feb 1, 2027 – DSP provides aggregated UDG information to TSP
  By March 30, 2027 – TSP submits updated UDG information to ERCOT
May 1, 2027 – ERCOT posts UDG report
October 2027 – UDG Information in ERCOT Planning Cases
By Jan.15, 2028 – ERCOT posts pre-populated UDG template containing previous year’s response to ERCOT MIS

## Slide 8: Draft Pre-Populated Template
ERCOT has posted a draft pre-populated UDG template to the MIS website
  Prior to unboxing, the template will reside in the Requested Information location
    https://mis.ercot.com/secure/data-products/data-product-details?id=np12-230
  Post unboxing, a new MIS location will be created
    EMIL-ID and URL will be announced via Market Notice
Notes: Note that when the meeting content is posted, the pre-populated template may not yet be in the Requested Information location. The information will available prior to the UDG workshop.

## Slide 9: UDG Data Update Process
ERCOT will facilitate a yearly process to request, collect, and incorporate updates to UDG information into the model
Pre-populated files will be generated containing all associated loads
A single file will be provided to each TSP via the MIS
An updated worksheet will be submitted to ERCOT
Via internal processes the TSP will update the UDG data within the spreadsheet
1.
2.
3.
4.
ERCOT
Transmission Service Provider
Internal Processes
Download
ERCOT MIS
Pre
-
Populated
UDG
Worksheet
Final URL TBD
(TSP
-
Specific Location)
Operations Modeling
Application
(NMMS)
Pre
-
Populated
UDG
Worksheet
Pre
-
Populated
UDG
Worksheet
Pre
-
Populated
UDG
Worksheet
Updated UDG
Worksheet
Updated UDG
Worksheet
Files generated
for each TSP
Worksheets posted
to MIS
Worksheet submitted to
ERCOT
Changes
imported
Corrections
requested
DSP

## Slide 10: Draft Pre-Populated UDG Worksheet
ERCOT has posted a pre-populated template worksheet containing all loads associated to TDSPs.
The initial columns of the worksheet are populated by ERCOT, and the contents should not be modified.
Subsequent columns are to be updated, if necessary, by TSPs/DSPs with the required UDG information

## Slide 11: Example: Different UDG Characteristics at One CIM Load
To accommodate UDG that cannot be aggregated together, additional rows have been added
Common types cannot be combined if they have a different 1547 vintage
Different UDG types cannot be aggregated into a single row

## Slide 12: Draft UDG Types
Draft form allows the following UDG types (captured from the protocols):
  Solar
  Wind
  Natural Gas
  Diesel
  Energy Storage, and
  Other
ERCOT is open to additional DG types if need is present

## Slide 13: Next Steps
Download the draft pre-populated template from the ERCOT MIS
  Requested Information Link
Review template and provide feedback at upcoming NDSWG meetings
  NDSWG Schedule Link
Discuss implementation in Planning cases at SSWG meetings
Monitor Market Notices for Updated Templates and Potential Additional Meetings