## Slide 1
NPRR 1214
ERCOT Comments
PRS
Sai Moorty
June 10, 2026

## Slide 2: NPRR 1214: ERCOT Comments @ PRS June 10, 2026
ERCOT's proposed changes keep or enhance the original intent of NPRR 1214 and streamline Nodal Protocol language.
Reason for the proposed changes:
  During the Impact Analysis phase, certain issues with NPRR1214 language were uncovered.
  More recently, the importance of modeling reliability deployments at their location has been highlighted.
  Add new reliability deployment categories for Load and SOG
Summary of Changes:
  Locational modeling of some categories of reliability deployments.
  Directly use the SCED Step 2 Pricing Run, when active, as the source of binding locational energy prices (LMPs) and Ancillary Service prices (AS MCPCs) — eliminating the need for energy and Ancillary Service Price Adders.
  Enhance the accuracy of the Reliability Deployment Indifference Payment.

## Slide 3: Locational Modeling of Reliability Deployments
ERCOT-directed deployment of AS from Load Resources that are not CLRs
ERCOT-directed deployment of Voluntary Early Curtailment Load (VECL)
ERCOT-directed deployment of Load under PURA § 37.0561, Must Run Alternative (MRA), or Contract for Capacity (new category)
ERCOT-directed deployment of SOG under MRA or Contract for Capacity (new category)
Newly modeled locationally (with sufficient XML message data):
Already modeled locationally (unchanged):
RUC, RMR, and Offline Non-Spinning Reserve Service (NSPIN)
ERCOT-directed DC Tie import/export changes (updated: pseudo-ESR replaced by pseudo-CLR or pseudo-GR)
Not modeled locationally (unchanged):
ERS | BLT in/out | TDSP standard offer load management program
Distribution voltage reduction measures | ERCOT-directed Firm Load Shed under EEA Level 3

## Slide 4: Replace Energy Price Adders with Direct SCED Pricing Run LMPs
Previous NPRR1214 approach:
Final LMP = SCED Dispatch Run LMP + Energy Price Adder
Energy Price Adder = SCED Pricing Run LMP − SCED Dispatch Run LMP
∴ Final LMP = SCED Pricing Run LMP (when active) or Dispatch Run LMP (when inactive)
ERCOT's proposed approach:
Use SCED Pricing Run LMPs directly when the Pricing Run is active; otherwise use SCED Dispatch Run LMPs.
Eliminates the need to calculate and maintain three sets of energy price adders:
  SCED interval energy price adders for every Electrical Bus
  Settlement Interval price adders for each Settlement Point
  Settlement Interval Meter price adders for every meter
Result: Simpler, more direct Protocol language with the same pricing outcome — and fewer intermediate calculations.

## Slide 5: Replace AS MCPC Price Adders with Direct SCED Pricing Run MCPCs
Previous NPRR1214 approach (post RTC+B):
AS MCPC Price Adder = positive difference between SCED Pricing Run MCPC and SCED Dispatch Run MCPC.
This approach retains an approximation for AS MCPCs.
ERCOT's proposed approach:
Use SCED Pricing Run AS MCPCs as the final MCPCs when the Pricing Run is active; otherwise use SCED Dispatch Run AS MCPCs.
Keeps AS MCPCs aligned with energy prices (LMPs) — consistent treatment.
Eliminates the need for AS price adders.
AS will now receive indifference payments in a manner consistent with the proposed indifference payment for energy.
Result: Replaces the determination of binding AS MCPC in the prior version of NPRR1214 with a methodology that is consistent with the determination of binding energy prices

## Slide 6: Modifications to Reliability Deployment Indifference Payment (6.9.1)
1 | More accurate indifference payment calculation
Changes have been made to the indifference payment calculation to use actual offers/bids instead of approximations present in prior versions of NPRR1214.
2 | Introduces AS indifference payment
With the use of SCED Pricing Run AS MCPCs, Resources now also receive Ancillary Services indifference payments consistent with the energy indifference payment methodology.
3 | Missed consideration in prior version — RUC, RMR, MRA Resources
The previous NPRR1214 version missed consideration of the indifference payment to RUC, RMR, and MRA Resource real-time revenues (5.7.1.3, 5.7.1.4, 6.6.6.3, 6.6.6.10). These are now addressed.

## Slide 7: Summary of ERCOT Proposed Changes to NPRR1214
Area | Previous Approach | ERCOT Proposed Change
Energy Prices (LMPs) | Dispatch LMP + Energy Price Adder | Direct use of SCED Pricing Run LMPs
AS Prices (MCPCs) | Dispatch AS MCPC + AS MCPC Price Adder (positive difference) | Direct use of SCED Pricing Run AS MCPCs
Locational Modeling | No change (RUC,RMR, Offline NSPIN, DC Tie already locational) | Modify existing and add new categories: Modify Existing: NCLR,VECL Add New: Load & SOG
Indifference Payment | Energy only; with approximation | Energy+AS; accurate calculation; RUC/RMR/MRA revenue calculation updated to include Indifference Payments

## Slide 8: ERCOT Reliability Deployments
Out-of-market actions that distort market outcomes
Price Distortion
Affects LMPs (Locational Marginal Prices) and AS MCPCs (Ancillary Service Market Clearing Prices).
Award Distortion
Affects energy awards (Base Points to Resources) and Ancillary Services awards.
SCED Dispatch Run
Calculates MW awards and prices (LMP & AS MCPCs) based on actual real-time grid conditions.
SCED Pricing Run
Calculates MW awards and prices (LMP & AS MCPCs) using modified inputs — representing a grid state absent ERCOT-directed reliability deployments.

## Slide 9: Binding Awards & Prices
Key rules governing settlement
1 | Binding MW Awards — Always from SCED Dispatch Run
Energy awards (Base Points) and AS awards from the SCED dispatch run are always binding — the MW quantities used in settlement and required to be provided by Resources — regardless of whether ERCOT reliability deployments are in effect.
2 | Binding Prices — Conditional on Reliability Deployments
Reliability deployments in effect: Prices (LMPs & AS MCPCs) from the SCED Pricing Run are binding.
No reliability deployments: Prices (LMPs & AS MCPCs) from the SCED Dispatch Run are binding.

## Slide 10: The Inconsistency & Indifference Payment
Ideal
If Settlement uses both awards AND prices from the SCED pricing run — the closest estimate of market outcomes absent ERCOT-directed reliability deployments.
In Practice
Settlement $ = Awards from SCED dispatch run X Prices from SCED pricing run.
Using pricing run awards as binding would cause reliability problems.
This inconsistency — awards reflecting actual grid conditions while prices reflect a hypothetical state — can financially harm Resources and creates a perverse incentive for market participants to chase prices.
Solution — Indifference Payment: Designed to neutralize this perverse incentive by making participants financially indifferent to ERCOT-directed reliability deployments.

## Slide 11: Indifference Payment (energy): Approximation in Previous Version of NPRR 1214
PGRR145
NPRR1325
NPRR1325
MW
PR_BP
DR_BP
$/MWh
PR_LMP
HDL
DR_LMP
LDL
a
b
c
d
Assumed
EOC
LRDPA
Previous Version of NPRR 1214 assumes an EOC that is a straight line between points (DR_BP,DR_LMP) and (PR_BP,PR_LMP)
Indifference payment = Area between PR_LMP and assumed EOC
=½(Area abcd)
This can lead to under payment or over payment if the actual EOC has a different shape

## Slide 12: Indifference Payment (energy): Changes to Calculation for Improved Accuracy
PGRR145
NPRR1325
NPRR1325
MW
PR_BP
DR_BP
$/MWh
PR_LMP
HDL
LDL
Actual
EOC
Proposal uses the actual EOC
Proposed Indifference payment = Area between PR_LMP and actual EOC
The comparison of the indifference payment calculations

## Slide 13: Indifference Payment Calculation
Visualized as an area on a graph: x-axis = MW award, y-axis = SCED Pricing Run price
The indifference payment for a Resource for a given product (energy or AS) is the area bounded by:
1 | SCED Dispatch Run MW Award
Vertical line representing the Base Point or AS award from the dispatch run.
2 | SCED Pricing Run MW Award
Vertical line representing the Base Point or AS award from the pricing run.
3 | SCED Pricing Run Price
Horizontal line representing the LMP or AS MCPC from the pricing run.
4 | Offer / Bid Curve
EOC-GR (Energy Offer Curve), EBC-CLR (Energy Bid Curve), EBOC-ESR (Energy Bid/Offer Curve), or AS Offer segment.
The following slides describe the rationale behind each scenario and the corresponding indifference payment calculation.

## Slide 14: Indifference Payment Calculation (cont’d)
Energy Indifference Payment |  | 
Resource Type | PR_BP > DR_BP | PR_BP < DR_BP
GR | Lost Revenue – Avoided Production Cost | Increased Production Cost – Increased Revenue
CLR | Lost Consumer Benefit – Avoided Charge | Increased Charge – Increased Consumer Benefit
ESR; PR_BP > 0, DR_BP > 0 | Same as GR: Lost Revenue – Avoided Production Cost | Same as GR: Increased Production Cost – Increased Revenue
ESR; PR_BP < 0, DR_BP < 0 | Same as CLR (PR_BP < DR_BP) as ESR BP < 0 Increased Charge – Increase Consumer Benefit | Same as CLR (PR_BP > DR_BP) as ESR BP < 0 Lost Consumer Benefit – Avoided Charge
ESR; PR_BP > 0, DR_BP < 0 | Increased Charge – Increased Consumer Benefit + Lost Revenue – Avoided Production Cost | 
ESR; PR_BP < 0, DR_BP > 0 |  | Increased Production Cost – Increased Revenue + Lost Consumer Benefit – Avoided Charge
AS Indifference Payment follows the same logic as GR Energy Indifference Payment and is calculated for each AS Offer segment, for each AS type, including the proxy AS Offer

## Slide 15: Indifference Payment Calculation (cont’d) GR : PR_BP > DR_BP;
GR’s QSE has no trades or DAM awards for energy and AS, GR not “in the money” for any AS awards
Real-Time Energy Imbalance Payment:
RTEIAMT= PR_LMP*DR_BP= Area abcd
Proposed Indifference payment:
RDIGA= Lost Revenue – Avoided Production Cost
= Area befc – Area ghfc
=Area behg
PGRR145
PGRR145
PGRR145
NPRR1325
NPRR1325
MW
PR_BP
DR_BP
$/MWh
PR_LMP
a
b
c
d
f
h
g
EOC
HDL
e

## Slide 16: Indifference Payment Calculation (cont’d) GR : PR_BP < DR_BP
PGRR145
PGRR145
PGRR145
NPRR1325
NPRR1325
MW
DR_BP
PR_BP
$/MWh
PR_LMP
a
b
c
d
f
g
EOC
GR’s QSE has no trades or DAM awards for energy and AS, GR not “in the money” for any AS awards
Real-Time Energy Imbalance Payment RTEIAMT = PR_LMP*DR_BP= Area abcd
Proposed Indifference payment:
RDIGA = Increased Production Cost – Increased Revenue
= Area efcg – Area ebcg
=Area efb
HDL
e

## Slide 17: Indifference Payment Calculation (cont’d) CLR: PR_BP > DR_BP
CLR’s QSE has no trades or DAM awards for energy and AS, CLR not “in the money” for any AS awards
Real-Time Energy Imbalance Charge:
RTEIAMT= PR_LMP*DR_BP= Area abcd
Proposed Indifference payment:
RDILA= Lost Consumer Benefit – Avoided Charge
= Area efgc – Area bhgc
=Area efhb
PGRR145
PGRR145
PGRR145
NPRR1325
NPRR1325
MW
PR_BP
DR_BP
$/MWh
PR_LMP
a
b
c
d
e
f
h
g
EBC
HDL

## Slide 18: Indifference Payment Calculation (cont’d) CLR: PR_BP < DR_BP
CLR’s QSE has no trades or DAM awards for energy and AS, CLR not “in the money” for any AS awards
Real-Time Energy Imbalance Charge:
RTEIAMT= PR_LMP*DR_BP= Area abcd
Proposed Indifference payment:
RDILA= Increased Charge – Increased Consumer Benefit
= Area ebcf – Area egcf
=Area ebg
PGRR145
PGRR145
PGRR145
NPRR1325
NPRR1325
MW
DR_BP
PR_BP
$/MWh
PR_LMP
a
b
f
d
e
g
c
EBC
HDL

## Slide 19: Indifference Payment Calculation (cont’d) ESR : PR_BP > DR_BP; with DR_BP < 0 & PR_BP>0
ESR’s QSE has no trades or DAM awards for energy and AS, ESR not “in the money” for any AS awards
Real-Time Energy Imbalance Charge:
RTEIAMT= PR_LMP*DR_BP= Area abcd
Proposed Indifference payment:
RDIEA= Increased Charge – Increased Consumer Benefit + Lost Revenue – Avoided Production Cost
= Area abcd – Area ecf + Area fgd + Area bhjc – Area eijc
=Area ahig
PGRR145
NPRR1325
MW
PR_BP
DR_BP
$/MWh
PR_LMP
a
b
c
d
f
h
g
EBOC
HDL
e
j
i

## Slide 20: Indifference Payment Calculation (cont’d) ESR : PR_BP < DR_BP; with DR_BP > 0 & PR_BP < 0
ESR’s QSE has no trades or DAM awards for energy and AS, ESR not “in the money” for any AS awards
Real-Time Energy Imbalance Payment (Charge):
RTEIAMT= PR_LMP*DR_BP=Area abcd
Proposed Indifference payment:
RDIEA= Increased Production Cost – Increased Revenue + Lost Consumer Benefit – Avoided Charge
= Area efba + Area abcd + Area eag - Area ghi + Area iadh
=Area hfc
PGRR145
NPRR1325
MW
DR_BP
PR_BP
$/MWh
PR_LMP
a
b
c
d
f
h
g
EBOC
HDL
e
i