## Slide 1
PDCWG Report to ROS
Chair: Open
Vice Chair: Open (ERCOT Interim)
ROS
June 4th, 2026

## Slide 2: Report Overview & Notes
Report Overview
  Meeting Minutes
    PDCWG Leadership Nomination Discussion
      Chair: Paul Messman
      Company: Tenaska
      Email: PMessmann@tnsk.com
    FME Selection Analysis
    Frequency Control & Regulation Reports
    Texas RE Report
    Analysis of Disturbances
  FME Selection Analysis
  Frequency Control Report

## Slide 3: Frequency Measurable Events SELECTION ANALYSIS

## Slide 4: FME Selection Analysis
Due to the evolving grid, ERCOT has observed the current criteria used is resulting in fewer FMEs than the desired 20 to 35 events per year. With too few events to evaluate, the Primary Frequency Response (PFR) performance monitoring per BAL-001-TRE standard and oversight of Responsive Reserve Service providers has nearly stalled.
To address this, ERCOT has proposed revised criteria to the PDCWG, this revised criteria is expected to increase the FME count and improve the performance monitoring.
ERCOT will continue to use additional quality checks and retains discretion when selecting FMEs.
ERCOT has shared the analysis supporting the revised criteria to the PDCWG. ERCOT is in the process of updating internal process and began using the revised criteria going forwards immediately.

## Slide 5: Frequency Control Report
April 2026

## Slide 6: CPS1 Performance
Current 12-Month Rolling Average: 180.17%
Notes: 12 month rolling average CPS1 score is 180.17 which is continuing the increasing trend of CPS1 scores.

## Slide 7: RMS1 Performance of ERCOT Frequency
Notes: A More granular look at last 15 years of RMS1 by month
11.46 mHz on avg for April 2026

## Slide 8: Frequency Profile Analysis
Notes: Comparison of frequency profile between April 2025 and April 2026. Compared to last year, there are slightly less instances of frequency hovering around the lower dead bands.

## Slide 9: Time Error Corrections
Notes: No time error corrections in the month of April.

## Slide 10: ERCOT Total Energy
Notes: 37,902,160 MWh

## Slide 11: ERCOT Total Energy from Wind Generation
Notes:   11,360,493 MWH

## Slide 12: ERCOT % Energy from Wind Generation
Notes: 29.97% of total energy was provided by wind generation

## Slide 13: ERCOT Total Energy from Solar Generation
Notes: 5,732,515 MWh

## Slide 14: ERCOT % Energy from Solar Generation
Notes: 15.12% of total energy was provided by solar generation

## Slide 15: ERCOT Daily Minimum System Inertia
Notes: Minimum Inertia in April 2026 = 132,705 MW*s on April 19th
Historical Overall Minimum was 109,029 MW*s on 3/22/2021
March Data:
Mean: 189,921 MW*s
Max: 246,411 MW*s on April 28th
Min: 132,705 MW*s on April 19th

## Slide 16: Total Inertia 2016-2026
Date and Time | 2016 4/10 2:00 AM | 2017 10/27 4:00 AM | 2018 11/03 3:30 AM | 2019 3/27 1:00 AM | 2020 05/01 2:00 AM | 2021 03/22 1:00 AM | 2022 03/21 2:00 AM | 2023 04/18 3:00 AM | 2024 03/29 4:00 AM | 2025 03/18 12:00 PM | 2026* 03/14 12:00 PM
Min synch. Inertia (GW*s) | 143 | 130 | 128.8 | 134.5 | 131.1 | 116.6 | 115.0 | 124.3 | 129.9 | 118.3 | 114.7
System load at minimum synch. Inertia (MW) | 27,831 | 28,425 | 28,397 | 29,883 | 30,679 | 31,767 | 33,784 | 35,578 | 37,039 | 49,130 | 48,013
Non-synch. Gen. in % of System Load | 47 | 54 | 53 | 50 | 57 | 66 | 65 | 61 | 68 | 74 | 81
FFR Award | N/A | N/A | N/A | N/A | 0 | 0 | 0 | 0 | 134 | 298 | 430
Critical Inertia (GW*s) | 100 | 100 | 100 | 100 | 100 | 100 | 100 | 100 | 93 | 92 | 87
Red circles denote inertia at max IRR penetration (= IRR Gen/Total Gen)
Notes: Summary of ERCOT inertia for the previous 10 years. Lowest inertia this year was on March 14th.
For each box, the central mark (red line) is the median, the edges of the box (in blue) are the 25th and 75th percentiles, the whiskers correspond to +/- 2.7 sigma (i.e., represent 99.3% coverage, assuming the data are normally distributed. The corresponding lowest inertia in each year is given in the table.
The circle on each boxplot is showing inertia during time when highest portion of load was served by wind/solar generation in that year.

## Slide 17
Questions?