## Slide 1: Monthly Review of Reliability Unit Commitment Market Impacts – June 2026 Wholesale Market Working Group ERCOT Market Analysis July 2026

## Slide 2: RUC Resource-Hours
June 2026 | Total | Capacity |  | Congestion | 
 |  | Opt-Out | Non-Opt-Out | Opt-Out | Non-Opt-Out
Instructed Resource-Hours |  |  |  |  | 
Total Count | 456.0 | 5.0 | 296.0 | 0.0 | 155.0
Effective Resource-Hours* |  |  |  |  | 
Total Count | 436.0 | 5.0 | 285.4 | 0.0 | 145.6
Average Megawatts (MW) for Effective Resource-Hours |  |  |  |  | 
Average LSL | 57.8 | 120.0 | 60.6 | - | 50.4
Average LDL | 62.3 | 271.1 | 64.5 | - | 51.0
Average BP | 64.4 | 335.4 | 65.8 | - | 52.7
Average HSL | 244.6 | 435.0 | 271.4 | - | 186.6
* The difference between “Instructed” and “Effective” values is a result of Resources starting up, shutting down, receiving partial hour instructions, or otherwise not being dispatchable by SCED.

## Slide 3: RUC Instruction Reasons: Last 13 Months
RUC activity increased slightly in June compared to May.
67% of RUC effective Resource-hours in June 2026 were nominally attributed to address capacity needs.

## Slide 4: RUC Instruction Reasons in June 2026
There were 436.0 RUC total effective Resource-hours in June and 290.4 hours (67%) were committed to address capacity needs.
The highest effective Resource-hours in June occurred on June 19th to support capacity needs, which was associated with the higher projected load forecast and uncertainty around wind availability in the evening hours.

## Slide 5: Non-opt-out and Opt-out Totals: Last 13 Months
June 2026 had a total of 431.0 non-opt-out effective Resource-hours (99%) and 5.0 opt-out effective Resource-hours (1%).

## Slide 6: Non-opt-out and Opt-out Totals: June 2026
All opt-out effective Resource-hours in June were on June 16th.

## Slide 7: RUC Lead Time Margin: June 2026
Most RUC commitment windows (69%) had a lead time margin of 2 hours or less.
“Lead time” refers to the length of time between a RUC instruction and the start of the commitment window.
“Lead time margin” is the difference between lead time and the Resource’s startup time.
  In cases where a Resource is committed for multiple back-to-back time blocks, lead time margin is calculated from the first instruction.

## Slide 8: Average Resource Age: Last 13 Months
In June 2026, the average age of RUC-committed Resources was 56.4 years for non-opt-out Resource-hours.
Note: For Resource configurations with multiple physical generators, the age of the oldest generator is used.

## Slide 9: Age Category: Last 13 Months
In June 2026, 88% of RUC effective Resource-hours were provided by Resources that were at least 50 years old.
Note: For Resource configurations with multiple physical generators, the age of the oldest generator is used.
Non-Opt-Out
Opt-Out

## Slide 10: RUC-Instructed Resource Dispatch above Low Dispatch Limit (LDL) in Non-Opt-Out Hours
Out of 431.0 non-opt-out effective Resource-hours, RUC-instructed Resources were dispatched above their LDL for 15.2 resource-hours.
  In no Resource-hours did the Locational Marginal Price (LMP) for the RUC-instructed Resource exceeded the RUC offer floor.
  In 15.2 of these Resource-hours, the LMP for the RUC-instructed Resource fell below the RUC offer floor.​ All 15.2 Resource-hours saw the RUC-instructed Resource being mitigated.
There were Exceptional Fuel Cost submissions for a single RUC-Committed Resource in June 2026.

## Slide 11: Reliability Deployment Price Adder for Energy: Last 13 Months
June 2026 had a total of 133.9 RTRDPA hours with a time-weighted average value of $1.18/MWh.
These graphs show RTRDPA instances by reliability action: 'RUC Only' for instances triggered solely by Reliability Unit Commitment, 'RUC and other triggers' for instances with RUC and additional triggers, and 'Other triggers only' for instances with non-RUC triggers. The daily average RTRDPA is calculated using the total duration across all categories. See ERCOT protocol section 6.5.7.3.1 for details.

## Slide 12: Reliability Deployment Price Adder for Energy: June 2026
These graphs show RTRDPA instances by reliability action: 'RUC Only' for instances triggered solely by Reliability Unit Commitment, 'RUC and other triggers' for instances with RUC and additional triggers, and 'Other triggers only' for instances with non-RUC triggers. The daily average RTRDPA is calculated using the total duration across all categories. See ERCOT protocol section 6.5.7.3.1 for details.
June 6th had the highest daily time-weighted average RTRDPA of $8.73/MWh.

## Slide 13: Reliability Deployment Price Adders for Ancillary Services: Last 7 Months
The average values are calculated as time-weighted average Real-Time Reliability Deployment Price Adders for each Ancillary Service during SCED intervals with RDPA active for any reliability event trigger. RDPAs for Ancillary Services are only available after RTC+B implementation on December 5, 2025
In June 2026, average Ancillary Service price adders increased from May with the exception of Regulation Down.

## Slide 14: Reliability Deployment Price Adder for Ancillary Services: June 2026
The daily average values are calculated as time-weighted average Real-Time Reliability Deployment Price Adders (RDPA) for each Ancillary Service during SCED intervals with RDPA active for any reliability event trigger.
For details on the triggers for reliability price adders, please refer to the previous slide titled “Reliability Deployment Price Adder for Energy: June 2026”
RDPA | Monthly Time Weighted Average ($/MWh)*
Regulation Up (Reg-Up) | 0.19
Regulation Down (Reg-Down) | 0.01
Responsive Reserve Service (RRS) | 0.16
ERCOT Contingency Reserve Service (ECRS) | 0.29
Non-Spinning Reserves (Non-Spin) | 0.49
June 2026’s elevated monthly average RDPAs were driven by a daily spike on June 6th.

## Slide 15: RUC Clawback, Make-Whole, and Shortfall
Of the $1,301,171 in Make-Whole payments made in June 2026, $6.14 was uplifted to load due to rounding. The remaining amount was collected through Capacity-Short charges.
For June 2026, the total Clawback charge was $138,880. The total Make-Whole payment was $1,301,171.

## Slide 16: RUC Clawback by Settlement Type
Month | Initial Settlement ($) | Final Settlement Change ($) | True-up Settlement Change ($) | Net ($)
Jun ‘25 | 173,176 | 0 | 0 | 173,176
Jul ‘25 | 246,479 | 0 | -18,991 | 227,488
Aug ‘25 | 12,319 | 0 | -2,121 | 10,198
Sep ‘25 | 122,634 | 0 | 0 | 122,634
Oct ‘25 | 128,343 | 0 | -68,059 | 60,284
Nov ‘25 | 80,805 | 0 | -14,883 | 65,922
Dec ‘25 | 233,500 | 0 | -14,862 | 218,638
Jan ‘26 | 1,130,396 | - | - | -
Feb ‘26 | 0 | - | - | -
Mar ‘26 | 856,743 | - | - | -
Apr ‘26 | 242,784 | - | - | -
May ‘26 | 77,429 | - | - | -
Jun ‘26 | 138,880 | - | - | -
Negative dollars represent a payment from ERCOT to a market participant
“-” indicates settlement has yet to be completed.
Net figures may differ slightly due to rounding.

## Slide 17: RUC Make-Whole by Settlement Type
Month | Initial Settlement ($) | Final Settlement Change ($) | True-up Settlement Change ($) | Net ($)
Jun ‘25 | -1,285,661 | 0 | -522,765 | -1,808,427
Jul ‘25 | -382,887 | 0 | -95,893 | -478,780
Aug ‘25 | -487,773 | 0 | -110,640 | -598,413
Sep ‘25 | -2,035,251 | 0 | -538,306 | -2,573,557
Oct ‘25 | -1,016,193 | 0 | -596,880 | -1,613,073
Nov ‘25 | -1,151,712 | 0 | -1,739,486 | -2,891,198
Dec ‘25 | -271,995 | 0 | -696,055 | -968,051
Jan ‘26 | -431,896 | - | - | -
Feb ‘26 | 0 | - | - | -
Mar ‘26 | -324,968 | - | - | -
Apr ‘26 | -76,725 | - | - | -
May ‘26 | -1,140,481 | - | - | -
Jun ‘26 | -1,301,171 | - | - | -
Negative dollars represent a payment from ERCOT to a market participant
“-” indicates settlement has yet to be completed.
Net figures may differ slightly due to rounding.

## Slide 18: Questions/Comments