## Slide 1: Analysis of Cost Allocation of Ancillary and Reliability Services in the ERCOT Region Responsive to PURA § 39.1593 | PUCT Project No. 58555 ERCOT Staff Technical Advisory Committee July 29, 2026
Discussion Outline
Background and study scope
Allocation methods and cost drivers
Preliminary primary-effect results
Secondary-effects analysis
Summary and next steps

## Slide 2: Introduction
Purpose of Today’s TAC Discussion
Discuss ERCOT’s preliminary findings and receive any further feedback so ERCOT can complete and deliver the final report to the PUCT by end of August.
2
Key Findings
At equilibrium, none of the three methods analyzed is expected to directly lower consumer costs versus today. Any savings would be indirect — by shifting AS/RS costs onto the resources that drive the need, these methods create an incentive to reduce it, though whether that incentive is large enough to change behavior is uncertain. Methods A and B offer only limited incentive; Method C mainly shifts who bears the cost and nudges resource availability during scarcity, without reducing overall AS/RS need.
Legislative Requirement
Public Utility Regulatory Act (PURA) § 39.1593 requires PUC to evaluate whether alternative Ancillary Service (AS) and Reliability Service (RS) cost allocation methods produce net savings to consumers compared with the current method of allocating costs to load and to report to the Legislature by Dec. 1, 2026.
Study Scope
Public Utility Commission of Texas (PUCT) outlined the alternative methods, historical data period, and analytical areas ERCOT should evaluate in the study scope filed in PUCT Project 58555.
ERCOT Deliverable
ERCOT is required to conduct analysis outlined in the study scope with input from TAC and submit its findings report to the PUCT by the end of August 2026.
May 19, 2026 TAC Meeting Recap
ERCOT presented the study approach and preliminary primary-effect results at the May 19, 2026 TAC.
Stakeholders and the IMM provided questions/feedback on the allocation logic and secondary-effects analysis.
ERCOT’s responses to the questions/feedback are posted to today’s TAC meeting page.

## Slide 3: Nomenclature for Today’s Discussion
Base Case: Current Load Ratio Share (LRS) allocation
Benchmark. AS/RS costs allocated primarily to QSEs representing load.
Method A: Highest reliability-risk hours1
Based on forecast errors during high reliability-risk hours2; allocation reflects hourly operational risk drivers; semi-annual allocation across generation (dispatchable, non-dispatchable) and load.
Method B: Operational-risk allocation
Based on forecast errors during all hours; allocation reflects hourly operational risk drivers; daily allocation.
Method C: QSE capacity-short allocation
Based on capacity-short positions; costs allocated first to capacity-short QSEs, with any residual uplift allocated by LRS; daily allocation.
Primary effects
Reallocate historical AS/RS costs using each method and compare to the Base Case.
Secondary effects
Assess how participant behavior, credit, settlement, and consumer-cost impacts could change.
Products in scope
AS: Regulation, Responsive Reserve Service (RRS), ERCOT Contingency Reserve Service (ECRS), Non-Spinning Reserve Service (Non-Spin) RS: Black Start Service (BSS), Emergency Response Service (ERS), Firm Fuel Supply Service (FFSS), Reliability Must Run (RMR), Reliability Unit Commitment (RUC), Voltage Support Service (VSS)
Note: Dispatchable Reliability Reserve Service (DRRS) excluded because it is currently under development and historical pricing and quantity data does not exist.
Historical Basis and Expected Outputs
Use 2024-2025 historical data for AS and RS; estimate allocation by method and service; assess consumer net savings and other implementation impacts under each alternative.
3
1. As defined by PURA § 39.1593(b)(1)
2. Seasonal morning (HE 5–7) and evening (HE 16–21, by season) ramp hours, plus any low-PRC hours. There were no hours in 2024 or 2025 that met the low PRC definition as outlined in study scope.

## Slide 4: Method A and B Allocation — Ancillary Services
Methods A and B allocate costs based on the operational risk the service is procured to address but apply it to different sets of hours.
Service | Purpose/Cause | Requirement Basis | Allocation
Regulation | SCED dispatches dispatchable resources to forecasted net load (load minus wind minus solar). Regulation offsets the ongoing mismatch between metered and dispatched net load. That mismatch is driven by movement in load, wind, and solar. | Error in the net load forecast SCED used, i.e., 5-minute-ahead load, wind and solar forecast errors | Load, Non-Dispatchable
RRS | Arrest frequency when a unit trips without triggering under-frequency load shed (UFLS). The credible single-resource loss large enough to move system frequency is a dispatchable/synchronous generator; loss of a single wind-turbine or solar-inverter is too small to affect frequency comparably. RRS is held to cover that contingency. | Arrest the loss of the two largest single-resource contingencies without triggering UFLS. Inertia determines how much RRS is needed to avoid triggering UFLS. | Dispatchable (Sharper allocation: Synchronous dispatchable resource)
ECRS | A fast reserve that covers net-load movement within the operating hour that the hourly commitment did not anticipate, bridging until Non-Spin and other resources respond. | 30-minute-ahead load, wind and solar forecast errors | Load, Non-Dispatchable
Non-Spin | A reserve that is used to cover multi-hour capacity shortfalls the hourly commitment did not anticipate — caused by net load forecast error and resource forced outages — until additional resources are committed. | 6-hour-ahead load, wind and solar forecast errors and 6-hour-cumulative forced outage risk | Dispatchable, Non-Dispatchable, Load

## Slide 5: Method A and B Allocation — Reliability Services
Reliability Services (RS) address system-wide or fuel-related reliability needs; under Methods A and B they are allocated 100% to load — except FFSS, whose need arises from natural-gas supply risk.
Service | Purpose | Allocation
BSS | Provides the capability to restart the grid without support of the ERCOT Transmission Grid | Load
ERS | Contracted load and generation deployed to help prevent or alleviate an actual or anticipated Energy Emergency Alert (EEA) event | Load
RMR | Generation Resource needed to provide voltage support, stability, or management of localized transmission constraints that would otherwise retire | Load
RUC | A process to ensure adequate capacity is committed in the proper locations to serve ERCOT forecasted Load and procure required reserves | Load
VSS | Required to maintain transmission and distribution voltages on the ERCOT Transmission Grid within acceptable limits | Load
FFSS | Firm or on-site fuel to ride through gas-supply disruption in extreme cold | Load * Non-FFSS-qualified gas units
5
*Consistent with the scope's guidance to assign each reliability service in line with its purpose, ERCOT refined the allocation of FFSS. LEI is in the process of incorporating this change in its analysis.

## Slide 6: Method A and B – Preliminary Allocation
The information below summarizes preliminary 2024–2025 results by category — Method A using the high reliability-risk hours (defined on slide 3), and Method B using all hours.
6
Key Takeaway: In comparison to today where all AS+RS cost is allocated to load (Base Case), both methods shift cost onto generation; Method A places more on non-dispatchable than Method B.

## Slide 7: Method C – QSE Capacity Short Approach
Method C allocates AS and RS costs based on QSE capacity short positions using the RUC capacity short Adjustment Period equations that were in effect prior to the implementation of RTC (Protocols § 5.7.4.1.1). Refer to Slide 17 in the Appendix for the Settlement Equations.
How Method C Works
1
Capacity Shortfall Calculation
Each QSE’s capacity shortfall (RUCSF) is computed per 15-minute Settlement Interval using real-time metered load, COP capacity, trades, and DC Tie imports.
2
Capacity-Short Charge (RUCCSAMT)
AS/RS costs are charged to QSEs proportional to their share of total capacity shortfall for each interval, subject to a cap.
3
LRS Uplift (LARUCAMT)
If capacity-short charges are insufficient to cover total cost, the shortfall is uplifted to all QSEs by Load Ratio Share.
QSE Classification Categories
Category Description
Generation-Only QSE represents only generation
Load-Only QSE represents only load
Load-and-Generation QSE represents both generation and load
Power Trader QSE does not represent generation or load
Equation Modifications
Replace the RUC Make-Whole Amount (RUCMWAMTTOT) with the appropriate AS or RS cost
Replace RUC Capacity Total (RUCCAPTOT) with the corresponding MW quantity
For IRRs, the HSL was used in place of High Ancillary Service Limit at Adjustment Period (HASLADJ)
RUC costs are drawn directly from ERCOT systems, as they are allocated on a capacity-short basis
7

## Slide 8: Method C – Preliminary Allocation
The information below summarizes preliminary 2024–2025 results under capacity short framework by QSE category for AS and RS.
8
Key Takeaway: In comparison to today, where all AS+RS costs excluding RUC costs are allocated based on LRS to Load (Load-Only and Load-and-Generation QSEs), Method C shifts a substantial share of costs from Load to Power Traders and Generation, although this doesn’t account for possible additional Capacity Trades to cover capacity-short positions.

## Slide 9: Estimating Secondary Effects — Outlined in Study Scope
Reallocating AS/RS costs to generators or QSEs does not, by itself, determine the impact on consumers. The study scope set out three questions to assess this impact. ERCOT partnered with London Economics International (LEI) to help answer them1. The following slides share the preliminary directional and qualitative findings on each.
Market-participant behavior
Evaluate whether new AS/RS cost exposure could change operational, trading, maintenance, or investment decisions, and how those responses could affect reliability and costs.
Bottom line: Would new AS/RS cost exposure change operating, trading, maintenance, or investment decisions — and in turn affect reliability or cost?
1
Consumer net savings
Assess whether each method could produce consumer net savings; focus primarily on wholesale market activities.
Bottom line: Would any alternative method lower the total cost borne by consumers?
2
Settlement & Credit
Assess Method A semi-annual settlement impacts, including advance charges for expected obligations, delayed true-ups, and potential barriers for smaller entities.
Bottom line: What are the settlement, credit, and cash-flow implications — particularly Method A’s semi-annual timing (advance charges, true-ups, and effects on smaller entities)?
3
9
1. LEI performed modeling to help ERCOT to answer Question 1 only. They were not asked to perform modeling to answer either of Questions 2 or 3.

## Slide 10: Secondary Effects Analysis Methodology - Methods A & B
Calculate resource-level AS cost allocation from January 1, 2024, to December 4, 2025
Utilize ERCOT’s calculated interval-level AS costs for each type of AS product, hourly cost allocation ratios by resource category for Method A and Method B
Obtain HSL of each resource in each SCED interval from ERCOT’s 60-day SCED report
Obtain nameplate capacity of each resource from ERCOT’s Capacity, Demand, and Reserves (CDR) and Monthly Outlook for Resource Adequacy (MORA) reports
Calculate each resource’s AS cost allocation in each SCED interval based
Normalize results to a $ of AS cost per MW of nameplate capacity ($/MW-year) metric, grouped into dispatchable and non-dispatchable
Analyze long-term equilibrium impact
Evaluate impact on CONE due to higher fixed costs from AS cost allocation
Estimate number of hours where dispatchable are setting marginal prices in 2024 and 2025
Calculate energy price increase required for new entry to compensate for increase in fixed costs
Calculate net consuming impact

## Slide 11: Secondary Effects Findings - Methods A & B
Methods A and B differ only in which hours are counted — Method A uses the high-risk ramp hours, which are a subset of Method B's all-hours. Restricting to those hours changes each category's cost share only slightly, so at the category level the cost per MW of capability comes out similar under both methods. The difference shows up within the non-dispatchable category: Method A's early-morning and evening ramp hours carry less solar output as compared to Method B, so wind bears a larger share of the non-dispatchable cost for Method A relative to Method B.
*The "no short-term change" finding holds under HSL-based allocation. An output/MWh-based allocation would make the charge a variable cost and could change offers — reversing this result. Long-term effects are directional inferences from the fixed-cost analysis and economic reasoning. The comparison to cost first allocated is based on a simplified illustrative calculation.
SHORT TERM — NO BEHAVIOR CHANGE
The allocated cost behaves as a fixed cost. The cost assigned to a generator would not change with how much energy the generator produces. It is based on the generator's High Sustained Limit (HSL) — its capability — not on the power (MW) or energy (MWH) it generates.
A generator would not be able to reduce the cost by changing its operational behavior. Because the charge does not depend on output, a resource cannot lower it by adjusting its output or its offers, and it cannot understate its HSL to avoid it.
So, no short-term change to energy offers or SCED output is expected.*
One exception — PUNs, which could lower HSL by serving load internally. With limited qualifying capacity currently, the effect is expected to be small, though it could grow as that capacity increases.
LONG TERM — PROFITABILITY & INVESTMENT Impact
The cost may reduce generator profitability over time. Because it is a fixed cost that cannot be avoided by changing operations, it is expected to reduce profitability rather than changing day-to-day dispatch and operational practices.
Lower profitability could, over time, affect investment and retirement decisions. Resources could retire somewhat earlier, and new resources could be built later, than they otherwise would under the status quo.
These long-term changes could pass some of the cost back to consumers. As supply and demand tighten, energy prices could rise over time. It is possible that this long-term increase in consumer energy costs could be larger than the amount of ancillary service cost first allocated to generators.
Key Takeaway: Methods A and B act as a fixed cost: no meaningful short-term behavior change; long-term profitability and investment effects are possible, tending toward higher consumer costs.

## Slide 12: Secondary Effects Analysis Methodology - Methods C
QSE-to-QSE capacity trading is a zero-sum game where one QSE’s reduction in capacity shortfall exposure would lead to an increase in AS+RS allocation costs borne by another (capacity short) QSEs
QSEs who are capacity short (before QSE-to-QSE capacity trading) are incentivized to offset as much capacity shortfall as possible through capacity trading (i.e. buying capacity from QSEs that have long capacity)
Analyzing secondary effect of Method C involves simulating trading outcome QSE-to-QSE capacity trading in each settlement interval using actual data in 2024 and 2025
In a liquid market with no transaction costs, QSEs with net short capacity should be willing to pay a price for capacity up to its potential AS+RS cost allocation exposure assuming all other QSEs will also buy capacity to cover their net short positions
Excess supply condition, equilibrium price is $0/MW
Any long capacity remaining has no value, prices race to the bottom
1
Scarcity condition, equilibrium price is maximum willingness-to-pay
Supply is fixed; prices clear at the maximum willingness-to-pay
2
Equilibrium price simulated using simplified game theory model
Prices are lower when there are more jointly-pivotal QSEs with long capacity
3
Net long capacity > net short capacity, no pivotal player
Net long capacity < net short capacity
Net long capacity > net short capacity, with pivotal player(s)
Maximum willingness-to-pay = min[((Market-wide AS+RS Cost for Allocation) / (Capacity demand – capacity supply)), AS+RS cost allocation cap]
where the AS+RS cost allocation cap is:
AS+RS cost allocation cap = 2 x [(Market-wide AS+RS Cost for Allocation) / (MW of AS + RS procured)]
The equilibrium price in each settlement interval depends on the demand-supply balance:
Note that the payments between QSEs for QSE-to-QSE capacity trades are not visible to ERCOT, as they are settled outside of existing ERCOT administered markets. However, the positions after the trades will be submitted to ERCOT’s systems for settlement purpose.

## Slide 13: Secondary Effects Findings - Method C
Unlike Methods A and B, Method C assigns cost at the QSE level, based on each QSE’s capacity-short position in a 15-minute interval. This gives QSEs an incentive to trade capacity and reduce their exposure. In 2024–2025, the system was short in only ~0.3% of intervals, so after modeled trading, about 96% of cost is allocated to load.
Assumption: QSEs can trade capacity bilaterally to manage exposure (no transaction costs and full information available).
*These are expected directions, not observed outcomes; historical trading was limited, so actual behavior could differ.
HOW IT WORKS
Cost falls on capacity-short QSEs — using Capacity Trades, capacity-short QSEs can buy capacity from capacity-long QSEs to reduce this cost, an incentive Methods A and B do not create.
Trading is zero-sum — when one short QSE covers its shortfall, the remaining short QSEs pay more.
An allocation cap is recommended — without it, the last QSE left short could bear the entire interval’s AS+RS cost. Consequently, this allocation approach could be deemed risky by market participants, negatively impacting appetite for participating or investing in the ERCOT market.
WHO IT MOVES AND LONG-TERM IMPACTS*
Money moves between QSEs — After trading, QSEs with load continue to bear most AS/RS cost. Once trading outcomes are accounted, Generation-Only QSEs emerge as net receivers while QSEs with load incur additional cost to secure those trades.
Uncertainty of financial impact — the financial impact of the exposure depends both on how often the system is short and how large those QSE’s shortfalls are during those intervals.
Dispatchable is the more effective offset— shortage intervals tend to coincide with low non-dispatchable generation output, so for QSEs that are seeking to reduce their exposure to this cost, contracting with dispatchable generation capacity (that can sustain output through the shortage) could be the more effective way to do so.
Key Takeaway: Method C's cost-shifting effect depends on how often intervals are capacity-short: when that number is low, as it is today, most AS+RS cost stays with load.

## Slide 14: Secondary Effects Findings – Consumer Net Savings
Methods A & B Findings
The allocated costs act as fixed costs, so there is no short-term behavior change or net savings anticipated.
In the long-term, increased costs may result in higher consumer energy costs due to portfolio management decisions (earlier retirements, delayed entry). This is also unlikely to result in net consumer savings, more likely the opposite.
Limited incentives to make improvements that reduce the need for AS. Because cost is allocated by HSL-share within each category, a resource that lowers risk captures only part of the benefit – it is shared across the allocation category.
Method C Findings
The allocated costs remain on load-share except in scarcity intervals, where a portion shifts to capacity-short QSEs. The incremental cost burden will depend on each QSE’s aptitude at hedging against short positions during periods of scarcity.
In 2024–2025 the system was short only ~0.3% of intervals, so in retrospect the cost burden rarely left load-share — the overall outcome stayed close to the status quo, and no net savings are anticipated for this method.
Incentive exists, but mostly to hedge against short positions — Method C rewards covering a short position (trading, contracting dispatchable), which changes who bears the cost and not the total AS need.
The AS/RS cost allocation methods studied would reapportion the cost burden of AS/RS to different Market Participants — this reallocation by itself produces no consumer net savings. Savings would require reducing the overall cost of the services or introducing efficiency gains, which generally would only occur if the need for AS/RS decreases. The portion of the cost which remains on load-share would reach consumers as it does today; the portion of the costs shifted elsewhere would reach consumers indirectly over the long-run.
Key Takeaway: At equilibrium, none of the three methods studied are expected to directly produce consumer net savings compared to the status quo. Any savings would be indirect: unlike today’s allocation, these methods place cost on the resources that drive AS need, creating a potential incentive to reduce that need – but whether that incentive is strong enough to change behavior is uncertain and unquantified. Methods A and B create limited incentives to do so; Method C incentivizes hedging that shifts who pays and provides a small incremental incentive to have resources available during times of scarce capacity but does not reduce the total need for AS/RS.

## Slide 15: Secondary Effects – Settlement and Credit Impacts for Method A
Settlement impacts
Average daily uplift for AS/RS in 2024-2025 is approximately $1.4M; moving to semi-annual settlement would have increased the uplift to approximately $254M on a single invoice. This could increase the risk of a QSE default.
Process considerations under semi-annual settlement:
  Initial settlement charges would rely on historical generation/load data during high-risk hours. Changes in ownership, behavior, or system conditions could cause the initial estimate to diverge materially from a QSE’s actual generation/load data.
  Initial AS charges would be based on historical AS prices, which may not reflect actual prices for the period.
  Payments for daily AS awards would either need to be made at the end of the 6-month period during the true up, or a fund would need to be created and managed to disburse funds throughout the period.
  For RS, any additional payments or clawbacks tied to performance would be addressed during the true up settlement once actual data becomes available.
A new invoice structure would likely be required to support semi-annual settlement.
Credit impacts
Requiring advance semi-annual settlement rather than daily settlement significantly increases the collateral and liquidity burden on market participants, as they must pre-fund large sums upfront. This can elevate credit risk exposure relative to the current model where payments track actual daily usage.
Initial collateral for new entrants to the market would have to be increased arbitrarily to account for potential future AS and RS charges given that historical initial estimate data will not be available.
Key Takeaway: Shifting AS/RS cost allocation for Method A from a daily to a semi-annual cadence would introduce substantial changes and associated implementation costs to the Settlement System, elevate the risk of QSE default, and impact collateral requirements.

## Slide 16: Summary and Next Steps
Summary
  Preliminary finding: At equilibrium, none of the three methods analyzed is expected to directly lower consumer costs versus today. Any savings would be indirect — by shifting AS/RS costs onto the resources that drive the need, these methods create an incentive to reduce it, though whether that incentive is large enough to change behavior is uncertain.
  ERCOT evaluated the Base Case and three alternative AS/RS cost allocation methods (A, B, and C) identified in the PUCT study scope. Today ERCOT shared preliminary primary-effect results and preliminary secondary-effect findings across all scope areas — market-participant behavior, consumer net savings, and settlement & credit.
  ERCOT appreciates TAC’s engagement and feedback, which will help ERCOT in finalizing the report for this effort.
Next steps
  Incorporate July TAC input and finalize ERCOT's report to the PUCT by the end of August 2026.
Project Schedule Recap (from Study Scope)
Jan. 15, 2026
Project scope approved by PUCT at Open Meeting.
Jan. – Aug. 2026
ERCOT analysis and report drafting phase. ERCOT's final report scheduled for end of August 2026.
Sept. – Nov. 2026
PUCT Staff-led workshop and request for public comment on ERCOT's final report in September, followed by proposed findings and recommendations filed in October, and PUCT consideration in October and November.

## Slide 17: Appendix - Method C Capacity Short Settlement
Settlement Equations
RUCCSAMTi,q = (−1) × Max [RUCSFRSi,q × RUCMWAMTTOTh, 2 × RUCSFi,q × RUCMWAMTTOTh / RUCCAPTOTh] / 4
Where:
RUCSFRSi,q = RUCSFi,q / RUCSFTOTi
RUCSFTOTi = RUCSFi,q
RUCSFi,q = Max(0, RTAMLq,p,i × 4 − RUCCAPADJq,i)
RUCCAPADJq,i = HASLADJq,r,h + (RUCCPADJq,h – RUCCSADJq,h) + ( DAEPq,p,h – DAESq,p,h) + ( RTQQEPADJq,p,i – RTQQESADJq,p,i) + DCIMPADJq,p,i
LARUCAMTq,i = (−1) × (RUCMWAMTTOTh / 4 + RUCCSAMTTOTi) × LRSq,i
Variables
RUCCSAMT – $ – Capacity Short Amount
RUCSFRS – Capacity Shortfall Ratio Share
RUCSF – MW – Capacity Shortfall Quantity
RUCMWAMTTOT – $ – Total cost of the AS or RS Settlement
RUCCAPTOT – MW – Total MW of the RS or AS Settlement
RUCSFTOT – MW – Capacity Shortfall Quantity Total
RTAML – MWh – Real-Time Adjusted Meter Load
RUCCAPADJ – MW – Calculated Capacity for the QSE
HASLADJ – MW – High Ancillary Service Limit at Adjustment Period
RUCCPADJ – MW – Capacity Purchases at Adjustment Period
RUCCSADJ – MW – Capacity Sales at Adjustment Period
DAEP – MW – Day-Ahead Energy Purchase
DAES – MW – Day-Ahead Energy Sale
RTQQEPADJ – MW – Real-Time QSE to QSE Energy Purchase
RTQQESADJ – MW – Real-Time QSE to QSE Energy Sale
DCIMPADJ – MW – DC tie Import
LARUCAMT – $ – Load-Allocated Capacity Short Amount
RUCCSAMTTOT – $ – Total Capacity Short Amount
LRS – Load-Ratio Share

## Slide 18: Appendix - Method A and B cost allocation preliminary results
Preliminary modeled AS cost allocated in $/MW Nameplate capacity using 2024 and 2025 data
Impact on Cost of New Entry of a hypothetical gas peaker due to AS cost allocated under Method A
Note: CONE data based on data in “ERCOT CONE for 2026” Table ES-1
  AS costs allocated to generators will be passed on to consumers through long-term changes in retirement and new entry decisions
  Existing units may retire earlier (due to higher fixed costs) as compared to the status quo
  New entry would wait until expected net revenue is higher before they enter the market, and such higher net revenue is achieved through tighter supply-demand balance
  On average, dispatchable resources have lower $/MW-year AS cost allocation as compared to non-dispatchable resources
  AS cost allocation varies between technology types within non-dispatchable resources, with wind units have a larger $/MW-year AS cost allocation
  Moving from Method A to Method B increases AS cost allocation for solar, but decreases AS cost allocation for wind

## Slide 19: Consolidated themes - Stakeholder May TAC Feedback
ERCOT’s responses to the feedback are posted to today’s TAC meeting page.
RRS allocation challenged. [NRG · LCRA · Vistra]
Splitting regulation on forecast error implies "no forecast error, no regulation," which is wrong; regulation's value is its ramp rate to hold frequency even under perfect forecasts. [APA/SEIA]
Allocation logic & mechanics
Cost recovery & Net Savings
Assigning AS/RS costs to generators will be built into offers and ultimately borne by consumers. [APA/SEIA · Vistra]
Compensating generators for AS and then reallocating those costs back to them is a "circular and counterproductive" construct that weakens reliability investment signals. [Vistra]
Allocation logic & mechanics, Contd.
Show how the dispatchable / non-dispatchable / load cost shares were derived for Methods A/B (e.g., the regulation split). [APA/SEIA · LCRA]
Clarification requested on A/B mechanics — how cost shares were derived, outage handling, HSL vs. seasonal capacity, ESR charging/deploying, and the ECRS ND/Load split. [APA/SEIA · LCRA]
IMM prefers Method B (Method A close); Method C rationale less clear; suggests a performance-based option — track thermal forced outages by QSE/DME over several years for RRS, similar for renewables/regulation. [IMM]
Clarify Method C mechanics, RMR/RUC being called "reliability services," and whether load AS cost settles at the QSE level. [TAC: Engie, Vistra, CMC Steel]
Market impacts & implementation
Reallocating to generators could undermine the dispatchable investment/retention the Legislature has prioritized (SB3, HB1500, SB2627) — evaluate long-term, not just near-term accounting. [Vistra]
The charge is an economic headwind to dispatchable investment that grows as the system tightens; RTC has already cut AS revenues. [Vistra]
Model cost allocation under a probabilistic AS procurement methodology (the reform direction). [APA/SEIA]
As large loads grow they will shift A/B shares; provide large-load risk-driver data and consider allocating incremental large-load AS cost to that subset + note in the Legislature report. [APA/SEIA · LCRA]
Watch double-counting with firming — firmed resources already cover ramp-hour shortfalls. [APA/SEIA]
19