## Slide 1: FFSS Offer Cap Determination Heat Rate Methodology – 2026-2027 Season Ino González Principal Engineer – Market Design and Generation Economics ERCOT Wholesale Market Subcommittee (WMS) – August 5, 2026

## Slide 2: FFSS Offer Cap Determination – 2026-2027 Season Overview
FFSS Offer Cap ($/MW) = Heat Rate × Fuel Price × Hours, per 16 TAC § 25.520.
ERCOT must set a single heat rate for each of the three FFSSR categories eligible under § 25.520(c): on-site (Cat. 1), resource-controlled (Cat. 2), and contractual off-site (Cat. 3).
Fuel price = commodity index price + price adder, fuel oil index for Categories 1–2, natural gas index for Category 3, price adder $0.05/Gl for Category 1 and $0.50/MMBtu for Category 3.
Key Takeaway: For the 2026-2027 obligation period ERCOT calculated three separate FFSS Offer Caps – one per resource category – each combining a category-specific heat rate with the applicable fuel price and deployment hours (48-hour deployment), .
Category | Heat Rate (MMBtu/MWh) | Offer Cap ($/MW)
Cat. 1 – On-site | 13.52 | 17,083
Cat. 2 – Resource-controlled | 11.36 | 14,163
Cat. 3 – Contractual off-site | 12.62 | 2,183

## Slide 3: Heat Rate Methodology – Categories 1 & 2 (EPA Operating Data)
Key Takeaway: Category 1 and 2 heat rates are grounded in actual historical EPA operating data captured during hours when the Resources burned fuel oil, using a conservative 90th-percentile thresholds.
Parameter | Category 1 (Oil) | Category 2 (NG)
Data source | EPA hourly generation data | EPA hourly generation data
Study period | 2022–2026 (4 seasons) | 2022–2026 (4 seasons)
Output band used | 0.8–1.2 × midpoint (LSL–HSL) | 0.8–1.2 × midpoint (LSL–HSL)
Heat rate basis | 90th percentile of resource AHRs | 90th percentile of AHRs
Resulting heat rate | 13.52 MMBtu/MWh | 11.36 MMBtu/MWh

## Slide 4: Heat Rate Methodology – Category 3 (Verifiable Cost Data)
Category 3 – Contractual off-site FFSS
  Heat rate determined from ERCOT-approved Verifiable Cost (VC) data, not EPA operating data.
  Calculated heat rate at the midpoint for all Simple Cycle (SC) and Combined Cycle (CC) resources with approved VC not already included in Category 1.
  Averaged the individual heat rates separately by unit type – SC and CC.
  Used the SC average (12.62 MMBtu/MWh) as the Category 3 heat rate to encourage competitive offers from both SC and CC resources.
  Criteria may be revisited in future years as actual submissions are evaluated.
Key Takeaway: Category 3’s heat rate relies on approved Verifiable Cost data rather than EPA data, and ERCOT selected the higher Simple-Cycle value as the single category heat rate to preserve incentives for competitive offers from all eligible resource types.
Category 3 – Resource Type | Heat Rate (MMBtu/MWh)
Simple Cycle (SC) average | 12.62
Combined Cycle (CC) average | 8.04
Category 3 heat rate used (SC basis) | 12.62