## Slide 1
PUBLIC
NPRR 1337: ERS Enhancements
Mark Patterson
Sponsor, ERCOT
Posted May 26, 2026
Purpose
To summarize NPRR 1337, ERS Enhancements. This NPRR revises how ERS Loads qualify for the Alternate Baseline and how ERCOT measures ERS availability, so payments track actual, time-specific performance rather than a portfolio average.
Status
Requesting vote today from WMS.
Key Takeaways
Tightens the Alternate Baseline Test so only genuinely unpredictable Loads bypass the default baseline — closing a gap.
Replaces one portfolio-wide availability factor per Contract Term with a factor calculated for each ERS Time Period, so payments track actual performance.
ERCOT supports approval: These changes enhance the ERS program by improving reliability.

## Slide 2
PUBLIC
2
OVERVIEW
What this presentation covers
What is Emergency Response Service
How ERS pays QSEs to curtail Load or inject energy during emergencies
The problem this NPRR solves
Alternate baseline being used in ways that were not intended. Aggregated time periods hide some risk.
Change 1 — Alternate Baseline Test
Tightens who qualifies to skip the default baseline
Change 2 — Time-Period Availability
Moves from a single QSE first evaluation per Contract-Term to resource specific per-Time-Period evaluations
Reliability impact
Improving reliability by improving information available to ERCOT operators during ERS deployment events
Status & next steps
Where NPRR 1337 stands in the stakeholder process
Key Takeaway: NPRR 1337 makes two targeted changes to ERS qualification and payment rules — ERCOT staff supports approval.

## Slide 3
PUBLIC
3
BACKGROUND
Emergency Response Service, in brief
ERS is one of ERCOT's demand-side reliability tools.
A reliability backstop
ERCOT pays QSEs representing ERS Resources to curtail Load when ERCOT calls a deployment event — to avoid firm Load shed.
Two baseline types
The Default Baseline predicts Load from history and weather. The Alternate Baseline is reserved for Loads ERCOT determines are too unpredictable for a default model.
Payments
QSEs are paid for both performance during deployment or test events and resource availability during the contract term.
Key Takeaway: ERS is paid, testable, dispatchable demand response — and this NPRR refines how ERCOT decides who qualifies and how their performance is scored.

## Slide 4
PUBLIC
4
FRAMING THE PROBLEM
Why it matters
Some loads self-deploy. Alternate baseline being used in ways that were not intended. This allows many ERS loads to pass both event performance and availability requirements which they would otherwise likely fail if measured with any of the default baselines.
Aggregation hides risk. A single aggregate availability number at the QSE portfolio level can let a QSE and its resources pass overall while failing when it matters most — during the highest-risk periods.
Baseline selection. A Load with a highly price-responsive but otherwise flat shape can currently qualify for the Alternate Baseline. Reacting to price can make a Load's shape look “dynamic.”
Key Takeaway: Both gaps let ERS payments flow to capacity in ways not originally intended by ERS rules.
Aggregated time periods. Availability is measured per Contract Term across a QSE's whole portfolio, so a Resource's poor availability in a single high-risk ERS Time Period can be masked by strong availability in others.

## Slide 5
PUBLIC
5
PROPOSED CHANGE 1 OF 2
A tighter Alternate Baseline Test
New Alternate Baseline test. Before a Load can qualify for the Alternate Baseline, ERCOT will test whether its load shape is genuinely unpredictable — not just dynamic because it responds to price. Loads that fail the test. Must select one of the default baseline types to participate in ERS. Why this closes the gap. Today, a price-responsive Load can look “dynamic” during flat-price periods and “flat” during an event — letting it self-deploy ahead of ERCOT's instruction and still collect ERS payment for capacity that would have moved anyway.
Key Takeaway: Only Loads that are truly hard to predict — not merely price-responsive — should bypass the default baseline.

## Slide 6
PUBLIC
6
PROPOSED CHANGE 2 OF 2
Availability measured by ERS Time Period
Today. ERCOT calculates one QSE-portfolio-level availability factor for the entire ERS Standard Contract Term, using a time- and capacity-weighted average across all ERS Time Periods. Under NPRR 1337. ERCOT instead calculates the availability factor for each ERS Resource separately for each ERS Time Period. Effect on payment. The availability component of a QSE's payment for a given ERS Time Period is based on that period's own availability — high-availability periods no longer offset a poor one.
Key Takeaway: Granular, per-period availability scoring replaces a single number that could hide a bad period inside a good term.

## Slide 7
PUBLIC
7
SIDE BY SIDE
Current rules vs. NPRR 1337
Today
Under NPRR 1337
Alternate Baseline available to any Load even if its historical energy usage shows its predictable to be measured using a true baseline — including ones that are simply price-responsive
One availability factor covers an entire ERS Standard Contract Term for a QSE
A high availability period can offset a low one inside the same term
Alternate baseline is currently used in ways that were not originally intended
A dedicated test screens out Loads that only look dynamic because of price response
Availability to be measured at the resource level and calculated separately for each ERS Time Period
Each period's payment reflects that period's own performance
Payments track ERCOT's goal: reward capacity that wouldn't be there without the ERS payment
Key Takeaway: The NPRR improves the use of the alternate baseline and sharpens the availability metric — without changing the basic ERS payment structure.

## Slide 8
PUBLIC
9
WHERE THIS STANDS
NPRR 1337 status
May 26, 2026
Posted
ERCOT files NPRR 1337, ERS Enhancements.
August 5, 2026
WMS
ERCOT requesting vote today.
August 12, 2026
PRS
ERCOT will request urgent status and vote.
August 26, 2026
TAC
TAC review.
Next
Board & PUCT
If recommended by PRS / TAC, the NPRR proceeds to the ERCOT Board and PUCT for final action.
Key Takeaway: ERCOT aiming for September Board review.

## Slide 9
PUBLIC
10
KEY TAKEAWAYS
What to carry forward
1
ERS has grown among price-responsive Loads
Rapid growth in ERS Loads that can cheaply shift consumption has exposed two soft spots in the current rules.
2
Baseline choice is being tightened
Only Loads that are genuinely hard to predict — not just price-responsive — should qualify for the Alternate Baseline.
3
Availability will track each ERS Time Period
Payments no longer let a strong availability period mask a weak one inside the same Contract Term.
4
ERCOT supports approval
NPRR 1337 strengthens ERS qualification testing and performance evaluation.

## Slide 10
PUBLIC
11
CONTACTS & REFERENCES
Who to contact, what to read
Contacts
Sponsor
Mark Patterson, ERCOT Mark.Patterson@ercot.com
Market Rules Staff Contact
Brittney Albracht Brittney.Albracht@ercot.com
Related documents
ERS Technical Requirements and Scope of Work
Suspension and Reinstatement Procedures
Demand Response Baseline Methodologies (ERCOT.com)