## Slide 1
Netted Networks Proposal
Sai Moorty
August 21st, 2026

## Slide 2: Purpose
Foster discussion and solicit feedback
Identify Problem Statement(s)
Review Current Approach and its “Issues”
Review Netted Network Proposal
Discuss Next Steps and Design Criteria
NOTE: The term “BTM generation” in this presentation refers to generation co-located with load that operates when synchronously connected to the grid. Does NOT include Back-Up Generation.

## Slide 3: Some Terminology
BTM generation: In this presentation refers to generation co-located with load that normally operates when synchronously connected to the grid. Does NOT include Back-Up Generation.
Load Ratio Share (LRS) : Ratio of an Entity’s AML to ERCOT AML for an interval (e.g.15-minute Settlement Interval, or monthly peak, etc.)
IGF-PUN: Industrial generation facility as described in PURA § 39.151. (e.g., generation provides steam to industrial facility)
RPOL: Resource Planned Outage Limit
QSA: Quarterly Stability Assessment
VSS: Voltage Support Service
TCOS / 4CP: Transmission Cost / 4-Coincident Peak

## Slide 4: The Problem: Only One Registration Path for Co-located Load + Generation + Storage
Today, registration of a site with load and BTM generation/storage must register as a PUN and requires netting the generation and load within the site for purposes of settlement, and dispatch.
This single path creates three issues:
  ERCOT market and RUC processes have reduced visibility into the site's generation and storage — only surplus MW (after serving load) is offered into the market
  ERCOT's dispatch and commitment processes (SCED and RUC) are not well designed to call on off-line PUN generation, when there's a reliability need
  Energy Storage Resources (ESR) in a PUN are not eligible for Wholesale Storage Load (WSL) treatment — limiting how batteries can be monetized

## Slide 5: Netted Networks: The Concept
This concept is not proposal for a “speed to power”.
It is an operational construct for co-located load, generation and batteries that :
  Gives ERCOT operations more visibility and control
  Gives market participants - unlike a PUN - increased operational flexibility, and a better pathway to monetize their assets
  "Netted Networks" is a concept, not a specific implementation.

## Slide 6: Netted Networks Proposed Mechanics
All generation and batteries in a Netted Network must register as a market resource (GR,ESR)  enhanced ERCOT ISO visibility in comparison to a non-market resource
Resources (GRs, ESRs) in a Netted Network offer their entire capacity into the market (not just the surplus as is currently done at a PUN)
The gross load within Netted Network is part of ERCOT Load (not the net load as is the case for PUN load)
ESRs are eligible for WSL treatment as the co-located Load is part of ERCOT Load
Energy Settlements is net for the site – just like a PUN
Adjustments are needed in the calculation of energy prices for Load Zone and Netted Network POI Meter Price

## Slide 7: Comparison of PUN and Netted Network
AuxLd/StnLd
PUN Load
LZLd : Non-ERCOT Load
GR,ESR: HSL,LSL, NetMW calculated as Net of Gross minus AuxLd/StnLd and co-located load: HSL= Gross-AuxLd-LZLd
ESR in a PUN is not eligible for WSL treatment
Energy Settlements : Net at POI
4CP: Net at POI
LRS charge/credit: Net at POI
HSL, LSL, NetMW
GR
CLR
PUN
ESR
Reactive Power requirements measured at POIB
AuxLd/StnLd
GR,ESR: HSL,LSL, NetMW calculated as Net of Gross minus AuxLd/StndLd only: HSL= Gross-AuxLd
ESR in a Netted Network is eligible for WSL treatment
Energy Settlements : Net at POI
4CP: Gross Load or Net at POI (POLICY Decision)
LRS charge/credit: Gross load behind POI or Net at POI (POLICY Decision)
HSL, LSL, NetMW
GR
CLR
Netted Network
WSL
ESR
Reactive Power requirements measured at POIB
NN Load
LZLd : ERCOT Load
NO WSL

## Slide 8: Comparison of PUN (IGF and non-IGF) and Netted Networks
 | IGF PUN | Non-IGF PUN | Netted Network
Transmission/Distribution | Transmission only | Transmission only | Both Transmission and Distribution
Site can have Settlement Only generation and battery energy storage systems | Yes | Yes | No. Site cannot have any Settlement only generation or battery energy storage system All generation and battery energy storage systems must register with ERCOT as Generation Resources or Energy Storage Resource
Interconnection process for any Generation Resource (GR) and Energy Storage Resource (ESR) within this site | Identical to any Generation Resource and Energy Storage Resource for sites with co-located loads | Same as IGF PUN | Same as IGF PUN
Modeling for Quarterly Stability Assesment (QSA) | All modeling requirements for conducting adequate QSA studies must be submitted | Same as IGF PUN | Same as IGF PUN
Voltage Support/Reactive Requirements (VSS) | As per requirements for GR and/or ESR in ERCOT Nodal protocols Section 3.15 (4 (a) & (b) and Nodal Operating Guide Section 3.3.2, the provision of VSS/Reactive requirements are measured at the POIB | Same as IGF PUN | Same as IGF PUN
Outage process and RPOL | Certain exemptions to RPOL as per PURA § 39.151 | Planned Outages must be approved by ERCOT. Planned Outage approval subject to RPOL | Same as Non-IGF PUN unless exempted under PURA § 39.151
Telemetry and COP | Only surplus MW available after serving all co-located load for NetMW, HSL,LSL | Same as IGF PUN | Identical to any stand-alone GR and ESR. i.e. show gross capacity minus Aux/Station Load only.

## Slide 9: Comparison of PUN (IGF and non-IGF) and Netted Networks
 | IGF PUN | Non-IGF PUN | Netted Network
Energy Settlements | Net at POI | Net at POI | Net at POI
Resource Offer MW How much capacity (MW) can a Resource Offer to sell? | Net at POI (Surplus MW capacity after self serving all BTM load) | Net at POI (Surplus capacity after self serving all BTM load) | Gross MW capacity after serving Aux/Stn load – just like standalone Resource.
Wholesale Storage Load (WSL) eligibility for ESR | Not eligible | Not eligible | Eligible for WSL treatment as BTM load is ERCOT load
Load Ratio Share (LRS) calculation | Net at POI | Net at POI | TBD Policy decision: gross load or net at POI?
Transmission Cost (TCOST) allocation | Net at POI | Net at POI | TBD Policy decision: gross load or net at POI?
PowerFlow network model Vs RUC network model | Different as RUC model is net | Different as RUC model is net | PowerFlow network model and RUC network model are the same

## Slide 10: Further Refinements to the Netted Network concept?
Support Multiple POIs  being discussed at ERCOT
  Issue with Resource Entity owned transmission voltage station with multiple feeds having to become a NERC Balancing Authority/ Transmission Operator
  Meter Price, Load Zone Price, Settlements adjustments if site has storage
Support Settlement Only Generators and Settlement Only Energy Storage
  Storage systems that operate in synchronism with the ERCOT grid installed to address Voltage/Frequency Ride Through and Load Balancing for Electronic Large Loads that do not participate in the ERCOT markets
Address metering issues ( too many meters required, other configurations)