## Slide 1
Downstream Production Changes (DPC)- Process Automation
Yugendher Karedla / Yong Ma
Aug 20, 2026
Outline
  Refresher on DPC Automation concept
  Market Testing updates
  Access Request
  Implementation Timelines
This effort provides new tool to Market Participants to facilitate DPC submission process for Temporary DPCs.

## Slide 2: Downstream Production Changes (DPC)
Downstream Production Change (DPC) is a standard process that makes changes to the Network Model in production in between the weekly model loads without having to load a new model (database load).
This process is managed by the multiple teams at ERCOT (Network Modeling, GMS, Shift Engineers, Operations etc.).
DPC process helps update the network model in both Energy and Market Management systems (EMS and MMS) incorporating the changes submitted by the transmission operators that are critical to maintaining the reliability of the system.
The DPC process allows ERCOT to make specific data modifications in real-time including:
  Static Line / Transformers Ratings
  Dynamic Line Ratings
  Line / Transformer Impedance
  Contingency Definition updates
  Enabling and Disabling of Contingencies
  GTC updates
  RAP and RAS changes
GTC and RAP/RAS definition updates related DPCs are submitted by ERCOT Operations team.

## Slide 3: Downstream Production Changes (DPC)
DPC process is intended to make model changes in production between weekly model loads as necessary, not for model changes that can follow normal NOCMR timelines.
Current High level DPC Process
MP
(Submits Model changes for DPC)
NMMS
Jira Process
1. Review and Approve by Operations team
2. Track DPC implementation in EMS/MMS systems across multiple models
EMS/MMS
Review Model and Create DPC
DPC process demands significant collaboration efforts between several departments within ERCOT and market participants. It requires significant amount of manual effort to create, validate, track and implement DPCs in multiple environments across multiple weekly model loads.
The manual nature of DPC tasks often leads to inefficiencies, delays, and increased resource loading across several departments within ERCOT. This multifaceted process demands extensive time and resources to ensure accuracy and efficiency.

## Slide 4: Summary of feedback received from TOs
  TSP initiates new DPC submission
    when an operational line or transformer ratings / Impedances that gets published from their engineering team, is different from ERCOT Model ratings / Impedances.
    Based on rating comparisons done every month at TSP side & if they see discrepancy with ERCOT Model ratings.
  Current DPC NOMCR submission process involves
    Submitting DPC NOMCRs into ERCOT modeling system
    Send out email to notify ERCOT network modeling group
    Attach a DPC request form and reason for DPC with NOMCR
    After DPC is processed into ERCOT system, update TSPs EMS model to reflect the change.
  Current DPC CAMR submission process involves
    For equipment outages / reclosures, submit a DPC CAMR to enable Manual contingencies within 3 business days of effective date.
    If a new CTG is needed to reflect new configuration, attach an excel sheet with proposed CTG definition in CAMR.
    Submit a separate DPC CAMR within 3 business days of configuration returning to Normal.
    When active CTGs are found to be incorrect, CAMR DPC submitted to disable or edit incorrect CTGs.

## Slide 5: Distinction between Permanent and Temporary DPC type updates
  Permanent DPC types
    DPC updates that will be done in Production , but they also will need to go into Network Model
    These DPC updates will continue to be applied in Production for few more model loads, before they are included within NMMS CIM XML file.
    All DPC types are eligible for Permanent DPCs.
    Continue to follow the current process of submitting Permanent DPC NOMCRs into ERCOT modeling system.
  Temporary DPC types
    DPC updates that does not need to go into Network Model.
    DPC updates that requests ERCOT control room to make a temporary update to model data due to a field outage / field work, that can last for up to 2 weeks.
    Below are the 2 major Temporary DPC types that ERCOT receives from MPs
      Static Line / Transformers Ratings
      Enabling and Disabling of Contingencies
    New DPC UI Tool is developed to provide ability for MPs to quickly submit temporary DPCs, with effective dates to ERCOT production system.
  A new DPC Dashboard will be developed that provides full list of DPCs (both permanent and temporary DPCs) with their status (planned / Implemented) with a historian for past DPCs implemented.

## Slide 6: New DPC Tool – High Level Implementation Details
  New displays and dash boards will be added in current Outage Scheduler UI (OS UI) to allow Market Participants to submit Temporary DPCs with start and end times.
  Currently QSEs with resources and TOs have the access to OS UI through ERCOT MIS website
  A new role will be created to TOs to access these displays using OS UI.
  ERCOT Operations will review and approve Temporary DPCs.
  Upon approval, Temporary DPCs get implemented in ERCOT real-time systems (EMS/MMS) automatically and provides status back to DPC tool.
  Thereafter, DPCs get implemented automatically in EMS/MMS systems during every week model load until end time of DPCs.
  This new DPC tool will provide visibility to Market Participants on DPC implementation status in ERCOT EMS/MMS systems. Dashboards will be developed to meet this requirement along with ability to sorting and filtering capabilities

## Slide 7: New DPC Tool – High Level Implementation Details
  If a Temporary DPC submitted through DPC UI, is not yet implemented, TOs will have an option to Withdraw the DPC from their DPC Dashboard, using “Withdraw” status option.
  Once a Temporary DPC is approved at ERCOT and is Implemented in EMS / MMS Applications, TOs will not be able to “Withdraw” their submitted DPC. If this scenario arises, TOs can submit another new Temporary DPC to revert the implemented DPC TOs have to update the planned end date which eventually would close the DPC by reverting the updates with aligning to the model.
  ERCOT is pursuing an option to provide ability for TOs to associate Temporary DPC to an Outage. This will be an optional attribute (not mandatory), which allows more visibility to ERCOT, as we see several instances of Contingency status update DPCs tied to an Outage condition.
  TOs DPC dashboard will continue to show status updates on the submitted DPCs (both Permanent and Temporary DPCs), as ERCOT goes through DPC implementation and confirmation steps.

## Slide 8: New DPC Tool – High Level Implementation Details
  DPC Tool support following DPC Types
    Update Static Line / Transformers Ratings
    Enabling and Disabling of Contingencies
  DPC Tool Data Flows:
MPs
DPC Tool
EMS/MMS
ERCOT Review & Approval (DPC Dashboard)
Temporary DPCs
NMMS Mage (Network Model)
Permanent DPCs
DPC
Importer
MPs DPC dashboard (All DPCs)
OS UI

## Slide 9: Submitting Temporary DPCs – Contingency Status Changes
For Contingency Status Change DPCs this includes:
  Planned start/end, nature of work, operating company
  Notes, attachments
  Individual contingencies and future state
    Associated equipment for each contingency can also be viewed
  On submit, a summary of the changes will be presented along with a prompt to confirm

## Slide 10: DPC Dashboard- Default View
Displays DPCs pending approval or implementation with general info and link to view full details
Users can apply filters and personalize the view then save and reload it
Other views include the Archive (completed or rejected DPCs).

## Slide 11: DPC Details Popup
A DPC’s details can be viewed in the DPC Details popup
  This includes:
    General Information: description, type, creation date, duration, etc.
    Change Log: the list of all changes applied in this DPC
    DB Loads: the DB Loads the DPC is applied in
    Activity Log: key dates and events relating to the DPC (created on, implemented on, etc.)

## Slide 12: Submitting Temporary DPCs- Static Rating
Static Rating update DPCs form includes:
  Planned start/end, nature of work, operating company
  Notes, attachments
  Can review each specific device ratings and update.
  On submit, a summary of the changes will be presented along with a prompt to confirm
  Note – If a line/XF is dynamically rated, those lines/XFs will be automatically excluded from the drop down list for temporary DPCs, as this UI is only for Static rating updates.

## Slide 13: Handling Schedule Changes for Temporary DPCs
Withdrawal Option
  TOs can withdraw a DPC while it is “Submitted” Status , but NOT after it gets to “Approved for Implementation” status.
  Use case for Withdraw option is when TOs like to edit effective start/end dates or content of DPC, before it is approved for implementation at ERCOT. If Withdraw option is available, new DPC is not needed to make these modifications.
Effective End Date Modification- Applicable to implemented DPC.
  On Implemented status, TOs can modify the effective end date:
    Modify Effective end date to earlier date: Ends the DPC sooner.
    Modify Effective end date to later date: Extends the DPC duration.
  Note- effective end date needs to be greater than current date/time and cannot be 21 days from date of submission for Temporary DPCs.
No conflicting/duplicate DPCs for same elements:
  After DPC is implemented in production (Implemented Status, not Closed Status), if TOs want to change the DPC again, then a new DPC needs to be submitted for the same equipment. So, the procedure is to update the effective end date to current date/time and ensure the current DPC is in Closed Status (from DPC Dashboard). After DPC associated with a specific equipment is closed, TOs can submit a new DPC for same equipment with new start/end times.
Closed Status
  Once the effective end date is reached, the DPC automatically transitions to Closed status.
  Transition to Closed status - It would trigger EMS/Market applications to revert back to Model value/state in production.
  After DPC transitions to closed status, no further changes are allowed, and it will be archived for historical reference.

## Slide 14
DPC notifications from ERCOT CR
One address per organization — you manage the members
Suggested format
ercotdpcnotifications@[yourdomain]
ercotdpcnotifications@lcra.org
ercotdpcnotifications@oncor.com
ercotdpcnotifications@aep.com
ERCOT configures once
One address per org — no changes needed when your team membership changes
TO manages recipients
Add or remove team members from the alias without any ERCOT involvement
Instant staff changes
New hires added, departing members removed — all within your own systems
No personal emails at ERCOT
Individual addresses are never stored on the ERCOT side
NOTIFICATIONS SENT TO THIS ALIAS
✕
Rejected
DPC rejected by ERCOT; rejection reason included in the notification
⏰
Temporary DPC expiring
Sent XX days/hrs before expiration (6hrs??);

## Slide 15: DPC Dashboard Access
Access control
  Application access will be granted via digital certificates
  New roles must be added to the certificate for authorization
    Operator (DPC_M_OPERATOR)
    ReadOnly (DPC_M_VIEW)
    Effective for MOTE from 07/13/2026
    Effective for PROD from 08/28/2026
  How do I know if I have role in my certificate
  This is for PROD - https://mis.ercot.com/secure/profile
  Link will be available from current OSUI page (This feature will be available from September)

## Slide 16: Market Testing Updates
Companies onboarded and logged into the application during market testing
    Testing window opened on 11th May 2026
    TOs – 8 (Very low participation in Market Testing )
M-A051126-02 MOTE Testing: DPC Dashboard - Transmission Operator Testing of DPC Submission Form- Updates
TSPs can continue exploring in MOTE for the month of September. Ensure you got roles and ready for Submitting DPCs through new Dashboard from October.

## Slide 17: Implementation Timelines - Updates
Development and Testing Timelines
  12/09/2025 - Project got into Execution phase and Design Completed.
  DPC Tool changes Development and Testing – In Progress
  TOs Testing starts from 11th May – using MOTE.- In Progress M-A051126-02 MOTE Testing: DPC Dashboard - Transmission Operator Testing of DPC Submission Form- Updates
  ercotdpcsupport@ercot.com for any clarifications
Next Steps.
Capture/Resolve observations with Parallel Submission Period. – September 2026
Formal Go-Live / Switchover – October 2026

## Slide 18: Temporary DPC Submissions – Parallel Period & Switchover - Updates
Parallel Submission Period
  Starting September 2nd – TSPs are requested to submit Temporary DPCs in both NMMS MAGE and the new DPC UI
      Permanent DPCs not affected – continue through NMMS MAGE only, no change
      This is a parallel run, not a switchover – NMMS MAGE remains the system of record through September
      Purpose: gives TSPs a low-risk window to get comfortable with the DPC UI, and lets ERCOT confirm implementation, approvals, and notifications are working correctly – before Temporary DPCs move to the new tool exclusively
Formal Go-Live / Switchover
  October 2026 (date to be confirmed via Market Notice)
      Temporary DPCs will be submitted only through the DPC UI from this point forward
      NMMS MAGE will no longer be used for Temporary DPC submissions

## Slide 19: Questions/Comments?
ercotdpcsupport@ercot.com