## Slide 1: NPRR 1346, Updates to the Fuel Oil Price (FOP)
Protocol Revision Subcommittee (PRS)
September 16, 2026

## Slide 2: Truck Delivery Costs Have Risen Sharply Since 2015
Chart: 
| 2015 | 2016 | 2017 | 2018 | 2019 | 2020 | 2021 | 2022 | 2023 | 2024 | 2025 | 2026
Dry van truckload spot rate ($/mile, incl. fuel) | 1.85 | 1.66 | 1.88 | 2.22 | 1.86 | 2.05 | 2.66 | 2.72 | 2.34 | 2.33 | 2.46 | 3
Benchmark dry van truckload spot rates — the closest public proxy for tanker-truck fuel oil delivery — now stand at $3.00/mile as of July 2026, up roughly 60% since 2015 and above the 2022 annual average, though still below the January 2022 monthly peak of $3.11/mile, while the ERCOT fuel oil price adder has not been revisited in over a decade.
Illustrative only. Sources: DAT Freight Analytics / BTS; BLS PPI. Annual values are calendar-year averages of national dry van spot rates, incl. fuel; 2026 = July 2026.

## Slide 3: Texas Diesel Prices Are Back Near Cycle Highs
On-highway diesel serving Texas averaged $2.576/gal in 2015 and stands at $5.360/gal as of August 31, 2026 - more than double - reinforcing that delivered fuel oil costs have moved well beyond the assumptions behind the current $0.05/gal adder.
Source: EIA, Gulf Coast (PADD 3) No. 2 Diesel Retail Prices (Texas proxy; EIA publishes no Texas-specific diesel series). 2026 value is the 08/31/2026 weekly observation.

## Slide 4: Implied Delivery Cost Now Far Exceeds the $0.05 Adder
Chart: 
| 2015 | 2016 | 2017 | 2018 | 2019 | 2020 | 2021 | 2022 | 2023 | 2024 | 2025 | 2026
Freight only, excl. fuel surcharge ($/gal) | 0.051 | 0.045 | 0.052 | 0.061 | 0.051 | 0.056 | 0.073 | 0.075 | 0.064 | 0.064 | 0.067 | 0.082
Incl. diesel fuel surcharge ($/gal) | 0.057 | 0.049 | 0.058 | 0.069 | 0.058 | 0.061 | 0.081 | 0.091 | 0.076 | 0.074 | 0.076 | 0.101
Current ERCOT FOP adder ($0.05/gal) | 0.05 | 0.05 | 0.05 | 0.05 | 0.05 | 0.05 | 0.05 | 0.05 | 0.05 | 0.05 | 0.05 | 0.05
Converting freight rates to a per-gallon basis (≈200-mile Texas delivery, 7,300-gallon payload) implies $0.082/gal on freight alone today versus roughly $0.05/gal in 2015–2019.
Adding a diesel-based fuel surcharge at today’s $5.360/gal raises the implied cost to $0.101/gal – slightly above the proposed $0.10/gal adder.
Illustrative only. Freight series from public truckload spot rates; surcharge = (EIA Gulf Coast diesel – $1.25/gal peg) ÷ 6 mpg, applied over the stated delivery assumptions.

## Slide 5: Benefits and Next Steps
Benefits
  Aligns the FOP with the actual delivered cost of fuel oil.
  Reflects more than a decade of transportation cost inflation not captured in the current $0.05/gal adder.
  Relies on public, verifiable data sources that support transparent price validation.
  Improves cost recovery accuracy and supports fuel oil availability during scarcity conditions.
Next Steps
  ERCOT will file a subsequent NPRR to update the FOP in the Firm Fuel Supply Service (FFSS) context.
  Request PRS consideration and approval of NPRR 1346.

## Slide 6
Appendix

## Slide 7: Appendix: Transportation Cost Assumptions
Delivery Assumptions
  Representative Texas delivery distance, fuel terminal to generator: approximately 200 miles.
  Tanker-truck payload: 7,300 gallons, reflecting a full truck equivalent.
  Freight rate basis: national dry van truckload spot rate. Fuel surcharge inputs: EIA Gulf Coast diesel price, $1.25/gal base peg, 6 mpg tractor efficiency.
Calculation
  Freight cost per gallon = (freight rate $/mile × 200 miles) ÷ 7,300 gallons. Fuel surcharge per gallon = ((diesel $/gal – $1.25) ÷ 6 mpg × 200 miles) ÷ 7,300 gallons.
  2026 example: $0.082/gal freight ($3.00/mile, July 2026) + $0.019/gal surcharge (diesel at $5.360/gal) ≈ $0.101/gallon.
Sources and Limitations
  DAT Freight Analytics / BTS truck spot rates; BLS PPI, General Freight Trucking, Long-Distance Truckload; EIA Gulf Coast (PADD 3) No. 2 Diesel Retail Prices, used as the Texas proxy because EIA publishes no Texas-specific diesel series.
  Freight-only series excludes fuel surcharges; both series exclude Texas lane premiums, which would raise the estimate.
  All inputs are drawn from publicly available sources; no confidential or company-specific data is relied upon.