## Slide 1
Compute Heat Rate
Research note | Q3 2026 Index
1
Compute Heat Rate makes AI electricity tolerance measurable
An independent demand-side metric that translates workload economics into an electricity price threshold, expressed in $/MWh.
Research definition
Compute Heat Rate (CHR)
The long-run, full-cost electricity price threshold associated with workload economics, including non-electricity costs and a required-return treatment.
Dispatch Compute Heat Rate (CHR-D)
The dispatch-focused threshold at which an already-deployed workload becomes economically indifferent between continuing to operate and curtailing.
Q3 2026 public reference values
For a PCLR operating question, CHR-D is the relevant measure because it focuses on the economics of an already-deployed workload deciding whether to continue consuming.
~$9,070/MWh
Blended CHR-D
Q3 2026 dispatch and curtailment reference value across the active inference blend.
~$18,378/MWh
Frontier inference CHR-D
Dispatch-focused reference value for frontier inference, the highest-value active workload tier.
Long-run CHR
Blended CHR ~$5,630/MWh | Frontier inference CHR ~$12,791/MWh
Interpretation: high-value AI workloads can remain economically rational to operate at power prices far above conventional supply-side benchmarks.
Source: Royal, H. (2026), “CHR Reference Values, Q3 2026,” Compute Heat Rate Index, Sept. 1, 2026. Q3 canonical outputs: CHR_Master_Model_Q3 v3.2.
Framework: computeheatrate.com
Index: computeheatrate.com/chr-index
Commentary: computeheatrate.substack.com
Research: SSRN 6322318
Notes: Talk track: Compute Heat Rate is an independent research framework for expressing the economics of compute in electricity-market units. CHR is the long-run, full-cost threshold. CHR-D is the dispatch-focused threshold for an already-deployed workload. For the PCLR operating question, CHR-D is the relevant measure. Q3 2026 reports a blended CHR-D of $9,070.82/MWh and a frontier inference CHR-D of $18,377.75/MWh. [Sources] - Royal, H. (2026). "CHR Reference Values, Q3 2026." Compute Heat Rate Index, Sept. 1, 2026. https://computeheatrate.com/chr-index - Royal, Hans, "The Compute Heat Rate: Quantifying AI-Driven Electricity Price Tolerance and Its Implications for Wholesale Market Repricing" (Feb. 28, 2026), SSRN 6322318. https://doi.org/10.2139/ssrn.6322318 - Visual system: Kylie Pyatt, CHR research arm vs. RPE company brand comparison, Sept. 11, 2026.

## Slide 2
Compute Heat Rate
Research note | PCLR application
2
What the CHR means for PCLR
The research distinguishes a load’s economic willingness to consume from the separate reliability obligation created by the PCLR construct.
1. Economic value
CHR-D estimates the price at which an operating workload becomes economically indifferent between continuing to consume and curtailing.
2. Five-minute price signal
For high-value AI workloads, the relevant CHR-D can sit well above ordinary wholesale price signals. Continuous five-minute dispatch may therefore induce little voluntary response.
3. Reliability trigger
PCLR is a separate contractual reliability commitment. When the relevant transmission condition binds, the curtailment obligation remains controlling.
Research implication
CHR evidence supports separating ordinary economic dispatch from mandatory reliability curtailment. It does not imply a weaker curtailment obligation.
This is a research interpretation of the economic signal. ERCOT and stakeholders determine the operating standard and reliability trigger.
Framework: computeheatrate.com
Index: computeheatrate.com/chr-index
Commentary: computeheatrate.substack.com
Research: SSRN 6322318
Notes: Talk track: The narrow contribution from CHR is economic, not operational. CHR-D tells us how high an operating workload may rationally value continued consumption. That can explain why a five-minute price signal may not induce meaningful voluntary curtailment from a high-value AI workload. The PCLR reliability commitment is separate. When the transmission condition that matters for reliability binds, the agreed curtailment obligation still controls. [Sources] - Royal, H. (2026). "CHR Reference Values, Q3 2026." Compute Heat Rate Index, Sept. 1, 2026. https://computeheatrate.com/chr-index - Royal, Hans, "The Compute Heat Rate: Quantifying AI-Driven Electricity Price Tolerance and Its Implications for Wholesale Market Repricing" (Feb. 28, 2026), SSRN 6322318. https://doi.org/10.2139/ssrn.6322318 - Arushi Sharma Frank draft deck, "Relaxing Base Point Compliance for PCLRs," Sept. 20, 2026. - Visual system: Kylie Pyatt, CHR research arm vs. RPE company brand comparison, Sept. 11, 2026.