## Slide 1: Monthly Review of Reliability Unit Commitment Market Impacts – August 2026 Wholesale Market Working Group ERCOT Market Analysis September 2026

## Slide 2: RUC Resource-Hours
August 2026 | Total | Capacity |  | Congestion | 
 |  | Opt-Out | Non-Opt-Out | Opt-Out | Non-Opt-Out
Instructed Resource-Hours |  |  |  |  | 
Total Count | 821.0 | 33.0 | 756.0 | 4.0 | 28.0
Effective Resource-Hours* |  |  |  |  | 
Total Count | 782.1 | 32.9 | 717.4 | 3.8 | 27.9
Average Megawatts (MW) for Effective Resource-Hours |  |  |  |  | 
Average LSL | 45.2 | 77.4 | 43.0 | 148.0 | 50.1
Average LDL | 56.6 | 189.4 | 49.0 | 269.1 | 65.8
Average BP | 59.9 | 221.6 | 50.9 | 303.4 | 68.9
Average HSL | 166.0 | 249.4 | 155.3 | 412.1 | 308.2
* The difference between “Instructed” and “Effective” values is a result of Resources starting up, shutting down, receiving partial hour instructions, or otherwise not being dispatchable by SCED.

## Slide 3: RUC Instruction Reasons: Last 13 Months
RUC activity increased in August compared to July.
96% of RUC effective Resource-hours in August 2026 were nominally attributed to address capacity needs, particularly to ensure sufficient Ancillary Service quantities

## Slide 4: RUC Instruction Reasons in August 2026
There were 782.1 RUC total effective Resource-hours in August and 750.3 hours (96%) were committed to address capacity needs.
The highest effective Resource-hours in August occurred on August 8th to support capacity needs, which was associated with the higher projected net load forecast.

## Slide 5: Non-opt-out and Opt-out Totals: Last 13 Months
August 2026 had a total of 745.3 non-opt-out effective Resource-hours (95%) and 36.7 opt-out effective Resource-hours (5%).

## Slide 6: Non-opt-out and Opt-out Totals: August 2026
August 2026 had a total of 745.3 non-opt-out effective Resource-hours (95%) and 36.7 opt-out effective Resource-hours (5%).

## Slide 7: RUC Lead Time Margin: August 2026
60% of RUC commitment windows had a lead time margin of 2 hours or less.
“Lead time” refers to the length of time between a RUC instruction and the start of the commitment window.
“Lead time margin” is the difference between lead time and the Resource’s startup time.
  In cases where a Resource is committed for multiple back-to-back time blocks, lead time margin is calculated from the first instruction.

## Slide 8: Average Resource Age: Last 13 Months
In August 2026, the average age of RUC-committed Resources was 53.6 years for non-opt-out Resource-hours.
Note: For Resource configurations with multiple physical generators, the age of the oldest generator is used.

## Slide 9: Age Category: Last 13 Months
In August 2026, 91% of RUC effective Resource-hours were provided by Resources that were at least 50 years old.
Note: For Resource configurations with multiple physical generators, the age of the oldest generator is used.
Non-Opt-Out
Opt-Out

## Slide 10: RUC-Instructed Resource Dispatch above Low Dispatch Limit (LDL) in Non-Opt-Out Hours
Out of 745.3 non-opt-out effective Resource-hours, RUC-instructed Resources were dispatched above their LDL for 55.1 resource-hours.
  In 12.6 of these Resource-hours, the Locational Marginal Price (LMP) for the RUC-instructed Resource exceeded the RUC offer floor.
  In 42.5 of these Resource-hours, the LMP for the RUC-instructed Resource fell below the RUC offer floor.​ All 42.5 Resource-hours saw the RUC-instructed Resource being mitigated.
There were Exceptional Fuel Cost submissions for a single RUC-Committed Resource in August 2026.

## Slide 11: Reliability Deployment Price Adder for Energy: Last 13 Months
August 2026 had a total of 261.2 RTRDPA hours with a time-weighted average value of $1.48/MWh.
These graphs show RTRDPA instances by reliability action: 'RUC Only' for instances triggered solely by Reliability Unit Commitment, 'RUC and other triggers' for instances with RUC and additional triggers, and 'Other triggers only' for instances with non-RUC triggers. The daily average RTRDPA is calculated using the total duration across all categories. See ERCOT protocol section 6.5.7.3.1 for details.

## Slide 12: Reliability Deployment Price Adder for Energy: August 2026
These graphs show RTRDPA instances by reliability action: 'RUC Only' for instances triggered solely by Reliability Unit Commitment, 'RUC and other triggers' for instances with RUC and additional triggers, and 'Other triggers only' for instances with non-RUC triggers. The daily average RTRDPA is calculated using the total duration across all categories. See ERCOT protocol section 6.5.7.3.1 for details.
August 23rd had the highest daily time-weighted average RTRDPA of $16.00/MWh.

## Slide 13: Reliability Deployment Price Adders for Ancillary Services: Last 8 Months
The average values are calculated as time-weighted average Real-Time Reliability Deployment Price Adders for each Ancillary Service during SCED intervals with RDPA active for any reliability event trigger. RDPAs for Ancillary Services are only available after RTC+B implementation on December 5, 2025
In August 2026, average Ancillary Service price adders increased from July with the exception of Regulation Down.

## Slide 14: Reliability Deployment Price Adder for Ancillary Services: August 2026
The daily average values are calculated as time-weighted average Real-Time Reliability Deployment Price Adders (RDPA) for each Ancillary Service during SCED intervals with RDPA active for any reliability event trigger.
RDPA | Monthly Time Weighted Average ($/MWh)
Regulation Up (Reg-Up) | 0.30
Regulation Down (Reg-Down) | 0.01
Responsive Reserve Service (RRS) | 0.30
ERCOT Contingency Reserve Service (ECRS) | 0.50
Non-Spinning Reserves (Non-Spin) | 0.74

## Slide 15: RUC Clawback, Make-Whole, and Shortfall
Of the $1,151,299 in Make-Whole payments made in August 2026, $17.33 was uplifted to load due to rounding. The remaining amount was collected through Capacity-Short charges.
For August 2026, the total Clawback charge was $645,132. The total Make-Whole payment was $1,151,299.
Note: Settlements data as of 9/17/26

## Slide 16: RUC Clawback by Settlement Type
Month | Initial Settlement ($) | Resettlement 1 Change ($) | Final Settlement Change ($) | Resettlement 2 Change ($) | True-up Settlement Change ($) | Resettlement 3 Change ($) | Net ($)
Aug ‘25 | 12,319 | 0 | 0 | - | -2,121 | - | 10,198
Sep ‘25 | 122,634 | - | 0 | - | 0 | - | 122,634
Oct ‘25 | 128,343 | - | 0 | 0 | -68,059 | - | 60,284
Nov ‘25 | 80,805 | - | 0 | - | -14,883 | - | 65,922
Dec ‘25 | 233,500 | - | 0 | - | -14,862 | - | 218,638
Jan ‘26 | 1,130,396 | - | 0 | -530 | -123,450 | - | 1,066,416
Feb ‘26 | 0 | - | 0 | - | 0 | - | 0
Mar ‘26 | 856,743 | - | 0 | - | -758,806 | - | 97,937
Apr ‘26 | 242,784 | - | 0 | - | - | - | -
May ‘26 | 77,429 | - | 0 | - | - | - | -
Jun ‘26 | 138,880 | - | 0 | - | - | - | -
Jul ‘26 | 882 | - | 0 | - | - | - | -
Aug ‘26 | 645,132 | - | - | - | - | - | -
Negative dollars represent a payment from ERCOT to a QSE
For Initial, Final, and True-up Settlement, "–" means settlement is pending. For Resettlement, "–" means no Resettlement occurred for that month.
Resettlement types: Resettlement 1 occurs between Initial and Final Settlement; Resettlement 2 between Final and True-up Settlement; Resettlement 3 after True-up Settlement.
Net figures may differ slightly due to rounding.
Note: Settlements data as of 9/17/26

## Slide 17: RUC Make-Whole by Settlement Type
Month | Initial Settlement ($) | Resettlement 1 Change ($) | Final Settlement Change ($) | Resettlement 2 Change ($) | True-up Settlement Change ($) | Resettlement 3 Change ($) | Net ($)
Aug ‘25 | -487,773 | 0 | 0 | - | -110,640 | - | -598,413
Sep ‘25 | -2,035,251 | - | 0 | - | -538,306 | - | -2,573,557
Oct ‘25 | -1,016,193 | - | 0 | -3,671 | -593,209 | - | -1,613,073
Nov ‘25 | -1,151,712 | - | 0 | - | -1,739,486 | - | -2,891,198
Dec ‘25 | -271,995 | - | 0 | - | -696,055 | - | -968,051
Jan ‘26 | -431,896 | - | 0 | 2 | - | - | -431,893
Feb ‘26 | 0 | - | 0 | - | 0 | - | 0
Mar ‘26 | -324,968 | - | 0 | - | -13,440 | - | -338,409
Apr ‘26 | -76,725 | - | 0 | - | - | - | -
May ‘26 | -1,140,481 | - | 0 | - | - | - | -
Jun ‘26 | -1,322,710 | - | 0 | - | - | - | -
Jul ‘26 | -919,717 | - | 0 | - | - | - | -
Aug ‘26 | -1,151,299 | - | - | - | - | - | -
Note: Settlements data as of 9/17/26
Negative dollars represent a payment from ERCOT to a QSE
For Initial, Final, and True-up Settlement, "–" means settlement is pending. For Resettlement, "–" means no Resettlement occurred for that month.
Resettlement types: Resettlement 1 occurs between Initial and Final Settlement; Resettlement 2 between Final and True-up Settlement; Resettlement 3 after True-up Settlement.
Net figures may differ slightly due to rounding.

## Slide 18: Questions/Comments