## Slide 1: Comprehensive Transmission Planning (CTP)
October 20, 2026
Stakeholder workshop #3

## Slide 2
1. Antitrust admonition
2. CTP / Batch 1+ progress update
3. CTP process design: latest high-level process sequencing
4. Consensus building for selected design choices
    Case building and modeling
  PTA/RPG 2.0 and project criteria
  Batch Study
5. Summary of remaining open questions
6. Adjourn
7. Appendix – Supporting feedback from survey
2
On the agenda
PUBLIC

## Slide 3
1. Antitrust admonition
2. CTP / Batch 1+ progress update
3. CTP process design: latest high-level process sequencing
4. Consensus building for selected design choices
    Case building and modeling
  PTA/RPG 2.0 and project criteria
  Batch Study
5. Summary of remaining open questions
6. Adjourn
7. Appendix – Supporting feedback from survey
4
On the agenda
PUBLIC

## Slide 4: Progress on CTP
In Workshop 1 (Aug 31), we discussed the initial CTP scope and design criteria and shared themes from interviews with 27 TSPs
In Workshop 2 (Sep 24), we reviewed takeaways from survey responses and discussed several ideas for the future process design, including a Combined Batch + Reliability process, a consolidated case set, and the evolution of RPG into PTA / RPG 2.0
Since the last workshop, we have continued to digest and evaluate feedback on potential process designs. We have concluded that a Standalone Batch process (Batch, Commitment, Reliability studies) will best meet stakeholder needs near-term
Today, we will:
walk through the Standalone Batch end-to-end process;
go deeper on selected design choices; and
discuss the remaining open questions ahead of the Revision Request(s)

## Slide 5: Stakeholder roadmap: We are in the third stakeholder workshop, and moving towards drafting an initial NPRR/PGRR package
We are here
Stakeholder workshops
Initial process design & TSP interviews
Initial NPRR/PGRR draft package
Board consideration and transition
TAC and Board consider the package for approval; ERCOT transitions to the new CTP process
Draft rule package released for stakeholder review; full engagement sessions continue
ERCOT engages TSPs and stakeholders to understand preferences and pain points in depth
ERCOT scoped the early process design and completed initial TSP touchpoints

## Slide 6: Stakeholder roadmap: Workshops are on the path to revision requests
Forums
ROS
2026
2027
Q3
Q4
Q1
Jul
Aug
Sep
Oct
Nov
Dec
Jan
PRS
Workshops and working groups
Formally present CTP and Batch 1 PGRRs/NPRRs for approval
ERCOT Board
Objective
Interview TSP planning staff on CTP scope
Engage with Protocol Revisions Subcommittee on NPRR(s)
Engage with Reliability and Operations Subcommittee on PGRR(s)
TAC
Review/endorse combined NPRR/PGRR package for Board approval
ROS 11/5
ROS 12/3
PUCT OM
Provide updates to Commission on progress/emerging policy considerations
Conduct stakeholder workshops on CTP process design and Batch 1+
Stakeholder engagement
Meeting
Targeted date
July 16 – late August
Workshop 1 8/31
LLWG
Engage with Large Load Working Group on Batch 1+
LLWG 8/21
LLWG 9/17
LLWG 11/19
LLWG 12/17
Workshop 2 9/24
Draft scope from ERCOT
Workshop 3 – Batch 10/15
Workshop 5 12/2
Workshop 4 11/9
Further scoping details discussion
Details of design elements discussion
Review Revision Requests and market comments
April Board approval
11/1 File initial Revision Requests
7/8 ERCOT market notice
March TAC approval
Feb
Mar
Apr
Q2
ROS 1/7
ROS 2/4
ROS 3/4
ROS 4/8
ROS 10/1
Board 12/7-8
Board 2/8-9
Board 4/12-13
PRS 10/14
PRS 11/11
PRS 12/9
PRS 1/12
PRS 2/16
PRS 3/10
PRS 4/14
LLWG 10/15
TAC 10/28
TAC 11/18
TAC 1/20
TAC 8/28
TAC 7/29
TAC 2/24
TAC 3/24
TAC 4/28
As needed
Specific sessions to be selected for updates
Preliminary
Workshop 3 – CTP 10/20
To be discussed

## Slide 7
1. Antitrust admonition
2. CTP / Batch 1+ progress update
3. CTP process design: latest high-level process sequencing
4. Consensus building for selected design choices
    Case building and modeling
  PTA/RPG 2.0 and project criteria
  Batch Study
5. Summary of remaining open questions
6. Adjourn
7. Appendix – Supporting feedback from survey
8
On the agenda
PUBLIC

## Slide 8: A Combined Batch + Reliability process may be impractical under current requirements
  Over the past several weeks, we have evaluated two approaches to a Comprehensive Transmission Planning process (both of which have been shared in prior workshops):
    A standalone Batch process with planning studies (e.g., steady state reliability studies, short circuit) completed after the Batch and commitment window;
    A combined Batch + Reliability process that completes both scopes in tight coordination, followed by a commitment window and a refinement study
  The combined approach minimizes restudies, but is hard to execute due to the large pre-commitment scope, a challenging path to an annual cadence, and rework risk
  Based on our analysis, stakeholder interviews, and survey feedback, we are proposing a standalone Batch process as the most effective path forward
  The following slides outline how the standalone Batch process works and what it means for stakeholders

## Slide 9: A standalone Batch process can be implemented in the near term; a combined Batch may offer greater efficiency as capabilities mature
How it works
Advantages
Disadvantages
The Batch acts as a screening of large loads, allocating capacity so loads can commit
Reliability studies (addressing TPL and ERCOT reliability criteria) then run on committed loads only to produce the actionable transmission plan
Batch study scope can be completed sooner as standalone study
Standalone Batch (Batch then Reliability)
Combined Batch (Batch + Reliability)
Batch and reliability studies run in parallel before commitment, addressing allocation TPL/ERCOT reliability criteria
A refinement study afterwards produces the actionable transmission plan based only on committed load
Most efficient: the system is studied once for both allocation and TPL, which avoids restudies
Shorter end-to-end timeline: ~18 months, with potential to accelerate further with an integrated study and limited load attrition at commitment
The system is studied twice: once in the Batch and again in the reliability study
Longer end-to-end cycle: 20 months+, with overlapping annual cycles
Large pre-commitment scope: analyses on all cases with higher load volume
Does not fully remove rework risk: early handoffs of cases for Batch and reliability studies requiring potential rework in every iteration
Simpler for near-term implementation: builds on Batch Zero and works with today’s tools and staffing
Longer-term option: may be viable in future years depending on size of Batch study, process improvements or automation

## Slide 10: CTP process: Key design elements of the standalone Batch process
Annual cadence
Batch study (allocation and commitment) runs every year
Allocate all 5 years
Batch study allocates capacity for all 5 years (Y2-Y6)
Reliability study on committed loads
Full reliability (e.g., steady state, short circuit, dynamics, NERC TPL and ERCOT-specific criteria1) studies are performed on committed loads only (i.e., post-Batch)
Transparency for all projects
ERCOT and TSPs provide visibility into reliability projects prior to finalizing the actionable transmission plan
Targeted project alternatives
Run alternatives analysis on specific projects (e.g., high-cost, CCN required)
1. ERCOT reliability criteria include P7 treatment, X‑1+N‑1, Large Load contingencies, minimum deliverability and maintenance outage criteria

## Slide 11: Standalone Batch process: A ~20-month end-to-end cycle preserves pre-commitment allocation while shifting detailed reliability work after that
PRELIMINARY
Batch identifies preliminary transmission solutions and allocates capacity; the subsequent reliability study completes the required TPL and ERCOT reliability analyses
Source: ERCOT Extended Work Sessions for Comprehensive Transmission Planning
Batch process
Modeling
Reliability study
XX
Areas for further alignment
Beginning of next Batch + CTP cycle
Meet TPL and ERCOT reliability requirements
Finalize actionable Txn plan
M2
M1
M3
M5
M7
M9
M12
M10
M11
M14
M13
M16
M18
M19
M15
M17
M4
M20
M6
M8
Model prep
Cases and modeling
A
First CTP model build
Remaining non-CTP model builds
Other CTP model build
Post-commitment reliability study: Full NERC TPL and ERCOT reliability criteria analysis
C
Steady state reliability study
Short circuit reliability study
Full stability (dynamic) reliability study
This path leaves more complex analyses for the post-commitment reliability study, providing more time to complete reliability requirements
Commitment window (60 days)
Committed loads (being reflected in latest model build)
Proposed preliminary projects
Pre-commitment Batch study: Capacity allocation and preliminary project identification
Dynamic model preparation
Preliminary stability screening
N-1 cases
Final Batch cases
N-1 Y6
B
Steady state study
Short circuit study
RPG 2.0
RPG 2.0
RPG 2.0
RPG 2.0
Project Transparency and Alternatives (PTA)
Capacity allocation and Batch transmission project library
PRELIMINARY
ERCOT and TSPs collaborate to identify preliminary solutions; stakeholders get visibility into proposed projects
ERCOT and TSPs collaborate to resolve reliability violations. Stakeholders can review and comment on projects, including alternatives where applicable

## Slide 12: Year over year: a new cycle starts every 12 months and takes ~20 months, delivering an actionable transmission plan every 12 months
PRELIMINARY
Source: ERCOT Extended Work Sessions for Comprehensive Transmission Planning
CTP model building complete
Modeling inputs (i.e., loads, topology, generation)
Batch study (6 months)
Commit (2 mo.)
Reliability study (TPL + ERCOT criteria) – 12 months
Batch study (6 months)
Commit (2 mo.)
Reliability study (TPL + ERCOT criteria) – 12 months
Batch study (6 months)
Commit (2 mo.)
Reliability study (TPL + ERCOT criteria) – 12 months
6 months
6 months
6 months
6 months
6 months
6 months
6 months
CTP Year N
CTP Year N+1
CTP Year N+2
Extraction of the Batch projects w/ some refinement (4 months)
Extraction of the Batch projects w/ some refinement (4 months)
Actionable transmission plan
Load
Generation
Topology
Load
Generation
Topology
Load
Generation
Topology
One actionable transmission plan every 12 months
No-regrets / local projects can get approved earlier
No-regrets / local projects can get approved earlier
Single annual CTP model build; Batch inherits latest models
~20 months
Each cycle takes ~20 months end to end
Actionable transmission plan
Unresolved major projects
Unresolved major projects
RPG 2.0
RPG 2.0
RPG 2.0
RPG 2.0
RPG 2.0
RPG 2.0
RPG 2.0
Project Transparency and Alternatives (PTA)
PRELIMINARY

## Slide 13
1. Antitrust admonition
2. CTP / Batch 1+ progress update
3. CTP process design: latest high-level process sequencing
4. Consensus building for selected design choices
    Case building and modeling
  PTA/RPG 2.0 and project criteria
  Batch Study
5. Summary of remaining open questions
6. Adjourn
7. Appendix – Supporting feedback from survey
14
On the agenda
PUBLIC

## Slide 14: How the next section is organized
Each topic starts with a process deep-dive, then covers the key design choices, and closes with a summary of consensus and open areas
Process details and deep-dive
Design choices
Summary and open areas
Detail on the selected process step and its specific items (e.g., sequencing, hand-offs, cases and timing), and how the step fits into the standalone Batch process
Key design choices for the step: the design question, the options considered, the working assumption, what was heard from stakeholders, and the rationale; each choice is tagged by level of alignment
A recap of where there is consensus and which questions remain open for further discussion, plus space to raise any additional topics
We have tagged open questions for discussion on select slides with icons

## Slide 15
1. Antitrust admonition
2. CTP / Batch 1+ progress update
3. CTP process design: latest high-level process sequencing
4. Consensus building for selected design choices
    Case building and modeling
  PTA/RPG 2.0 and project criteria
  Batch Study
5. Summary of remaining open questions
6. Adjourn
7. Appendix – Supporting feedback from survey
16
On the agenda
PUBLIC

## Slide 16: Cases and modeling – deep-dive: A single consolidated CTP case set, built sequentially, serves the Batch, TPL and other users
Takeaways
  One consolidated case set: 17 CTP cases replace the separate SSWG and RTP builds
    Sequential build: the Y6/Y4/Y2 cases come first so the study can start early, followed by Y5/Y3 and the TPL-only cases
  Non-CTP cases built last: raw network data is published so stakeholders can build their own cases
Illustrative process schematics
Model prep
Update network topology
Update gen data
Update load forecasts
First CTP model build
Produce Y6/4/2 cases
Solve Y6/4/2 sum pk cases
Other CTP model build
Produce Y5/Y3 cases
Solve Y5/Y3 sum peak + Y3 ML/HRML cases
Remaining non-CTP model builds
Solve remaining cases for internal and external stakeholders (e.g., FIS cases)
Hand over library of raw data (network files)
Supporting feedback: All TSPs support consolidating SSWG and RTP case building, and most respondents support publishing raw network data for self-service
  ERCOT produces 9 cases for the planning years Y6, Y4 and Y2 (summer peak, no solar and fall peak for each year)
  ERCOT produces the remaining 8 CTP cases (summer peak, no solar and fall peak for Y5 and Y3, plus the Y3 minimum load and Y3 HRML cases needed for TPL)
  ERCOT builds the other cases that internal and external users need, e.g., interconnection (FIS), operations and seasonal cases and hands over a library of raw network files
XX
XX
TSP engagement
Areas for further alignment

## Slide 17: Cases and modeling – deep-dive: Timing of the annual CTP model snapshot: available options
Supporting feedback: All TSPs support a single consolidated CTP case build; TSPs are split on whether one snapshot per year is enough, which suggests targeted updates between snapshots
Description
ERCOT takes the annual CTP snapshot at the start of each cycle, with updated topology, generation and load forecasts; the Batch study runs on this snapshot
After commitment, the same model is updated with committed loads for the reliability study
ERCOT takes the annual CTP snapshot once committed loads are known
It becomes the starting point for the reliability study, and the next Batch runs on the same model, plus its own Batch loads
Implications
The Batch starts from the latest system data captured at the start of the cycle
A committed-load update is needed after commitment (redispatch, contingencies, TSP data) before reliability studies can begin
The snapshot already reflects committed loads, so reliability studies start directly from it
The Batch uses the prior cycle’s snapshot; changes since then are captured in the next reliability study cycle and the next snapshot
Year N
Year N
Year N-1
Option
CTP model snapshot taken before Batch Study
CTP model snapshot taken after Batch Study commitment window
Modeling
Modeling
Reliability study
Batch Study
Reliability study
Commit
Batch Study
Reliability study
Commit
Modeling
Proposed option
Modeling update with committed loads
  Open question Updates between snapshots: which targeted updates are needed between snapshots, and when inputs are frozen each cycle

## Slide 18: Cases and modeling – design choice: One two-step CTP case build replaces SSWG and RTP
Meet TPL and ERCOT reliability requirements
Project Transparency and Alternatives
RPG 2.0
RPG 2.0
RPG 2.0
RPG 2.0
Batch process
Modeling
Reliability study
Latest CTP process
Source: CTP TSP survey, fielded 09/15–09/21
Beginning of next Batch + CTP cycle
Finalize actionable Txn plan
M2
M1
M3
M5
M7
M9
M12
M10
M11
M14
M13
M16
M18
M19
M15
M17
M4
M20
M6
M8
Allocate capacity
Post-commitment reliability study: Full NERC TPL and ERCOT reliability criteria analysis
C
Steady state reliability study
Short circuit reliability study
Full stability (dynamic) reliability study
Commit. window (60 days)
Preliminary Txn plan and capacity allocations
Committed loads
Proposed projects
Pre-commitment Batch study: Capacity allocation and preliminary project identification
Dynamic model preparation
Preliminary stability screening
Batch transmission project library
N-1 cases
Final Batch cases
N-1 Y6
B
Steady state study
Short circuit study
Design question
Should SSWG and RTP case building be consolidated into one CTP case-building process?
Options considered
1. Sequential CTP build: critical planning cases first, remaining cases after, replacing SSWG and RTP
2. Keep SSWG and RTP separate
What we heard through interviews and/or surveys
71%
of respondents support full consolidation (100% of TSPs)
Rationale
One common case foundation and forum for all CTP analyses; critical path cases are prioritized and the rest follow
Highlighted steps show where this design choice applies in the standalone Batch process
Model prep
Cases and modeling
A
First CTP model build
Remaining non-CTP model builds
Other CTP model build
Clear alignment

## Slide 19: Cases and modeling – design choice: ERCOT publishes a core set of solved cases; the format for additional case data is still to be defined
Meet TPL and ERCOT reliability requirements
Project Transparency and Alternatives
RPG 2.0
RPG 2.0
RPG 2.0
RPG 2.0
Batch process
Modeling
Reliability study
Latest CTP process
Source: CTP TSP survey, fielded 09/15–09/21
Beginning of next Batch + CTP cycle
Finalize actionable Txn plan
M2
M1
M3
M5
M7
M9
M12
M10
M11
M14
M13
M16
M18
M19
M15
M17
M4
M20
M6
M8
Allocate capacity
Post-commitment reliability study: Full NERC TPL and ERCOT reliability criteria analysis
C
Steady state reliability study
Short circuit reliability study
Full stability (dynamic) reliability study
Commit. window (60 days)
Preliminary Txn plan and capacity allocations
Committed loads
Proposed projects
Pre-commitment Batch study: Capacity allocation and preliminary project identification
Dynamic model preparation
Preliminary stability screening
Batch transmission project library
N-1 cases
Final Batch cases
N-1 Y6
B
Steady state study
Short circuit study
Design question
What should ERCOT provide for cases beyond the core set1?
Options considered
1. Core set of solved cases only
2. Core set of solved cases + network data packages3 for self-service (format and tooling to be defined)
3. Core set of solved cases + ERCOT-solved additional cases
What we heard through interviews and/or surveys
64%
of respondents agree/ strongly agree2: concern on support needed to solve/ assemble additional cases
Rationale
Allows entities build the cases they need without ERCOT solving every combination. Either format needs new tooling, training and a support model
Model prep
Cases and modeling
A
First CTP model build
Remaining non-CTP model builds
Other CTP model build
1. Core set = the 17 CTP cases ERCOT builds for Batch and TPL: summer peak, no solar and fall peak for Y2–Y6, plus Y3 minimum load and Y3 high-renewable minimum load (HRML) | 2. The survey (Q21) referenced an 8-case minimum core set (Y2 summer peak and no solar; Y3 HRML, minimum load and summer peak; Y5 summer peak and no solar; Y6 summer peak). The proposed 17-case set includes all 8 | 3. Two possible formats: (a) unsolved cases built from the CTP model, or (b) the underlying MOD project files that users apply themselves
Views differ
Highlighted steps show where this design choice applies in the standalone Batch process
  Open question Format for additional case data: unsolved cases or MOD project files, and the tooling, training and support each would need

## Slide 20: Cases and modeling – design choice: One short-circuit case per study year, based on summer peak topology
Meet TPL and ERCOT reliability requirements
Project Transparency and Alternatives
RPG 2.0
RPG 2.0
RPG 2.0
RPG 2.0
Batch process
Modeling
Reliability study
Latest CTP process
Source: CTP TSP survey, fielded 09/15–09/21
Beginning of next Batch + CTP cycle
Finalize actionable Txn plan
M2
M1
M3
M5
M7
M9
M12
M10
M11
M14
M13
M16
M18
M19
M15
M17
M4
M20
M6
M8
Allocate capacity
Post-commitment reliability study: Full NERC TPL and ERCOT reliability criteria analysis
C
Steady state reliability study
Short circuit reliability study
Full stability (dynamic) reliability study
Commit. window (60 days)
Preliminary Txn plan and capacity allocations
Committed loads
Proposed projects
Pre-commitment Batch study: Capacity allocation and preliminary project identification
Dynamic model preparation
Preliminary stability screening
Batch transmission project library
N-1 cases
Final Batch cases
N-1 Y6
B
Steady state study
Short circuit study
Design question
Which short-circuit cases should ERCOT produce for CTP?
Options considered
1. A short-circuit case for every steady-state scenario
2. One short-circuit case per study year, based on summer peak topology (with a winter topology case to be evaluated)
3. Keep today’s SPWG short-circuit case set
What we heard through interviews and/or surveys
TSPs split on whether short-circuit cases need to match every steady-state case
Rationale
Short-circuit studies model all generation online and don’t depend on load, so only topology matters. Summer peak captures the highest generation each year
Highlighted steps show where this design choice applies in the standalone Batch process
Model prep
Cases and modeling
A
First CTP model build
Remaining non-CTP model builds
Other CTP model build
NOTE: A winter case may be needed where winter topology differs materially from summer. Cases will continue to be delivered in ASPEN format for TSP short-circuit studies
Clear alignment
  Open question Short-circuit case building: whether to consolidate it with steady-state case building?

## Slide 21: Cases and modeling: Areas with consensus…
… and questions that need further debate
One CTP case build replaces SSWG and RTP: a single, two-step build of the 17-case set for the Batch and TPL
Critical cases first: Y6/Y4/Y2 are built first so the study can start early, with the remaining cases after
One short-circuit case per study year, based on summer peak topology
Format for additional case data: unsolved cases or MOD project files, and the tooling, training and support each would need
Updates between annual snapshots: which targeted updates are needed between snapshots, and when inputs are frozen each cycle
Short-circuit case building: whether to consolidate it with steady-state case building
Is there anything else that you would like to discuss?
Is there disagreement on any of the above items?

## Slide 22
1. Antitrust admonition
2. CTP / Batch 1+ progress update
3. CTP process design: latest high-level process sequencing
4. Consensus building for selected design choices
    Case building and modeling
  PTA/RPG 2.0 and project criteria
  Batch Study
5. Summary of remaining open questions
6. Adjourn
7. Appendix – Supporting feedback from survey
23
On the agenda
PUBLIC

## Slide 23: Project Transparency and Alternatives: Pathway for a given project is determined based on project type
Current pathway
RPG
Project type
Economic
  In-kind
TSP criteria
Resiliency
Load growth
  Reliability
Proposed pathway
RPG 2.0
CTP Project Transparency and Alternatives (can continue processing in RPG 2.0 if not complete by the end of CTP)
Project identified in CTP?
PUBLIC
  Storm-hardening
  Aging infrastructure
Illustrative – for discussion

## Slide 24: Project Transparency and Alternatives: Project eligibility mapping for PTA and RPG 2.0 projects
Alternative testing
Stakeholder transparency
RPG review and comments
RPG with ERCOT Independent Review
Does project meet materiality threshold?
Project type
RPG 2.0
Storm-hardening
Aging infrastructure
In-kind
Economic
Resiliency
CTP Project Transparency only
CTP Project Transparency and Alternatives
Yes
No
Is a full project alternative analysis needed?
PTA
Load growth project identified through CTP
Reliability project identified through CTP
PUBLIC
Yes
No
Illustrative – for discussion
Detailed next
  Open question Early approvals: which projects can move ahead before the full actionable plan (e.g., no-regrets, local, Tier 3/4)

## Slide 25: Project Transparency and Alternatives: Four proposed criteria help determine which projects might need an alternative review
CCN
Cost
Regional vs local
Voltage level
Does the project require a Certificate of Convenience and Necessity (CCN)?
Does the total project capital cost exceed the defined cost threshold (currently $200M)?
Does the project include facilities at or above the defined voltage threshold (currently 345 kV)?
Does the project have competing transmission solutions proposed by different TSPs (regional project)?
Criterion
Open questions
-
What should the cost threshold be?
What should the voltage threshold be?
How should regional vs. local be defined (e.g., regional projects have competing TSP proposals?)

## Slide 26: Project Transparency and Alternatives: Proposed combination of criteria determines the level of project review
Alternative project review needed?
Any
CCN
Yes
No
No
No
No
No
Cost
>=$200M
<$200M
>=$200M
>=$200M
<$200M
Voltage level
>=345 kV
<345 kV
<345 kV
>=345 kV
>=345 kV
Regional vs local
Regional
Local
Local
Regional
Local
Tier 3 / 4 projects today
Clear need for Project Alternative Testing
ERCOT discretionary review
Criteria
Project Transparency and Alternatives
Project Transparency and Alternatives
Project Transparency and Alternatives
No
<$200M
>=345 kV
Regional
Project Transparency and Alternatives
No
<$200M
<345 kV
Regional
ERCOT discretion
Project Transparency only
ERCOT discretion
No
>=$200M
<345 kV
Local
Project Transparency and Alternatives
ERCOT discretion

## Slide 27: PTA: Ongoing transparency spans CTP and RPG 2.0, while unresolved CTP projects continue through RPG 2.0
Stakeholder transparency and engagement forum Ongoing visibility into proposed projects; stakeholder input and alternative proposals where applicable
Model prep
Model build
Commitment window
Reliability study (TPL + ERCOT criteria)
Batch Study
Approved CTP/RPG 2.0 projects feed into subsequent CTP model
Projects not finalized within CTP continue through RPG 2.0
Batch process
Modeling
Reliability study
No-regrets / local projects going directly to RPG 2.0
Stakeholder transparency and review (via RPG monthly meetings - TBC)
TSPs and other eligible project sponsors
RPG 2.0 (e.g., every 6 months)
RPG-eligible projects (storm-hardening, economic, TSP criteria, in-kind, aging infrastructure, and resiliency projects)
CTP - Project Transparency and Alternatives (PTA)
Qualified load and reliability projects (from steady state, stability, short circuit)
  Open question Stakeholder engagement: whether PTA and RPG 2.0 share one forum and cadence, and how long comment windows last RPG 2.0 cadence and review: how often windows open (e.g., every 6 months) and the level of review by project type

## Slide 28: PTA/RPG 2.0 – design choice: PTA makes all CTP projects transparent and tests alternatives where it matters, RPG 2.0 handles everything else (1/4)
Meet TPL and ERCOT reliability requirements
Batch process
Modeling
Reliability study
Latest CTP process
Source: CTP TSP survey, fielded 09/15–09/21
Beginning of next Batch + CTP cycle
Finalize actionable Txn plan
M2
M1
M3
M5
M7
M9
M12
M10
M11
M14
M13
M16
M18
M19
M15
M17
M4
M20
M6
M8
Allocate capacity
Post-commitment reliability study: Full NERC TPL and ERCOT reliability criteria analysis
C
Steady state reliability study
Short circuit reliability study
Full stability (dynamic) reliability study
Committed loads
Design question
How is RPG integrated with CTP?
What we heard through interviews and/or surveys
Rationale
Avoids duplicate reviews and longer approvals; keeps a path for other project types
Highlighted steps show where this design choice applies in the standalone Batch process
Model prep
Cases and modeling
A
First CTP model build
Remaining non-CTP model builds
Other CTP model build
Commit. window (60 days)
Preliminary Txn plan and capacity allocations
Proposed projects
Pre-commitment Batch study: Capacity allocation and preliminary project identification
Dynamic model preparation
Preliminary stability screening
Batch transmission project library
N-1 cases
Final Batch cases
N-1 Y6
B
Steady state study
Short circuit study
Options considered
1. Load-driven and reliability projects go through PTA within CTP; RPG 2.0 handles the rest
2. Retain RPG for all projects
3. Allow either path
Clear alignment
RPG 2.0
RPG 2.0
RPG 2.0
RPG 2.0
61%
of respondents agree/ strongly agree with alternative testing and public comment alongside CTP
Project Transparency and Alternatives

## Slide 29: PTA/RPG 2.0 – design choice: PTA makes all CTP projects transparent and tests alternatives where it matters, RPG 2.0 handles everything else (2/4)
Meet TPL and ERCOT reliability requirements
Batch process
Modeling
Reliability study
Latest CTP process
Source: CTP TSP survey, fielded 09/15–09/21
Beginning of next Batch + CTP cycle
Finalize actionable Txn plan
M2
M1
M3
M5
M7
M9
M12
M10
M11
M14
M13
M16
M18
M19
M15
M17
M4
M20
M6
M8
Allocate capacity
Post-commitment reliability study: Full NERC TPL and ERCOT reliability criteria analysis
C
Steady state reliability study
Short circuit reliability study
Full stability (dynamic) reliability study
Committed loads
Design question
What remains in RPG 2.0?
What we heard through interviews and/or surveys
55%
of respondents (84% of TSPs) support expanding Tier 3/4 to more in-kind, aging-infrastructure and storm-hardening projects
Rationale
CTP is comprehensive for reliability; a path remains for other project types
Highlighted steps show where this design choice applies in the standalone Batch process
Model prep
Cases and modeling
A
First CTP model build
Remaining non-CTP model builds
Other CTP model build
Commit. window (60 days)
Preliminary Txn plan and capacity allocations
Proposed projects
Pre-commitment Batch study: Capacity allocation and preliminary project identification
Dynamic model preparation
Preliminary stability screening
Batch transmission project library
N-1 cases
Final Batch cases
N-1 Y6
B
Steady state study
Short circuit study
RPG 2.0
RPG 2.0
RPG 2.0
RPG 2.0
Options considered
1. All except CTP load and reliability projects: economic, resiliency, storm-hardening, in-kind, aging infrastructure, TSP criteria and projects unresolved at cycle end
2. All currently RPG-eligible projects
3. Tier 3/4 only
Clear alignment
Project Transparency and Alternatives

## Slide 30: PTA/RPG 2.0 – design choice: PTA makes all CTP projects transparent and tests alternatives where it matters, RPG 2.0 handles everything else (3/4)
Meet TPL and ERCOT reliability requirements
Batch process
Modeling
Reliability study
Latest CTP process
Source: CTP TSP survey, fielded 09/15–09/21
Beginning of next Batch + CTP cycle
Finalize actionable Txn plan
M2
M1
M3
M5
M7
M9
M12
M10
M11
M14
M13
M16
M18
M19
M15
M17
M4
M20
M6
M8
Allocate capacity
Post-commitment reliability study: Full NERC TPL and ERCOT reliability criteria analysis
C
Steady state reliability study
Short circuit reliability study
Full stability (dynamic) reliability study
Committed loads
Design question
What is the scope of PTA?
What we heard through interviews and/or surveys
61%
of respondents agree/ strongly agree with alternative testing and public comment alongside CTP
Rationale
Builds confidence where it matters most and keeps the plan on schedule
Highlighted steps show where this design choice applies in the standalone Batch process
Model prep
Cases and modeling
A
First CTP model build
Remaining non-CTP model builds
Other CTP model build
Commit. window (60 days)
Preliminary Txn plan and capacity allocations
Proposed projects
Pre-commitment Batch study: Capacity allocation and preliminary project identification
Dynamic model preparation
Preliminary stability screening
Batch transmission project library
N-1 cases
Final Batch cases
N-1 Y6
B
Steady state study
Short circuit study
Options considered
1. Transparency for all projects; alternatives analysis for a subset of impactful projects
2. Stakeholder comments only
3. Alternatives for all projects
RPG 2.0
RPG 2.0
RPG 2.0
RPG 2.0
Clear alignment
Project Transparency and Alternatives

## Slide 31: PTA/RPG 2.0 – design choice: PTA makes all CTP projects transparent and tests alternatives where it matters, RPG 2.0 handles everything else (4/4)
Meet TPL and ERCOT reliability requirements
Batch process
Modeling
Reliability study
Latest CTP process
Source: CTP TSP survey, fielded 09/15–09/21
Beginning of next Batch + CTP cycle
Finalize actionable Txn plan
M2
M1
M3
M5
M7
M9
M12
M10
M11
M14
M13
M16
M18
M19
M15
M17
M4
M20
M6
M8
Allocate capacity
Post-commitment reliability study: Full NERC TPL and ERCOT reliability criteria analysis
C
Steady state reliability study
Short circuit reliability study
Full stability (dynamic) reliability study
Committed loads
Design question
What determines which projects require alternatives analysis?
What we heard through interviews and/or surveys
71%
of respondents say tiering should be revisited, but views differ on the basis
Rationale
A transparent, repeatable framework, with ERCOT discretion limited to edge cases
Highlighted steps show where this design choice applies in the standalone Batch process
Model prep
Cases and modeling
A
First CTP model build
Remaining non-CTP model builds
Other CTP model build
Commit. window (60 days)
Preliminary Txn plan and capacity allocations
Proposed projects
Pre-commitment Batch study: Capacity allocation and preliminary project identification
Dynamic model preparation
Preliminary stability screening
Batch transmission project library
N-1 cases
Final Batch cases
N-1 Y6
B
Steady state study
Short circuit study
Options considered
1. Defined criteria (CCN, cost, regional vs. local impact, voltage) with limited ERCOT discretion
2. ERCOT discretion only
RPG 2.0
RPG 2.0
RPG 2.0
RPG 2.0
Views differ
Project Transparency and Alternatives

## Slide 32: PTA/RPG 2.0: Areas with consensus…
… and questions that need further debate
PTA within CTP: load-driven and reliability projects go through Project Transparency and Alternatives inside CTP, and RPG is narrowed to RPG 2.0
Transparency for all projects: alternatives analysis is reserved for a subset of impactful projects
RPG 2.0 for other project types: economic, resiliency, storm-hardening, in-kind, aging infrastructure and TSP-criteria projects
Staged transparency: ERCOT and TSPs collaborate during the Batch, stakeholders review projects during the reliability study
Stakeholder engagement: whether PTA and RPG 2.0 share one forum and cadence, and how long comment windows last
Criteria for alternatives analysis: cost and voltage thresholds, how regional vs. local is defined, and how much ERCOT discretion applies
RPG 2.0 cadence and review: how often windows open (e.g., every 6 months) and the level of review by project type
Early approvals: which projects can move ahead before the full actionable plan (e.g., no-regrets, local, Tier 3/4)
Is there anything else that you would like to discuss?
Is there disagreement on any of the above items?

## Slide 33
1. Antitrust admonition
2. CTP / Batch 1+ progress update
3. CTP process design: latest high-level process sequencing
4. Consensus building for selected design choices
    Case building and modeling
  PTA/RPG 2.0 and project criteria
  Batch Study
5. Summary of remaining open questions
6. Adjourn
7. Appendix – Supporting feedback from survey
34
On the agenda
PUBLIC

## Slide 34: Year-by-year breakdown of study scope and expected outputs
PRELIMINARY
Year
Y6
Y5
Y4
Y3
Y2
System condition
Summer peak
No solar
Fall peak
Summer peak
No solar
Fall peak
Summer peak
No solar
Fall peak
Summer peak
No solar
Fall peak
Summer peak
No solar
Fall peak
HRML
Min load
Contingencies to be studied
N-1
GX
Other2
N-1-1
N-1
GX
Other
N-1-1
GX
Other
N-1-1
N-1
GX
Other
N-1-1
N-1
GX
Other
N-1-1
N-1
GX
Other
N-1-1
N-1
GX
Other
N-1-1
N-1
GX
Other
N-1-1
N-1
GX
Other
N-1-1
N-1
GX
Other
N-1-1
N-1
GX
Other
N-1-1
N-1
GX
Other
N-1-1
N-1
GX
Other
N-1-1
N-1
GX
Other
N-1-1
N-1
GX
Other
N-1-1
N-1
GX
Other
N-1-1
N-1
GX
Other
N-1-1
Selection
Steady State study depth
Transmission projects
Preliminary projects
Validate only
Validate only
Identify placeholders
Identify placeholders
Identify placeholders
Identify placeholders
Identify placeholders
PRELIMINARY – DRAFT FOR DISCUSSION
MW Allocation
Full
Partial
Rollover
Full
Partial
Rollover
Full
Partial
Rollover
Full
Partial
Rollover
Full
Partial
Rollover
Full
Partial
Rollover
Full
Partial
Rollover
Full
Partial
Rollover
Full
Partial
Rollover
Full
Partial
Rollover
Full
Partial
Rollover
Full
Partial
Rollover
Full
Partial
Rollover
Full
Partial
Rollover
Full
Partial
Rollover
N-1
Full
Partial
Rollover
Full
Partial
Rollover
Batch study
Reliability/TPL
Cost allocation
Dynamics study depth
Standalone Batch
Combined Batch
Standalone Batch Process – Batch Study
Preliminary projects
Preliminary projects
Validate only
Validate only
Validate only
Validate only
Identify placeholders
Yes
Yes
Yes
Yes
Yes
1. Dynamics screening refers to a preliminary stability assessment using steady-state study cases to identify potential stability constraints (e.g., voltage collapse), without developing the full dynamic models or performing comprehensive time-domain simulations required for TPL | 2. Other: selected NERC TPL‑001 multiple-element events (P2, P4, P5), e.g., internal breaker failure, stuck breaker, and protection system failure
Yes
NOTE: Partial studies evaluate only problematic contingencies identified in neighboring full-study years vs. rerunning the complete contingency sets. Rollover carries forward the allocation from an adjacent studied year, without new analysis
Dynamics screening1

## Slide 35: Batch study – design choice: Full study of three of five years (Y2, Y4, Y6) with partial study in between, allocating capacity for all five years
Meet TPL and ERCOT reliability requirements
RPG 2.0
RPG 2.0
RPG 2.0
RPG 2.0
Project Transparency (ERCOT and TSPs collaborate and share project information)
Project Transparency and Alternatives (projects are formally reviewed by stakeholders)
Batch process
Modeling
Reliability study
Latest CTP process
Source: CTP TSP survey, fielded 09/15–09/21
Beginning of next Batch + CTP cycle
Finalize actionable Txn plan
M2
M1
M3
M5
M7
M9
M12
M10
M11
M14
M13
M16
M18
M19
M15
M17
M4
M20
M6
M8
Allocate capacity
Post-commitment reliability study: Full NERC TPL and ERCOT reliability criteria analysis
C
Steady state reliability study
Short circuit reliability study
Full stability (dynamic) reliability study
Committed loads
Design question
How many years receive a full study in the Batch, and how are the remaining years covered?
Options considered
1. Full study of all five years (Y2–Y6)
2. Full study of three years (Y2/Y4/Y6), partial study of Y3/Y5, with capacity allocated for all five years
What we heard through interviews and/or surveys
65%
of respondents prefer studying three years instead of all five, for a faster Batch process
Rationale
Studying three of five years keeps the Batch on schedule. Evenly spaced full-study years bracket each partial year, so capacity is still allocated in every year, consistent with the Batch Zero approach
Highlighted steps show where this design choice applies in the standalone Batch process
Model prep
Cases and modeling
A
First CTP model build
Remaining non-CTP model builds
Other CTP model build
Commit. window (60 days)
Preliminary Txn plan and capacity allocations
Proposed projects
Pre-commitment Batch study: Capacity allocation and preliminary project identification
Dynamic model preparation
Preliminary stability screening
Batch transmission project library
N-1 cases
Final Batch cases
N-1 Y6
B
Steady state study
Short circuit study
Clear alignment

## Slide 36: Batch study – design choice: ERCOT and TSPs identify preliminary solutions together through planner-to-planner sessions
RPG 2.0
RPG 2.0
RPG 2.0
RPG 2.0
Project Transparency (ERCOT and TSPs collaborate and share project information)
Project Transparency and Alternatives (projects are formally reviewed by stakeholders)
Batch process
Modeling
Reliability study
Latest CTP process
Source: CTP TSP survey, fielded 09/15–09/21
Beginning of next Batch + CTP cycle
Meet TPL and ERCOT reliability requirements
Finalize actionable Txn plan
M2
M1
M3
M5
M7
M9
M12
M10
M11
M14
M13
M16
M18
M19
M15
M17
M4
M20
M6
M8
Allocate capacity
Post-commitment reliability study: Full NERC TPL and ERCOT reliability criteria analysis
C
Steady state reliability study
Short circuit reliability study
Full stability (dynamic) reliability study
Committed loads
Design question
How do ERCOT and TSPs identify and confirm preliminary solutions?
Options considered
1. ERCOT-led, TSP review at fixed milestones
2. Collaborative ERCOT–TSP model e.g., 60-day window for TSPs to create preliminary solutions, with bi-weekly planner-to-planner sessions
What we heard through interviews and/or surveys
72%
of respondents support planner-to-planner sessions (100% of TSPs)
Rationale
TSPs get enough time to validate feasibility and in-service dates, and bi-weekly sessions keep ERCOT and TSPs exchanging results throughout
Highlighted steps show where this design choice applies in the standalone Batch process
Model prep
Cases and modeling
A
First CTP model build
Remaining non-CTP model builds
Other CTP model build
Commit. window (60 days)
Preliminary Txn plan and capacity allocations
Proposed projects
Pre-commitment Batch study: Capacity allocation and preliminary project identification
Dynamic model preparation
Preliminary stability screening
Batch transmission project library
N-1 cases
Final Batch cases
N-1 Y6
B
Steady state study
Short circuit study
Views differ
79%
of TSPs want more than 45 days for preliminary solutions
  Open question TSP review window length: 60 days vs. a shorter window (30–45 days) Batch project library: the tooling to record projects and share them with TSPs

## Slide 37: Batch study: Areas with consensus…
… and questions that need further debate
Study years: full study of Y2, Y4 and Y6 and partial study of Y3 and Y5, with capacity allocated for all 5 years
Collaborative ERCOT–TSP model: planner-to-planner sessions to identify and confirm preliminary solutions
Clear output: capacity allocations and a preliminary project library, with the actionable plan coming from the reliability study
TSP review window length: 60 days vs. a shorter window (30–45 days)
Batch project library: the tooling to record projects and share them with TSPs
Is there anything else that you would like to discuss?
Is there disagreement on any of the above items?

## Slide 38
1. Antitrust admonition
2. CTP / Batch 1+ progress update
3. CTP process design: latest high-level process sequencing
4. Consensus building for selected design choices
    Case building and modeling
  PTA/RPG 2.0 and project criteria
  Batch Study
5. Summary of remaining open questions
6. Adjourn
7. Appendix – Supporting feedback from survey
39
On the agenda
PUBLIC

## Slide 39: Unresolved topics we still need to discuss (today or next workshop)
Macro-area
Open questions
Cases and modeling
Format for additional case data: unsolved cases or MOD project files, and the tooling, training and support each would need
Updates between annual snapshots: which targeted updates are needed between snapshots, when inputs are frozen each cycle
Short-circuit case building: whether to consolidate it with steady-state case building
PTA/RPG 2.0
Stakeholder engagement: whether PTA and RPG 2.0 share one forum and cadence, and how long comment windows last
Criteria for alternatives analysis: cost and voltage thresholds, how regional vs. local is defined, and how much ERCOT discretion applies
RPG 2.0 cadence and review: how often windows open (e.g., every 6 months) and the level of review by project type
Early approvals: which projects can move ahead before the full actionable plan (e.g., no-regrets, local, Tier 3/4)
Batch study
TSP review window length: 60 days vs. a shorter window (30–45 days)
Batch project library: the tooling to record projects and share them with TSPs

## Slide 40
1. Antitrust admonition
2. CTP / Batch 1+ progress update
3. CTP process design: latest high-level process sequencing
4. Consensus building for selected design choices
    Case building and modeling
  PTA/RPG 2.0 and project criteria
  Batch Study
5. Summary of remaining open questions
6. Adjourn
7. Appendix – Supporting feedback from survey
41
On the agenda
PUBLIC

## Slide 41: Thank you

## Slide 42
1. Antitrust admonition
2. CTP / Batch 1+ progress update
3. CTP process design: latest high-level process sequencing
4. Consensus building for selected design choices
    Case building and modeling
  PTA/RPG 2.0 and project criteria
  Batch Study
5. Summary of remaining open questions
6. Adjourn
7. Appendix – Supporting feedback from survey
43
On the agenda
PUBLIC

## Slide 43: Appendix Supporting slides and Survey Results

## Slide 44: CTP survey results are informing future process design
Dimension
What we heard from stakeholders
Topic
Batch process
Modeling and case building
Reliability study
Most survey participants support fewer Batch study years with a faster Batch process (65%)
Batch scope
Most survey participants support ERCOT's proposals for ILLEs with unfulfilled ramps (76%), uncommitted large loads (73%), and large loads excluded from Batch Zero (76%)
Batch re-study proposals
Majority of TSPs (62%) believe TSPs should select a load’s POI; ILLEs are more evenly split between TSPs and ILLEs as the selector
POI determination
Most survey respondents (71%) and all TSPs (100%) support the consolidation of the SSWG and RTP case building processes
Case building consolidation
45% of TSPs agree an annual CTP case re-build is sufficient, while 36% disagree
Case building frequency
Respondents have suggested expanding the core case set to include winter peak cases (9 respondents), as well as no-solar cases (6 respondents)
Case set
Most respondents (61%) support (strongly agree or agree) the introduction of a project alternative testing process within CTP
Project alternative testing
Most respondents (55%) and TSPs (84%) support the expansion of Tier 3 and Tier 4 to include more in-kind, aging infrastructure and storm-hardening projects
Tier 3 and 4 expansion
TSPs (100%) are fully supportive of establishing planner-to-planner sessions to review preliminary transmission solutions
Planner-to-planner sessions
PUBLIC
Preliminary

## Slide 45: Batch processes: Key takeaways from the survey
PUBLIC
Topic
Takeaways
POI determination
Majority of TSPs (62%) believe TSPs should select a load’s POI; ILLEs are more evenly split between TSPs and ILLEs as the selector
Batch re-study proposals
Most survey participants support ERCOT's proposals for ILLEs with unfulfilled ramps (76%), uncommitted large loads (73%), and large loads excluded from Batch Zero (76%)
Batch screening
Most TSPs support POI identification (80%) and minimum interconnection identification (87%) prior to Batch study qualification. ILLEs are more divided, with 61% supporting POI identification and 48% supporting minimum interconnection identification
Batch enhancement prioritization
Respondents support prioritizing the following Batch enhancements in the near term:
Large load self-supply outside of Batch (24 respondents)
BYOG at a different location (21 respondents)
WLPUN exit plan (18 respondents)
Define operational battery registration (17 respondents)
Develop rules for using an interconnected battery as part of PCLR (16 respondents)

## Slide 46: Batch processes: Point of Interconnection (POI) identification
XX
# of respondents
PUBLIC
Source: CTP TSP survey, fielded 09/15–09/21 (n = 74 respondents; 15 blank responses).
Q1: Which entity should select a load’s POI? % of respondents
Chart: 
 | 61.5385 | 41.3793 | 29.4118 | 42.3729
 | 15.3846 | 41.3793 | 47.0588 | 37.2881
 | 15.3846 | 6.8966 | 11.7647 | 10.1695
 | 7.6923 | 3.4483 | 0 | 3.3898
 | 0 | 6.8966 | 11.7647 | 6.7797
0%
TSP
ILLE
Others
Total
TSP
ILLE
DSP
ERCOT
No Opinion
13
29
17
59
Respondent
Majority of TSPs (62%) believe TSPs should select a load’s POI; ILLEs are more evenly split between TSPs and ILLEs as the selector

## Slide 47: Batch processes: TSP POI modeling timing
Q2: After a TSP signs an Intermediate Agreement with a Large Load, how long should it take for the TSP to submit to ERCOT the POI and modeling information (steady state only)? (free response)
Common themes (# of responses)
Observations
Converge on ~30 days as the default (9)
Plurality landed on 30 days, with some allowing up to 45 for complex configurations
Tier the deadline by complexity (10)
For simple POIs, respondents accept deadlines in the order of days. Complex POIs needing steady-state analysis seen as meriting 6-8 weeks. Several noted "workload" and case-specific factors as legitimate drivers of variance
Flexibility around delays (3)
If the TSP misses the deadline for reasons outside the ILLE's control, the project shouldn't lose its Batch slot. Any extension should come with a documented, revised binding date
Source: CTP TSP survey, fielded 09/15–09/21 (n = 74 respondents; 27 blank responses).
PUBLIC

## Slide 48: Batch processes: Pre-Batch feasibility screens
80%
61%
87%
48%
40%
26%
33%
32%
0%
13%
Q4: When should pre-Batch feasibility screens be completed and by whom? % of respondents
Q3: What pre-Batch feasibility screens, if any, should TSPs run before loads qualify for a batch study (select all that apply)? # of selections
XX
% of respondent type selecting
PUBLIC
Chart: 
 | 8 | 3 | 7 | 5 | 5 | 1
 | 19 | 15 | 8 | 10 | 1 | 4
 | 12 | 13 | 6 | 5 | 0 | 0
Point of Interconnection Identification
3
Minimum Interconnection Identification
Required Local Screening Study
Optional Local Screening Study
1
None
1
No opinion
39
31
21
20
6
5
TSP
ILLE
Others
Source: CTP TSP survey, fielded 09/15–09/21 (n = 74 respondents; 10 blank responses).
Chart: 
 | 61.5385 | 61.5385 | 86.6667 | 68.5185
 | 38.4615 | 38.4615 | 13.3333 | 31.4815
TSP
ILLE
Others
Total
Prior to Batch application by TSPs
After Batch application and prior to Batch study by TSPs
13
# of respondents
26
15
54
xx
44%
17%
39%
28%
6%
0%
3%
28%
POI and minimum interconnection identification were the most recommended pre-Batch feasibility screens
Majority of respondents (69%) believe pre-batch screens should be completed by TSPs prior to a Batch application

## Slide 49: Batch processes: Platform features
Q5: ERCOT is considering the following features for the proposed load interconnection and registration platform: application tracking, timeline visibility, and document upload and sharing. Are there any other features you would like to be considered in the first release of the platform?
Theme
Survey quotes and suggestions
Automate milestone and deficiency alerts
  "Automated notifications/alerts when milestones are approaching or overdue"
  Notices on "deadlines, status changes, and upcoming milestones"
Make ownership explicit
  "Responsibility matrix identifying each required action and responsible party"
  Visibility into "who is responsible for the next step"
Preserve an audit trail; allow error correction without penalty
  "Time-stamped audit trail of submissions and decisions"
  Version control on documents
  "Correcting administrative errors without losing Batch eligibility”
Extend role-based access and confidentiality to third parties
  "Role-based access with robust confidentiality/permission controls"
  ILLE can "authorize access for its DSP, TSP, consultants“
  "Heavy confidentiality restrictions on all data uploaded"
Enable in-platform messaging and case management
  "Secure messaging between ILLE, TSP and ERCOT"
  "Ticketing and case-management function" to submit, track, resolve questions
Show queue position and attribute delays by party
  "Queue position visibility" within the study pipeline
  "Distinguish ILLE-caused delays from ERCOT/TSP processing time"
Track full project lifecycle, not just intake
  Extend tracking through ramp schedules, security/fee payments, to commissioning and energization
Source: CTP TSP survey, fielded 09/15–09/21 (n = 74 respondents; 31 blank responses).
PUBLIC

## Slide 50: Batch processes: Batch re-study proposals
Q6: ILLEs with unfulfilled ramp: ERCOT is proposing that ILLEs with unfulfilled ramp may request re-study under their original Large Load Batch (LLB) tracking number
Q7: Uncommitted large loads: ERCOT is proposing for large load projects that did not commit in prior Batch, that they may request inclusion in subsequent Batch studies, provided they (i) formally request it and (ii) pay a new study fee. The ILLE’s financial security, intermediate agreement, LL tracking number, and all portal information would carry forward to the new Batch study
Q8: Large loads excluded from Batch Zero: ERCOT is proposing to allow large loads that received a tracking number, but were excluded from Batch Zero, to request inclusion in Batch One. ERCOT will waive the subsequent Batch fee if the interconnecting TSP/DSP attests that the ILLE has already paid at least $100k in study fees for the project. The ILLE must meet all other Batch One study requirements
Q6-8: Do you agree with ERCOT’s proposed approach [to the following issues]? % of respondents
PUBLIC
Source: CTP TSP survey, fielded 09/15–09/21 (n = 74 respondents; 15 blank responses).
Chart: 
 | 66.6667 | 81.8182 | 76 | 87.5 | 76.2712
 | 13.3333 | 9.0909 | 8 | 12.5 | 10.1695
 | 20 | 9.0909 | 16 | 0 | 13.5593
TSP
ILLE
Generators
Others
Total
Yes
No
No Opinion
Chart: 
 | 86.6667 | 54.5455 | 72 | 75 | 72.8814
 | 0 | 36.3636 | 8 | 25 | 13.5593
 | 13.3333 | 9.0909 | 20 | 13.5593
TSP
ILLE
Generators
Others
Total
# of respondents
xx
15
11
25
8
Chart: 
 | 73.3333 | 63.6364 | 76 | 100 | 76.2712
 | 6.6667 | 18.1818 | 24 | 0 | 5.0847
 | 20 | 18.1818 | 18.6441
TSP
ILLE
Generators
Others
5%
Total
59
15
11
25
8
59
15
11
25
8
59
Majority of respondents (73-76%) agree with ERCOT’s three proposed approaches to improve the Batch process

## Slide 51: Batch processes: Priority BYOG enhancements (1/4)
Category
WLPUN registration and lifecycle
WLPUN enhancements
Alternative BYOG enhancements
Enhancement
WLPUN opt-out option during Commitment
WLPUN exit plan
WLPUN generation additions
WLPUN on-ramp for existing Large Load
WLPUN Dynamic Limits
Large load self-supply outside of Batch
WLPUN with Settlement Only Generation
Large Load island transition to grid-connected
BYOG at different location
Description
Allow a Large Load with WLPUN to elect to be a standalone Large Load if the batch study results in full withdrawal capability for the load; i.e., cancel the GINR project without losing the load allocation
Define how a WLPUN can transition to different registration upon completion of energization of planned facilities (load, generation, and transmission upgrades as applicable)
Define how to add more generation to an existing/planned WLPUN site.
Define how to add generation to an existing/planned standalone Large Load so that it becomes a WLPUN
Define how WLPUN withdrawal limits could change from static to dynamic values in real-time
Allow a Large Load with generation to connect before going through the batch if the load ensures that it will not consume from the grid until after it goes through a batch process, i.e., use the GINR process
Allow a WLPUN to use Settlement Only generation
Define process for islanded configurations to become grid-connected
Develop BYOG option for generation at a different location from the Large Load (if selected, provide comment on extent of "different location", such as one station away, or beyond)
1
2
3
4
5
6
7
8
9

## Slide 52: Batch processes: Priority BYOG enhancements (2/4)
Category
Alternative BYOG enhancements cntd.
Battery enhancements
Enhancement
Description
Define and allow Self-Limiting Facility (SLF) Private Use Networks (PUN)
Combine SLF and PUN concepts
10
Pursue BYOG option of Netted Network
Consider in the planning process how Netted Network concept discussed at Aug 21 LLWG would impact allocations if adopted in Operations.
11
Allow Multiple POIs and/or Customer-owned Substations
n/a
12
Allow mix of resources at PUN
Allow a mix of different resource registration categories at a PUN, i.e., Generation Resources AND Settlement Only
13
Allow temporary generation
Allow temporary generation until the transmission is built to reliably serve the Large Load. Generation is planned from the beginning to be temporary without having to go through the RMR process
14
Define operational battery registration
Define battery registration for batteries that are only used for meeting operational requirements, e.g., voltage ride-through
15
Develop rules for market-operating operational batteries
Define rules for batteries that are added for operational requirements, and want to participate in the market
16
Develop rules for using an interconnected battery as part of PCLR
17
n/a

## Slide 53: Batch processes: Priority BYOG enhancements (3/4)
Q9: Select the four highest priority BYOG enhancements that you would like ERCOT to work on in the NEAR TERM, # of selections
PUBLIC
Chart: 
 | 3 | 1 | 7 | 4 | 1 | 4 | 2 | 5 | 1 | 3 | 3 | 1 | 1 | 2 | 2 | 2 | 2 | 4
 | 3 | 5 | 4 | 1 | 2 | 2 | 5 | 1 | 1 | 2 | 2 | 8 | 1 | 3 | 1 | 1 | 0 | 2
 | 16 | 10 | 7 | 7 | 9 | 6 | 7 | 8 | 6 | 8 | 6 | 3 | 6 | 4 | 4 | 0 | 0 | 1
 | 2 | 5 | 0 | 5 | 4 | 3 | 1 | 1 | 5 | 0 | 1 | 0 | 3 | 0 | 0 | 0 | 0 | 3
1
1
2
1
2
1
2
1
1
1
1
2
1
2
1
1
1
2
1
2
1
2
2
1
2
24
21
18
17
16
15
15
15
2
13
12
12
11
13
7
3
2
10
9
1. Defined as Independent Generators (n=13) and Developers (n=20)
Chart: 
 | 2 | 2 | 1 | 1 | 3 | 1 | 4 | 1 | 2 | 5 | 1 | 2 | 2 | 2 | 2 | 1 | 1 | 6
 | 1 | 3 | 1 | 1 | 2 | 2 | 2 | 3 | 1 | 1 | 3 | 0 | 3 | 0 | 0 | 1 | 1 | 3
 | 8 | 11 | 6 | 4 | 4 | 6 | 8 | 5 | 4 | 8 | 10 | 7 | 8 | 2 | 3 | 5 | 1 | 4
 | 2 | 2 | 0 | 3 | 1 | 3 | 1 | 1 | 2 | 3 | 2 | 3 | 1 | 0 | 1 | 1 | 0 | 5
1
(6) Large load self-supply outside of Batch
2
2
(9) BYOG at different location
1
1
(2) WLPUN exit plan
1
1
(15) Define operational battery registration
1
2
(17) Develop rules for using an interconnected battery as part of PCLR
2
1
(14) Allow temporary generation
1
2
(5) WLPUN Dynamic Limits
1
1
(4) WLPUN on-ramp for existing Large Load
2
1
2
(16) Develop rules for market-operating operational batteries
1
(8) Large load island transition to grid-connected
2
1
(3) WLPUN generation additions
2
(12) Allow Multiple POIs and/or Customer-owned Substations
1
2
(11) Pursue BYOG option of Netted Network
2
2
(1) WLPUN opt-out option during Commitment
1
2
(10) Define and allow Self-Limiting Facility (SLF) Private Use Networks (PUN)
1
1
1
(13) Allow mix of resources at PUN
1
1
1
(7) WLPUN with Settlement Only Generation
No opinion
2
18
8
9
10
12
15
10
9
13
16
12
14
4
6
8
3
18
17
Others
Generators1
ILLE
TSP
Q10: Select the four highest priority BYOG enhancements that you would like ERCOT to work on in the LONGER TERM, # of selections
Source: CTP TSP survey, fielded 09/15–09/21 (n = 74 respondents; 3 blank responses).
Survey identified clear differences between near-term and long-term enhancement priorities
Near-term: large load self-supply, BYOG at different locations, WLPUN exit plan, define operational battery registration
Long-term: BYOG at different locations, large load island transition to grid-connected, WLPUN generation additions, WLPUN dynamic limits

## Slide 54: Batch processes: Priority BYOG enhancements (4/4)
Category
Enhancement
WLPUN registration and lifecycle
WLPUN opt-out option during Commitment
1
WLPUN exit plan
2
WLPUN generation additions
3
WLPUN on-ramp for existing Large Load
4
WLPUN enhancements
WLPUN Dynamic Limits
5
Large load self-supply outside of Batch
6
WLPUN with Settlement Only Generation
7
Alternative BYOG enhancements
Large Load island transition to grid-connected
8
BYOG at different location
9
Define and allow Self-Limiting Facility (SLF) Private Use Networks (PUN)
10
Pursue BYOG option of Netted Network
11
Allow Multiple POIs and/or Customer-owned Substations
12
Allow mix of resources at PUN
13
Allow temporary generation
14
Battery enhancements
Define operational battery registration
15
Develop rules for market-operating operational batteries
16
Develop rules for using an interconnected battery as part of PCLR
17
Top 4 short-term priority
Top 4 long-term priority

## Slide 55: Modeling and case building: Key takeaways from the survey
Topic
Case building consolidation
Case building frequency
Short circuit consolidation
Case set
Takeaways
Most survey respondents (71%) and all TSPs (100%) support the consolidation of the SSWG and RTP case building processes
45% of TSPs agree an annual CTP case re-build is sufficient, while 36% disagree
TSPs are broadly supportive of combining the short circuit and steady state case building processes (58%), but are divided on whether those cases should match steady state cases
Respondents have suggested expanding the ‘core case set’ to include winter peak cases (9 respondents), as well as no solar cases (6 respondents)
Raw case materials
64% of respondents support (strongly agree or agree) the publishing of raw network case files to allow entities to self-serve and build cases as needed. Respondents are split whether this should be a near-term priority
Preliminary

## Slide 56: Modeling and case building: Case building processes
# of respondents
PUBLIC
Q24: ERCOT will create a CTP case with updated topology, generator, and load forecasts at least annually. Would an annual CTP case re-build be sufficient? % of respondents
Q18: Should ERCOT consolidate the SSWG and RTP processes into a single case-building process? % of respondents
Chart: 
 | 100 | 71.4286 | 50 | 70.9091
 | 3.5714 | 18.75 | 7.2727
 | 25 | 31.25 | 21.8182
TSP
ILLE
Others
Total
Yes, full consolidation case-building process
No, maintain separate case-building processes
No opinion
11
28
16
55
xx
Chart: 
 | 45.4545 | 41.3793 | 46.6667 | 43.6364
 | 36.3636 | 31.0345 | 20 | 29.0909
 | 18.1818 | 27.5862 | 33.3333 | 27.2727
TSP
ILLE
Others
Total
Source: CTP TSP survey, fielded 09/15–09/21 (n = 74 respondents; 19 blank responses).
Yes
No
No opinion
11
29
15
55
All TSPs (100%) support the consolidation of the SSWG and RTP case building processes
TSPs are split on whether an annual CTP case re-build is sufficient, with 45% agreeing and 36% disagreeing

## Slide 57: Modeling and case building: Short circuit cases
# of respondents
PUBLIC
Q23: Should ERCOT produce short circuit cases that match the core set of cases listed in Q19? % of respondents
Q22: Should ERCOT consolidate short circuit case building into the steady state case building processes? % of respondents
Chart: 
 | 58.3333 | 46.4286 | 33.3333 | 45.4545
 | 33.3333 | 3.5714 | 20 | 14.5455
 | 8.3333 | 50 | 46.6667 | 40
TSP
ILLE
Others
Total
Yes, full consolidation
No, maintain separate case-building processes
No opinion
12
28
15
55
xx
Chart: 
 | 33.3333 | 35.7143 | 33.3333 | 34.5455
 | 33.3333 | 10.7143 | 6.6667 | 14.5455
 | 33.3333 | 53.5714 | 60 | 50.9091
TSP
ILLE
Others
Total
Source: CTP TSP survey, fielded 09/15–09/21 (n = 74 respondents; 19 blank responses).
Yes
No
No opinion
12
28
15
55
Most TSPs support combining the short circuit and steady state case building processes (58%), but are evenly split on whether short circuit cases should match core steady state cases

## Slide 58: Modeling and case building: Case set
PUBLIC
Source: CTP TSP survey, fielded 09/15–09/21 (n = 74 respondents; 41 blank responses).
Details
Requested addition (number of responses)
  Winter peak case (9)
  Add winter peak case in response to reliability issues caused by Winter Storm Uri (2021) and Elliott (2022)
  No additions (8)
  Reassess case needs during scoping
  Refine or expand no solar case (6)
  Add no solar related to specific hours (e.g., HE7/8, HE20/21), cold-weather no solar, more no solar case coverage across years
  Expand summer peak coverage (3)
  Add Y4 summer peak so that a case is produced every summer peak
  Add fall / off-peak cases (6)
  Include Y5/Y6 fall peak and a Y5 off-peak case tied to long-term maintenance/N-1-1 planning
Q19: If ERCOT produces the following cases, are there additional essential cases that you would need for planning purposes? If so, why?
8 cases: Y2 summer peak; Y2 no solar; Y3 high renewable minimum load; Y3 regular minimum load; Y3 summer peak; Y5 summer peak; Y5 no solar; Y6 summer peak

## Slide 59: Modeling and case building: Case set
Q21: For cases that are not listed [in Q19], do you agree with ERCOT publishing a minimal core set (e.g., cases listed in Q19) plus raw network-data packages (unsolved cases), so entities can self-serve and build additional cases as needed? % of respondents selecting
PUBLIC
Source: CTP TSP survey, fielded 09/15–09/21 (n = 74 respondents; 18 blank responses).
Chart: 
 | 25 | 20.6897 | 26.6667 | 23.2143
 | 50 | 31.0345 | 53.3333 | 41.0714
 | 8.3333 | 20.6897 | 0 | 10.7143
 | 16.6667 | 3.4483 | 6.6667 | 5.3571
 | 3.4483 | 0 | 1.7857
 | 20.6897 | 13.3333 | 17.8571
TSP
3%
3%
ILLE
Others
2%
Total
Strongly agree
Agree
Neutral
Disagree
Strongly disagree
No opinion
12
29
15
56
# of respondents
xx
Q21a: Would you consider this to be a…? % of respondents
Chart: 
 | 41.6667 | 65.2174 | 46.1538 | 54.1667
 | 58.3333 | 34.7826 | 53.8462 | 45.8333
TSP
ILLE
Others
Total
Near-term issue to be resolved imminently
Longer-term issue to be resolved eventually
12
23
13
48
Source: CTP TSP survey, fielded 09/15–09/21 (n = 74 respondents; 26 blank responses).
64% of respondents support (strongly agree or agree) the publishing of raw network case files to allow entities to self-serve and build cases as needed

## Slide 60: Modeling and case building: Large load modeling
PUBLIC
Source: CTP TSP survey, fielded 09/15–09/21 (n = 74 respondents; 27 blank responses).
Q20a: Would you consider this to be a…? % of respondents
Chart: 
 | 66.6667 | 66.6667 | 63.6364 | 65.9574
 | 33.3333 | 33.3333 | 36.3636 | 34.0426
TSP
ILLE
Others
Total
Near-term issue to be resolved imminently
Longer-term issue to be resolved eventually
12
30
16
58
Source: CTP TSP survey, fielded 09/15–09/21 (n = 74 respondents; 16 blank responses).
Q20: Should ERCOT transition to leading large load modeling into the network operations model (similar to GINR process) to ensure consistent applications of assumptions? % of selections
12
24
11
47
# of respondents
xx
Chart: 
 | 16.6667 | 16.6667 | 31.25 | 20.6897
 | 33.3333 | 43.3333 | 37.5 | 39.6552
 | 25 | 10 | 6.25 | 12.069
 | 8.3333 | 0 | 6.25 | 3.4483
 | 16.6667 | 3.3333 | 0 | 5.1724
 | 26.6667 | 18.75 | 18.9655
TSP
3%
0%
ILLE
Others
3%
Total
Strongly agree
Agree
Neutral
Disagree
Strongly disagree
No opinion
Most respondents (61%) support (strongly agree or agree) ERCOT leading the large load modeling into the network operations model

## Slide 61: Medium loads: Thresholds and boundaries
PUBLIC
Q13A: What should be the minimum threshold for a large load? % of respondents
Q13B: What should be the minimum threshold for a medium load? % of respondents
Chart: 
 | 14.2857 | 7.4074 | 23.5294 | 13.7931
 | 85.7143 | 37.037 | 23.5294 | 44.8276
 | 29.6296 | 29.4118 | 22.4138
 | 25.9259 | 23.5294 | 18.9655
TSP
ILLE
Others
Total
10 MW
25 MW
50 MW
No opinion
14
27
17
58
Source: CTP TSP survey, fielded 09/15–09/21 (n = 74 respondents; 16 blank responses).
Chart: 
 | 53.3333 | 14.8148 | 15.7895 | 24.5902
 | 46.6667 | 40.7407 | 57.8947 | 47.541
 | 25.9259 | 21.0526 | 18.0328
 | 18.5185 | 5.2632 | 9.8361
TSP
ILLE
Others
Total
Source: CTP TSP survey, fielded 09/15–09/21 (n = 74 respondents; 13 blank responses).
50 MW
75 MW
100 MW
No opinion
15
27
19
61
# of respondents
xx
Majority of respondents (73%) support a minimum large load threshold of 50 or 75 MW, and majority (53%) of TSPs want 50 MW Majority of respondents (59%) and 100% of TSPs support a minimum medium-load threshold of 25MW or less

## Slide 62: Medium loads: Inclusion criteria
93%
39%
50%
87%
39%
47%
67%
44%
43%
67%
33%
20%
60%
28%
20%
Q14: To standardize the process in the future, what evidence, disclosures, and/or securities should medium loads provide to TSPs to be eligible for inclusion in CTP? # of selections
XX
% of respondent type selecting
PUBLIC
Chart: 
 | 7 | 7 | 8 | 6 | 5 | 5
 | 15 | 14 | 13 | 6 | 6 | 7
 | 14 | 13 | 10 | 10 | 9 | 8
Energization schedule
Site control evidence
Study fee
Disclosure of substantially similar interconnection requests
Evidence of financial security on a dollar MW basis
Disclosure of backup generating facilities
36
34
31
22
20
20
53%
28%
23%
Source: CTP TSP survey, fielded 09/15–09/21 (n = 74 respondents; 18 blank responses).
Q14a: Would you consider this to be a…? % of respondents
Chart: 
 | 80 | 59.2593 | 42.8571 | 60.7143
 | 20 | 40.7407 | 57.1429 | 39.2857
TSP
ILLE
Others
Total
Near-term issue to be resolved imminently
Longer-term issue to be resolved eventually
15
27
14
56
Source: CTP TSP survey, fielded 09/15–09/21 (n = 74 respondents; 11 blank responses).
TSPs
ILLEs
Others
TSPs strongly support (>87%) medium loads providing energization schedules and site control evidence for inclusion in CTP; 80% of TSPs view this as a near-term issue to be resolved immediately

## Slide 63: Medium loads: Medium load information collection
PUBLIC
Source: CTP TSP survey, fielded 09/15–09/21 (n = 74 respondents; 20 blank responses).
Q15a: Would you consider this to be a…? % of respondents
Chart: 
 | 80 | 62.5 | 40 | 61.1111
 | 20 | 37.5 | 60 | 38.8889
TSP
ILLE
Others
Total
Near-term issue to be resolved imminently
Longer-term issue to be resolved eventually
15
28
17
60
Source: CTP TSP survey, fielded 09/15–09/21 (n = 74 respondents; 14 blank responses).
Chart: 
 | 33.3333 | 42.8571 | 42.8571 | 41.8182
 | 50 | 28.5714 | 23.8095 | 29.0909
 | 16.6667 | 10.7143 | 4.7619 | 7.2727
 | 3.5714 | 19.0476 | 10.9091
 | 14.2857 | 9.5238 | 10.9091
TSP
ILLE
Others
Total
Medium load portal (similar to large load portal)
Included by TSPs during case-building process
Periodic RFIs
Planning model change request
No opinion
Q15: How should information about medium loads be collected? % of selections
15
24
15
54
# of respondents
xx
Slight preference (42%) among all respondents for a medium load portal to collect information on medium loads; 50% of TSPs would prefer to collect during the case-building process

## Slide 64: Future Batch processes and Reliability studies: Key takeaways from the survey
Topic
Tier 3 and 4 expansion
Project tiering
Planner-to-planner sessions
Insight
Project alternative testing
Most respondents (61%) support (strongly agree or agree) the introduction of a project alternative testing process within CTP
Most respondents (55%) and TSPs (84%) support the expansion of Tier 3 and Tier 4 to include more in-kind, aging infrastructure and storm-hardening projects
Most respondents (71%) support revisiting project tiering, supporting the inclusion of regional impact in addition to cost as a tiering criterion
TSPs (100%) are fully supportive of establishing planner-to-planner sessions to review preliminary transmission solutions
TSP-ERCOT collaboration model
Most TSPs (58%) would like 60 days to identify preliminary solutions. TSPs also prefer recurring meetings to review solutions (59%)
Future Batch scope
Most survey participants support fewer Batch study years with a faster Batch process (65%)

## Slide 65: Future Batch processes: Planning guide vs scoping document
# of respondents
PUBLIC
Q11: Should study requirements (study years) be prescribed in the Planning Guide, or be provided by ERCOT in the scoping document based on future risks and system attributes at the time of study? % of respondents
Chart: 
 | 40 | 50 | 46.6667 | 46.5517
 | 53.3333 | 32.1429 | 33.3333 | 37.931
 | 6.6667 | 17.8571 | 20 | 15.5172
TSP
ILLE
Others
Total
Prescribed in Planning Guide
Provided in scoping document
No opinion
15
28
15
58
Source: CTP TSP survey, fielded 09/15–09/21 (n = 74 respondents; 16 blank responses).
xx
Slight majority of TSPs (53%) prefer study requirements to be prescribed in scoping documents
Overall, however, more respondents prefer study requirements to be prescribed in the Planning Guide (47%)

## Slide 66: Future Batch processes: Cadence for future Batch studies
# of respondents
PUBLIC
xx
Chart: 
 | 26.6667 | 17.8571 | 14.2857 | 19.2982
 | 66.6667 | 60.7143 | 71.4286 | 64.9123
 | 6.6667 | 21.4286 | 14.2857 | 15.7895
TSP
ILLE
Others
Total
Source: CTP TSP survey, fielded 09/15–09/21 (n = 74 respondents; 14 blank responses).
Y2, Y3, Y4, Y5, and Y6 – more studies, slower batch process
Y2, Y5, Y6 – fewer studies, faster batch process
No opinion
15
29
16
60
Majority of respondents (65%) favor speed: a “fewer studies, faster Batch process” approach
Q12: Which years should ERCOT study (i.e., identify transmission projects) in Batch study? As a point of reference, Batch Zero studies Y2, Y4, and Y6 (three years). End-to-end time to execute the Batch study (and the overall CTP process) will take longer if more years are studied, % of respondents

## Slide 67: Future Batch processes: Interconnection request process exceptions
Q16a: Would you consider this to be a…? % of respondents
Chart: 
 | 75 | 62.5 | 50 | 62
 | 25 | 37.5 | 50 | 38
TSP
ILLE
Others
Total
Near-term issue to be resolved imminently
Longer-term issue to be resolved eventually
12
24
14
50
Source: CTP TSP survey, fielded 09/15–09/21 (n = 74 respondents; 24 blank responses).
Load type
Details
No/minimal transmission impact loads
Co-located w/ generation and no transmission or generation upgrades needed
Critical infrastructure & emergency
Hospitals, water/wastewater treatment, public-good facilities
Industrial/manufacturing projects
Projects with different development profiles compared to computational loads
Small/medium loads below threshold
Small and medium load projects can be handled via DSP or existing FAC-002-4 studies
In-flight legacy loads
Projects that already have study results, executed FEA, regulatory approvals, or under construction.
Policy-driven/state-designated exceptions
Good Cause exceptions for job creation, economic development
Q16: What type of load interconnection requests (if any) merit an exception to be processed outside of the CTP cycle? (free response)
PUBLIC
  Opposition and governance
  Narrow exceptions: Some respondents remarked that exceptions need to be narrow and follow published criteria
  Opposition: A minority of respondents opposed any exceptions, suggesting that all medium and large loads should go through the CTP process

## Slide 68: Reliability studies: Project alternative testing
Q25: Because projects associated with reliability and large loads will be processed through the CTP, ERCOT is considering escalating some projects for project alternative testing and public comment (as RPG does today). This process would run in parallel with CTP. In your view, would this be an acceptable way to test reliability and large load projects? % of respondents
Q26: What projects, other than projects associated with reliability and large loads, should be included in the project alternative testing process described above? (number of responses)
PUBLIC
Chart: 
 | 33.3333 | 11.1111 | 26.6667 | 20.3704
 | 33.3333 | 44.4444 | 40 | 40.7407
 | 16.6667 | 18.5185 | 13.3333 | 16.6667
 | 16.6667 | 7.4074 | 6.6667 | 5.5556
 | 7.4074 | 13.3333 | 3.7037
 | 11.1111 | 12.963
TSP
ILLE
Others
4%
Total
Strongly agree
Agree
Neutral
Disagree
Strongly disagree
No opinion
Source: CTP TSP survey, fielded 09/15–09/21 (n = 74 respondents; 20 blank responses)
# of respondents
xx
12
27
15
54
  Economic / economically-driven transmission projects (9)
  Major ROW acquisition, new high-voltage/voltage-class corridors, or material regional/interregional impact (3)
  Gen-tie lines / GTC exit-plan projects (2)
  No additions - current scope (reliability + large load) is sufficient (2)
  One-off suggestions (11)
61% of respondents support (strongly agree or agree) the introduction of project alternative testing process within CTP

## Slide 69: Reliability studies: Tier 3 and 4 criteria
Q27: Would you agree with expanding tier 3 and 4 criteria to include more in-kind, aging infrastructure, and storm-hardening projects? (e.g., by changing cost thresholds), % of respondents
PUBLIC
Chart: 
 | 66.6667 | 7.1429 | 23.0769 | 24.5283
 | 16.6667 | 42.8571 | 15.3846 | 30.1887
 | 8.3333 | 17.8571 | 23.0769 | 16.9811
 | 8.3333 | 32.1429 | 38.4615 | 0
 | 0
 | 28.3019
TSP
ILLE
Others
Total
Strongly agree
Agree
Neutral
Disagree
Strongly disagree
No opinion
# of respondents
xx
12
28
13
53
Source: CTP TSP survey, fielded 09/15–09/21 (n = 74 respondents; 21 blank responses)
Q27a: Would you consider this to be a…? % of respondents
Chart: 
 | 54.5455 | 28.5714 | 44.4444 | 39.0244
 | 45.4545 | 71.4286 | 55.5556 | 60.9756
TSP
ILLE
Others
Total
Near-term issue to be resolved imminently
Longer-term issue to be resolved eventually
11
21
9
41
Source: CTP TSP survey, fielded 09/15–09/21 (n = 74 respondents; 33 blank responses)
Most respondents (55%) and TSPs (84%) support the expansion of Tier 3 and Tier 4 to include more in-kind, aging infrastructure and storm-hardening projects

## Slide 70: Reliability studies: Legacy RPG and local projects
PUBLIC
Source: CTP TSP survey, fielded 09/15–09/21 (n = 74 respondents; 51 blank responses, 8 non-answers / No opinion).
Q28: What other projects, if any, should be considered through the legacy RPG process?
  Economic-driven projects (6)
Details
Requested addition (number of responses)
  Projects not yet captured by CTP cases, or already materially advanced under the existing process
  Non-large-load / lower-impact / tier-based projects (4)
  Tier 2/3/4 projects, TSP planning-criteria violations, projects that don't materially affect CTP assumptions
  Reliability projects independent of load interconnection (3)
  Aging infrastructure, substation upgrades below the CTP cost threshold, local reliability studies
  Policy/job-creation/public-support driven projects (1)
  Projects driven by public benefit, such as domestic manufacturing and projects reducing foreign import reliance
  None - transition everything to CTP (1)
  Sole dissent from keeping anything in legacy RPG
Q29: Should more local projects (i.e., projects entirely within one TSP’s jurisdiction) be studied as Tier 3 and 4 projects? If so, how would you want to modify the tiering criteria?
  Yes - expand Tier 3/4 to more local projects (8)
Details
Position (number of responses)
  Proposed criteria: voltage level (e.g., 345 kV or below), no new ROW needed, no impact on neighboring systems, revisit cost thresholds for today's equipment/labor costs
  Conditional yes - but gate on impact, not jurisdiction (4)
  Local status alone shouldn't qualify a project. Projects cannot have material impact on adjacent TSP systems or regional reliability
  No - jurisdiction doesn't determine impact (7)
  Projects entirely within one TSP's footprint can still change regional power flows, transfer capability, or ratepayer costs
Source: CTP TSP survey, fielded 09/15–09/21 (n = 74 respondents; 50 blank responses, 5 non-answers / No opinion).

## Slide 71: Reliability studies: Project tiering
PUBLIC
Q30: As part of the introduction of CTP, do you believe that ERCOT should revisit the project tiering framework? % of respondents
Chart: 
 | 80 | 68 | 70 | 71.1111
 | 20 | 32 | 30 | 28.8889
TSP
ILLE
Others
Total
Yes
No
# of respondents
xx
10
25
10
45
Source: CTP TSP survey, fielded 09/15–09/21 (n = 74 respondents; 37 blank responses)
If so, on what basis should project tiers be defined? % of respondents
Q30a: Would you consider this to be a…? % of respondents
Chart: 
 | 66.6667 | 66.6667 | 63.6364 | 65.9574
 | 33.3333 | 33.3333 | 36.3636 | 34.0426
TSP
ILLE
Others
Total
Near-term issue to be resolved imminently
Longer-term issue to be resolved eventually
12
24
11
47
Source: CTP TSP survey, fielded 09/15–09/21 (n = 74 respondents; 29 blank responses)
Chart: 
 | 22.2222 | 30 | 25 | 27.027
 | 44.4444 | 15 | 25 | 24.3243
 | 33.3333 | 5 | 12.5 | 5.4054
 | 15 | 12.5 | 10.8108
 | 35 | 25 | 32.4324
TSP
ILLE
Others
Total
Regional versus interregional system impact
Cost thresholds only and new ROW, as today
No changes
Voltage level
No opinion
9
20
8
37
Source: CTP TSP survey, fielded 09/15–09/21 (n = 74 respondents; 29 blank responses)
Most respondents (71%) support revisiting project tiering, supporting the inclusion of regional impact in addition to cost as a tiering criterion

## Slide 72: Reliability studies: TSP engagement (1/3)
Q31: Would there be value to establishing planner-to-planner (ERCOT and TSP) sessions to review preliminary solutions on an ongoing basis? % of respondents
PUBLIC
Chart: 
 | 100 | 71.4286 | 50 | 72.2222
 | 7.1429 | 21.4286 | 9.2593
 | 21.4286 | 28.5714 | 18.5185
TSP
ILLE
Others
Total
12
28
14
54
Source: CTP TSP survey, fielded 09/15–09/21 (n = 74 respondents; 20 blank responses)
Yes, establish planner-to-planner sessions
No, please explain
No opinion
# of respondents
xx
TSPs (100%) are fully supportive of establishing planner-to-planner sessions to review preliminary transmission solutions

## Slide 73: Reliability studies: TSP engagement (2/3)
XX
# of respondents
PUBLIC
Source: CTP TSP survey, fielded 09/15–09/21 (n = 74 respondents; 14 blank responses).
Q17: How much time should TSPs be given to identify preliminary steady state solutions and complete a feasibility review (excluding cost estimates) for preliminary solutions during the Batch study? % of respondents
Chart: 
 | 14.2857 | 50 | 62.5 | 45
 | 35.7143 | 26.6667 | 6.25 | 23.3333
 | 42.8571 | 10 | 6.25 | 16.6667
 | 7.1429 | 13.3333 | 25 | 15
TSP
ILLE
Others
Total
30 days
45 days
60 days
No opinion
14
30
16
60
79% of TSPs believe they should have >45 days to identify preliminary steady state solutions and complete feasibility reviews; >50% of non-TSP respondents believe TSPs should have 30 days

## Slide 74: Reliability studies: TSP engagement (3/3)
Q32: How much time should TSPs be given to identify preliminary solutions and complete a feasibility review for preliminary solutions during the Reliability study? % of respondents
Q33: How should TSP feedback be structured during the Reliability study to finalize solutions? % of respondents
PUBLIC
Chart: 
 | 16.6667 | 50 | 50 | 42.3077
 | 16.6667 | 28.5714 | 16.6667 | 23.0769
 | 58.3333 | 7.1429 | 8.3333 | 19.2308
 | 8.3333 | 14.2857 | 25 | 15.3846
TSP
ILLE
Others
Total
35 days
45 days
60 days
No opinion
Source: CTP TSP survey, fielded 09/15–09/21 (n = 74 respondents; 22 blank responses)
12
28
12
52
Chart: 
 | 16.6667 | 8 | 21.4286 | 13.7255
 | 41.6667 | 32 | 21.4286 | 31.3725
 | 33.3333 | 8 | 21.4286 | 5.8824
 | 8.3333 | 20 | 7.1429 | 3.9216
 | 32 | 28.5714 | 19.6078
 | 25.4902
TSP
ILLE
Others
4%
Total
Recurring 1wk windows
Recurring 2wk windows
Recurring 4wk windows
Continuous / rolling
Milestone-based
No opinion
Source: CTP TSP survey, fielded 09/15–09/21 (n = 74 respondents; 23 blank responses)
12
25
14
51
# of respondents
xx
Most TSPs (58%) would like 60 days to identify preliminary solutions. TSPs also prefer recurring meetings to review solutions (59%)