# ERCOT Operations Bulletin 143

ERCOT has revised the Frequency Control Desk section of the Operating Procedure Manual.

Changes include updating Section 2.6.3 step1, adding a third bullet to Step F.

| 2.6.3 Issue an Operating Condition Notice (OCN) |
| --- |
| Step # | Procedural Steps |
| NOTE: | General guidelines: Knowledge of an emerging/existing situation that could/does require intervention to ensure system reliability requires ERCOT to notify Market Participants through the use of Emergency Notification Messaging System. |
| 1 | ISSUE an Operating Condition Notice per applicable text in Appendix 5 IF: There is a hurricane in the Gulf with >20% chance of landfall in Texas. A cold front is approaching with temperatures anticipated to be in mid to low 20o F range and maximum temperature expected to remain near or below freezing impacting 50% or more of major metropolitan areas. There is the potential for icing conditions to affect major transmission systems. Hot weather expected to result in either capacity shortages or transmission security criteria violations. Projected fuel limitations or emission limitations expected to lead to insecure operation. A situation is emerging that has the reasonable expectation of leading ERCOT into an insecure state; including: Forced outages which may lead to operating in an insecure state Expectation of operating in a single contingency insecure state for an established list of contingencies Insufficient Balancing Energy available to clear the next hour Balancing Energy requirement as shown on the MAI (if the load forecast is reasonable) |

A copy of the procedure, Frequency Control Desk V3R20, is available at http://www.ercot.com/AboutERCOT/PublicDisclosure/ERCOTProcedures.htm.