# Power Operations Bulletin #90

ERCOT has revised the Transmission & Security Desk section of the Operating Procedure Manual.

Changes include inserting new section 2.5.5 Notification of Condition Termination.

| 2.5.5 Notification of Condition Termination |
| --- |
| Step # | Procedural Steps |
| NOTE | If a condition increases in severity, then the posting of the corresponding Alert, Advisory, or Emergency Notice will constitute cancellation of the previous notification. |
| 1 | When the situation requiring the notification is relieved, NOTIFY Market Participants and Transmission Operators that the condition has been terminated. OCNs do not require “termination” notification. USE the Emergency Notification System AND ISSUE Termination Notice. (Short version – 32 characters) POST the long version of the Termination Notice on the Market Information System (MIS). Initiate a hotline call to all Transmission Operators and QSEs (or see that another operator does so). Make a printout of the hotline log and save it in the daily log file. |

A copy of the procedure, Transmission & Security Desk V2R23, is attached.

# Text boxes

CN  #124      5/18/2004

JEB         	 DP