# ERCOT Operations Bulletin 180

ERCOT has revised the Transmission & Security Desk section of the Operating Procedure Manual.

Changes include incorporating new section 2.1.2 “OOME – VDI Guidelines.”

| OOME – VDI Guidelines |
| --- |
| Step # | Procedural Steps |
| NOTE: | The order of steps in this procedure is a recommendation. The system operator will determine the sequence of steps, or any additional actions necessary to ensure system security. |
| 1 | If an OOME Dispatch instruction will result in the unit being dispatched off-line (i.e., less than the minimum operating limit for that resource), then: The duration of the OOME Dispatch instruction should end at the next scheduled off-line time according to the Resource Plan, OR the end of the operating day, whichever is shortest. If the QSE representing the resource expresses a need for that resource to be returned on-line, and there is no negative impact on system reliability, then issue a VDI to the QSE to disregard the OOME instruction for the appropriate intervals. |
| 2 | When system conditions require one CT of a Combined Cycle Plant to be OOMEd off line, use the following steps: Contact the QSE and determine which CT should receive the OOME Obtain from the QSE the MW output impact the CT’s OOME will have on the steam unit. OOME the required CT off line Send an OOME equal to the amount the steam unit will produce when the CT is shut down. The intervals for both OOMEs should be the same. |
| 3 | When issuing a unit specific dispatch instruction (s) to a plant to change the output, but where all units will remain on line: Determine what the net plant output should be. Determine the unit (s) and MW amount per unit to be dispatched. Send the dispatch instruction. |
| 4 | When a Dispatch Instruction prevents a QSE from performing their Ancillary Service obligation, the system operator may chose to exercise one of the two following options: Upon a QSE’s request, issue a VDI to relieve the QSE from their Ancillary obligation. Should system conditions warrant, a second market may be necessary to procure additional Ancillary Services. Inform the Shift Supervisor that it may be necessary to open a second market. Release the QSE from the dispatch instruction so they can come back into compliance. In this case, an element may exceed first contingency criteria. |
| 5 | If a VDI is issued to a QSE to relieve them from their Ancillary Service obligation, fax a copy of the VDI to ERCOT Compliance at 225-7165. |
| 6 | If a first contingency criterion is being exceeded, ISSUE a Transmission Alert and REQUEST the Operations Support Engineers develop a Mitigation Plan. |

A copy of the updated procedure, Transmission & Security Desk V3R46, is available at http://www.ercot.com/AboutERCOT/PublicDisclosure/ERCOTProcedures.htm.