# Power Operations Bulletin #94

ERCOT has revised the Shift Supervisor Desk section of the Operating Procedure Manual.

Changes include adding new section 2.1.10 “Monitoring Market Clearing Prices.”

V2R8 – CN#133

| Monitoring Market Clearing Prices |
| --- |
| Step # | Procedural Steps |
| 1 | Using the MOI, keep the “Zone” or the “Constraint” tab, which is on the Real-Time Balancing Market page, available to view at all times. IF a constraint becomes “ACTIVE”, verify that the Transmission & Security Desk Operator is monitoring it and that it is not being over constrained. IF the Zonal pricing shows to be abnormally high or low, check market conditions for that interval to insure that there is a sufficient amount of Balancing Energy, AND that the Balancing Offset is reasonable. |