# ERCOT Operations Bulletin 206

ERCOT has revised the Transmission & Security Desk section of the Operating Procedure Manual.

Changes include the following changes:

Updated section 2.1.4 “OOME – VDI Guidelines” added new step 5

| 2.1.4 OOME – VDI Guidelines |
| --- |
| Step # | Procedural Steps |
| 5 | When a TO informs ERCOT of an SPS activation and the SPS activation de-rates a resource or takes a resource off line, issue a VDI to the affected QSE. Immediately after the unit is derated, record the generation level on the VDI form. Only list the beginning of the interval, the ending interval is not necessary. If the resource is a DC tie, include the name and zone of the tie. |

A copy of the updated procedure, Transmission & Security Desk V3R54, is available at

http://www.ercot.com/AboutERCOT/PublicDisclosure/ERCOTProcedures.htm.