# ERCOT Operations Bulletin 213

ERCOT has revised the Frequency Control Desk section of the Operating Procedure Manual.

Changes include

V3R31		Update section 2.1.2, 2.1.5, 2.5.3, and Appendix 4

Adding new section 2.1.3 and 2.1.4

| 2.1.2 Verbal Dispatch Instructions (VDI) |
| --- |
| Step # | Procedural Steps |
| PURPOSE: | ISSUE a VDI to QSE(s) specifying changes to generation. |
| NOTE: | VDIs should not re-iterate an instruction given via XML. |
| 1 | Communicate required information to QSE(s) via telephone (using the hotline if appropriate). |
| 2 | As time permits, complete the VDI form (Appendix 3). The following are required fields on all VDIs: VDI # EXAMPLE: For the 4th VDI issued by the Frequency Control Desk on July 22, 2005 the number would appear as “F-072205-4” Operating Day ERCOT System Operator Receiving Entity Receiving Entity’s Operator Time & Date Instruction Reason for Instructions Intervals ERCOT Operator’s signature Blank fields are to have N/A entered. |
| 3 | As time permits, forward the VDI form to the Shift Supervisor. |
| 4 | LOG in the Operator’s Log the VDI information and information relevant to the decision for issuing the VDI. |

| 2.1.5 Replacing Responsive Reserve through a Bilateral Trade |
| --- |
| Step # | Procedural Steps |
| NOTE: | When a resource (either LAAR or generation) that is supplying RRS becomes unavailable to a QSE (QSE A) and needs to be replaced through a Bilateral Trade with another QSE (QSE B), then QSE A is expected to inform ERCOT. |
| 1 | Obtain the following information from QSE A: Intervals affected Name of QSE with whom the bilateral trade was made |
| 2 | IF the resource that became unavailable was a LAAR, then ENSURE QSE B maintains an amount of Responsive Reserve Service equal to their own obligations PLUS the amount of the bilateral agreement with QSE A for the affected intervals. |
| 3 | LOG in the Operator’s Log the conversation, including the information provided. |
| 4 | Email the information RRS@Ercot.com. |

| 2.5.3 Actions When Frequency Telemetry is Incorrect |
| --- |
| PURPOSE: | To prevent the unnecessary deployment of Responsive Reserve due to incorrect telemetry frequency data. |
| 1 | IF frequency is BELIEVED to be incorrect VERIFY that the frequency is correct by comparing the data from multiple sources. Go to the “Generation Area Status” display, and click on the “i” to the left of “Current Frequency” to view “OPA Measurement” window. |
| 2 | In “OPA Measurement” window, under “Status” column, check “Prime” on a valid frequency source. |
| 3 | LOG in the Operator’s Log any relevant information on this event. |

## Appendix 4:  Telephone Hotline

| QSEs |  |
| --- | --- |
| AEN | FULCRUM |
| AEP Ohio | Garland |
| ANP | LCRA |
| APX Equinix | Merrill Lynch |
| BEPC (Brazos) | MIRANT |
| British Petro | MPower |
| BTU | Reliant RES |
| Calpine | Sempra |
| Constellation | STEC |
| Coral | SUEZ |
| CPSB | Tenaska |
| Dynegy | TXGNQSER (Texas Genco) |
| Exelon | TXU |
| FP&L Juno Beach | XTend |

| TOs |  |
| --- | --- |
| AEN | Denton |
| AEP | Garland |
| BEPC | LCRA |
| BPUB | Magic Valley |
| BTU | Rayburn |
| Centerpoint | STEC |
| College Station | TNMP |
| CPSB | TXU Electric Delivery |

| 2.1.3 VDI for Hold Last Interval |
| --- |
| Step # | Procedural Steps |
| 1 | If market control mechanisms have failed, or ERCOT has issued erroneous instructions THEN, using the hotline, issue an instruction: Typical script: “VDI # ______. Hold the [interval ending time] interval Balancing Energy Service deployment until further notice.” |
| 2 | Print Hotline Log, ensure printout has date and time and forward to Shift Supervisor. |
| 3 | As time permits complete the VDI form (Appendix 3), using these instructions: Issued a Verbal Dispatch Instruction to – write in “All QSEs” Receiving entity’s operator – write in “All QSEs” The instruction was as follows – write in “Hold interval ending <time>, resume with interval <time> ALL fields are to have either pertinent data or N/A entered. Leave NO field(s) blank. |
| 4 | As time permits, forward VDI form to Shift Supervisor. |
| 5 | LOG in the Operator’s Log the VDI information and reason(s) why interval was held. |

| 2.1.4 VDI for RMR Unit Availability Change |
| --- |
| Step # | Procedural Steps |
| PURPOSE: | If an RMR unit availability changes, the QSE is NOT obligated to replace the energy deficiency of that RMR unit. If requested by the QSE a VDI shall be issued for the amount of the MW mismatch and will be valid for the period of time that the QSE cannot update their schedule. |
| 1 | If an RMR unit availability changes AND the QSE requests a VDI: Issue the VDI for the amount of MW mismatch Issue the VDI for the period of time that the QSE cannot update its schedule Have the QSE submit an updated availability plan Have the QSE submit an update schedule |
| 2 | As time permits, complete the VDI form (Appendix 3). |
| 3 | As time permits, forward the VDI form to the Shift Supervisor. |
| 4 | LOG in the Operator’s Log the VDI information and any other pertinent information relating to this event. |

V3R32		Update section 2.1.2 to reflect Release 4 changes – VDI Numbering

| Verbal Dispatch Instructions (VDI) |
| --- |
| Step # | Procedural Steps |
| PURPOSE: | ISSUE a VDI to QSE(s) specifying changes to generation. |
| NOTE: | VDIs should not re-iterate an instruction given via XML. |
| 1 | Communicate required information to QSE(s) via telephone (using the hotline if appropriate). |
| NOTE: | VDI numbers as described here are only required for VDIs documented using the paper form. VDIs documented using the OOM tool (post EMMS Release 4) will not have a number available to the operator. |

A copy of the procedure, Frequency Control Desk V3R32, is available at http://www.ercot.com/AboutERCOT/PublicDisclosure/ERCOTProcedures.htm.