# Power Operations Bulletin #133

ERCOT has revised the Transmission & Security Desk section of the Operating Procedure Manual.

Changes include new step six in section 2.2.3 “Manage Transmission Limits, Constraints, and Congestion.”

| 2.2.3 Manage Transmission Limits, Constraints, and Congestion |
| --- |
| Step # | Procedural Steps |
| 6 | When system conditions require one CT of a Combined Cycle Plant to be OOMEd off line, use the following steps: Contact the QSE and determine which CT should receive the OOME Obtain from the QSE the MW output impact the CT’s OOME will have on the steam unit. OOME the required CT off line Send an OOME equal to the amount the steam unit will produce when the CT is shut down. The intervals for both OOMEs should be the same. |

A copy of the procedure, Transmission & Security Desk V3R32, is available at http://www.ercot.com/AboutERCOT/PublicDisclosure/ERCOTProcedures.htm.