# ERCOT Operations Bulletin 235

ERCOT has revised the Operating Period Desk section of the Operating Procedure Manual.

Changes include adding new section 2.4 “Emergency Operations” and new section 2.4.1 “Emergency Site Failover.”

| Emergency Site Failover |
| --- |
| Step # | Procedural Steps |
| NOTE: | If communication with the primary control center is lost during normal business hours and support is unavailable from the primary control center, personnel at the backup site will serve as support. If communication with the primary control center is lost during non business hours, on-call personnel should be notified. |
|  | The following indicates a loss of communication from the active site: When the EMS (WebFG) fails, this message immediately appears: When the MOI fails, an hour glass and (Not Responding) will appear on the top edge of the window: If the EMS and MOI fail at the same time, it is an indicator a catastrophic failure at the active site. Loss of the primary control center may occur with the EMMS running from the backup site. When this takes place, the loss will not be apparent until such things as no offset number, lack of frequency control and/or congestion management or loss of telecommunication reveal the situation. |
| 1 | If the primary control center becomes inoperative, determine if the EMMS infrastructure is running. A & B indicate the EMMS is running from Taylor C & D indicate the EMMS is running from Austin |
| 2 | If the EMMS is still functioning, continue normal operations and proceed to step 4. |
| 3 | If the EMMS has failed, proceed to step 4. |
| NOTE: | A callout list for system operators and support personnel is maintained in a separate tab in the Operating Procedure Manual. |
| 4 | Callout the following System Operation’s shift personnel: 1 Shift Supervisor 1 Day-Ahead Desk Operator 1 Frequency Control Desk Operator 1 Transmission and Security Desk Operator |
| 5 | Continue calculating the Offset numbers for the restart of the EMMS. This will keep the spreadsheet current and also provide a “starting point” when the EMMS is restored. |
| 6 | Once the Shift Supervisor arrives at the backup site, he/she will coordinate the restoration of the EMMS. |

A copy of the procedure is available at http://www.ercot.com/mktrules/guides/procedures/index.html.