# ERCOT Operations Bulletin 250

ERCOT has revised the Shift Supervisor Desk section of the Operating Procedure Manual.

Changes include updating section 2.2.10 – first Note and step 1; renaming Attachment B to ‘Event Investigation Form – ERCOT Compliance.’

| ERCOT Compliance – Internal Reporting |
| --- |
|  | Procedural Steps |
| NOTE: | There are certain events listed in the Event Investigation Process that requires an e-mail from System Operations to ERCOT Operations Support and Compliance. An initial report from System Operations will trigger the investigation process. The subject line of the e-mail should read “ERCOT Compliance – Internal Reporting.” |
| NOTE: | Events that are deemed to be significant are listed but not limited to the following: EECP Implementation Emergency Notice issued Simultaneous loss of any combination of three generating unit facilities, transmission lines, and autotransformers (138KV and above). Note: Count combined cycle trains as one unit. SPS activation RAP implementation requiring load shedding Under frequency relay operations (or frequency deviations greater than .7Hz from scheduled frequency). Sustained voltage deviations greater than five percent on 345 Kv systems. Alerts for significant transmission elements (345 Kv). Failure of computer systems at ERCOT, the Qualified Scheduling Entity (QSE) or Transmission Operator (TO). Voltage collapse on portions of 138 Kv or 345 Kv system Loss of an ERCOT, QSE, or TO control center. Black Start initiation Uncontrollable loss of 150 MW or more of firm load shed for more than 15 minutes from a single incident. |
| NOTE: | There are also DOE and several NERC reportable events that could trigger an investigation. To report such an event, see section 2.2.11 |
| 1 | When a significant event occurs, within one hour complete the form located in Attachment B “Event Investigation Form – ERCOT Compliance” and email to: James Hinson, Steve Myers, Kent Saathoff, Kent Grammer, John Dumas, Leo Villanueva, Jeff Healy, and ERCOT Compliance Team (1 ERCOT Compliance Team). |

## Attachment B:  Event Investigation Form – ERCOT Compliance

  - Operator

  - Event

Brief Explanation of what occurred:

  - Date/Time  _______________________________________________________

  - Location  ________________________________________________________

  - Contact Information

  - Company _______________________________________________________

  - Person

  - Was this event DOE or NERC Reportable?  Yes   	No

A copy of the procedure is available at http://www.ercot.com/services/comm/mkt_notices/pobs/index.html.