# ERCOT Operations Bulletin 275

ERCOT has revised the Shift Supervisor Desk section of the Operating Procedure Manual.

Changes include incorporating new section 2.2.12 “PUC Daily Report.”

| PUC Daily Report |
| --- |
| Step # | Procedural Steps |
| NOTE: | The PUC reports are to be generated twice per day as outlined below at 1100 and 1500. |
| 1 | Complete the PUCT_Daily Report template at the appropriate times. E-mail the report to the distribution list entitled “PUC-Available Generating Resources.” |
| 2 | Revise the last report and resend it if: The probability of an EECP event increases. Give reason(s) for escalation, OR Conditions change that required new notices to be issued, such as, an OCN or an Alert, OR Local reliability concerns arise which include actual overloads and/or loss of load, especially the Laredo area, OR The Gibbons Creek Bryan East/Green Prairie 138 kV double circuit transmission line trips, or if there are unplanned outages of the generation units in the area. |
| NOTE: | Reporting unexpected generation outages is no longer required. However, be able to provide a list of unplanned generation outages for the day if requested by the PUC. |

A copy of the procedure is available at http://www.ercot.com/mktrules/guides/procedures/index.html.