# ERCOT Operations Bulletin 284

ERCOT has revised the Transmission & Security Desk Procedure.  Revision includes updating section 2.4.4 – first Note and step 1.

| 2.4.4 VSAT |
| --- |
| Step # | Procedural Steps |
| PURPOSE: | To monitor system voltages and to prevent voltage collapse. |
| NOTE: | VSAT should be checked at least every hour, or more frequently as necessary. |
| NOTE: | To contact VSAT support, check the board in the back of TCC for the on-call personnel. |
| 1 | Determine if VSAT has run in the last 80 minutes. Reference Display: Network Online Sequence If VSAT has not run in the last 80 minutes, contact VSAT support. IF a South-Houston or North-Houston CSC/CRE has a forced outage, manually rerun the whole sequence of RTNET, RTCA and RTDCP (VSA) immediately and proceed to step 2. Otherwise, continue with following steps. IF any of the last VSAT results approaches a safety margin, manually rerun the whole sequence of RTNET, RTCA and RTDCP (VSA) within one hour and proceed to step 2. Otherwise, continue with following steps. |

A copy of the procedure is available at http://www.ercot.com/mktrules/guides/procedures/index.html.