ERCOT Operations Bulletin 321

ERCOT has revised the Shift Supervisor Desk section of the Operating Procedure Manual.

This change updates sections 2.2.8 and 3.2

A copy of the procedure is available at

http://www.ercot.com/mktrules/guides/procedures/index.html

| 2.2.8 Initiate Request for Public Appeals |
| --- |
| Step # | Procedural Steps |
| CAUTION | Prior to entering EECP, ERCOT may issue an appeal through the public news media for voluntary load reduction if authorized by the ERCOT Chief Executive Officer or its designee based on an evaluation of existing and expected system conditions. |
| NOTE: | See Appendix 2 “Media Appeals for Voluntary Load Curtailments”. |
| NOTE: | See Phone Book at Shift Supervisor’s Desk. |
| NOTE: | The EECP procedures are coordinated between the system operators on the Transmission and Security desk and Frequency Control Desk. |
| 1 | WHEN the EECP procedures are invoked , at your discretion or in no case later than STEP 2 of the EECP, INITIATE a request for a public appeal for voluntary load reduction. See Appendix 2 “Media Appeals for Voluntary Load Curtailments” for notification guidelines. |
| 2 | As part of Restoration STEP 2 of the EECP procedure you may RECALL the request for a public appeal for voluntary load reduction. When the decision is made to RECALL the voluntary load reduction, See Appendix 2 “Media Appeals for Voluntary Load Curtailments” for notification guidelines. |

## 3.2   Appendix 2:  Media Appeals for Voluntary Load Curtailments

Section 5.6.7 of the ERCOT Protocols specifies steps in the Emergency Electric Curtailment Plan (EECP).  Step 2 of the EECP states:

Unless such a media appeal is already in effect, ERCOT staff shall issue an appeal through the public news media for voluntary energy conservation.

In addition to measures listed above, Section 5.6.6.1 of the ERCOT Protocols specifies:

ERCOT, at management’s discretion, may at any time issue an appeal through the public news media for voluntary energy conservation.

Decision to Make Media Appeals

- Medial appeal is required in EECP Step 2.

- Prior to entering EECP, the decision to make medial appeals must be authorized by the ERCOT Chief Executive Officer or designee. The Manager, System Operations or the Director, Grid Operations will promptly notify the Operations Shift Supervisor of the decision on initiating media appeals for voluntary load curtailment.

Procedure for Media Appeals

Operations Shift Supervisor

The Operations Shift Supervisor will notify the Manager, System Operations or the Director, Grid Operations that an appeal for voluntary load curtailment is necessary.

Administrative

The Manager, System Operations or the Director, Grid Operations will contact the Manager of Communications or designee and notify them that a media appeal for voluntary load curtailment is necessary.

Termination of Media Appeal

When System Operations has determined that the voluntary load curtailment is no longer necessary:

Operations Shift Supervisor

The Operations Shift Supervisor will notify the Manager, System Operations or the Director of Grid Operations the appeal for voluntary load curtailment is no longer necessary.

Administrative

The Manager, System Operations or the Director, Grid Operations will contact the Manager of Communications or designee and notify them that the media appeal for voluntary Load curtailment is no longer necessary.