ERCOT Operations Bulletin 341

ERCOT has revised the Operating Period Desk Procedure.  Changes include adding Section 2.5 Monthly Testing of Satellite Phone System

Adding Section 3.10 Attachment 1: Monthly Satellite Bridge Testing Form

A copy of the procedure is at:

http://www.ercot.com/mktrules/guides/procedures/index.html.

| 2.5 Monthly Testing of Satellite Phone System |
| --- |
| Step # | Procedural Steps |
| Purpose: | On the first weekend of each month, between the hours of 0000 Saturday and 0500 Monday, the Satellite Phone System Conference Bridge will be tested with Transmission Service Providers to ensure ERCOT maintains communication capability via the Satellite Phone System. As the Shift Supervisor makes the calls to the individual Transmission Service Provider. they will set a time that the ERCOT Operator will call the Satellite Phone System Conference Bridge and establish communication with the appropriate Transmission Service Providers. |
| Note: | Use the ERCOT Satellite Phone User Guide located in the Operating Procedure Manual for a list of the Transmission Service Providers that will be contacted by the ERCOT Operator and instructions on how to place a Satellite Phone System Conference Bridge Call. |
| 2 | On page 11 of the MX Turret phone select the appropriate line that applies to the ERCOT Operations Desk that is making the call. These numbers are located in the bottom right of the page 11 screen. BKST Day- Day Ahead Desk BKST Freq.- Frequency Desk BKST OPD – Operating Period Desk BKST TS #1 – Transmission Desk #1 BKST TS#2 – Transmission Desk #2 If the preprogrammed number does not function correctly, refer to Attachment B of the ERCOT Satellite Phone User Guide for the appropriate conference number. When prompted enter the Moderator Pass Code. If necessary wait on the line for approx. five minutes for the Participants to dial into the Conference Bridge. As each participant connects to the Conference Bridge record the name of the individual from the Transmission Service Provider making the call and any problems identified with the connection process. |
| 3 | If one or more of the Transmission Service Providers fails to connect to the Satellite Phone System Conference Bridge Call investigate the cause and log the following: Reason for inability to connect Actions taken by ERCOT Establish a time for a retest of the Transmission Service Providers not able to connect in the initial test. |
| 4 | When testing is completed, fill out the portion of the Monthly Satellite Phone Conference Bridge Testing Form (SEE Attachment 1). An electronic copy of this form is located in P:\ SYSTEM OPERATIONS ”Satellite Bridge Testing forms” folder. |
| 5 | When the applicable portion of the Monthly Satellite Phone Conference Bridge Testing Form is completed, save the form and close the file. Notify the Shift Supervisor that the Conference Bridge Call is complete and that the applicable portion of the Monthly Satellite Phone Conference Bridge Testing Form is complete. |
| 6 | Log the test date and results in the ERCOT Operations Log. |
| NOTE: | Notify the Help Desk of any Satellite phone problems during the test. |

## 3.10	Attachment 1 -- Monthly Satellite Bridge Testing Form (Typical)

| Conference Name | Transmission Service Provider | Call Connected? Yes / No | Operator from Transmission Service Provider making Call? | Problems Identified? |
| --- | --- | --- | --- | --- |
| Black Start Day Ahead | TXUED AEP GARLAND |  |  |  |  |
| Black Start Frequency Control | BTU CENTERPOINT |  |  |  |  |
| Black Start Operating Period | AEP STEC PUB |  |  |  |  |
| Black Start Transmission #2 | LCRA AEN TXUED CPS |  |  |  |  |