ERCOT Power Operations Bulletin #348

ERCOT has revised the Shift Supervisor Desk Procedure Manual.

The specific changes are shown below.

A copy of the procedure is available at:

http://www.ercot.com/mktrules/guides/procedures/index.html

| 2.2.10 TRE Investigation Reporting |
| --- |
|  | Procedural Steps |
| NOTE: | There are certain events listed in the Event Investigation Process that requires an e-mail from System Operations to ERCOT Operations Support and the TRE. An initial report from System Operations will trigger the investigation process. The subject line of the e-mail should read “TRE Investigation Reporting.” |
| NOTE: | Events that are deemed to be significant include, but are not limited to, the following: EECP Implementation Emergency Notice issued Simultaneous loss of any combination of three generating unit facilities, transmission lines, and autotransformers (138KV and above). Note: Count combined cycle trains as one unit SPS activation RAP implementation requiring load shedding Under frequency relay operations (or frequency deviations greater than .3Hz from scheduled frequency) Sustained voltage deviations greater than five percent on 345 Kv systems Alerts for significant transmission elements (345 Kv) Failure of computer systems at ERCOT, the Qualified Scheduling Entity (QSE) or Transmission Operator (TO) Voltage collapse on portions of 138 Kv or 345 Kv system Loss of an ERCOT, QSE, or TO control center Black Start initiation Uncontrollable loss of 150 MW or more of firm load shed for more than 15-minutes from a single incident |
| NOTE: | There are also DOE and several NERC reportable events that could trigger an investigation. To report such an event, see section 2.2.11. |
| 1 | When a significant event occurs, within one hour complete the form located in Attachment B “Event Investigation Form” and e-mail to distribution group entitled “TRE Investigation Reporting.” |

| 2.2.11 NERC and DOE Disturbance Reporting |
| --- |
|  | Procedural Steps |
|  | When Disturbance reporting is required: |
| NOTE: | NERC E-mail address: esisac@nerc.com, fax (609) 452-9550 DOE E-mail address: doehqeoc@oem.doe.gov, fax (202) 586-8485 DOE Operation Center voice phone: (202) 586-8100 ERCOT Compliance E-mail address: 1 ERCOT Compliance Team Send e-mail to distribution list entitled “NERC and DOE Disturbance Reporting.” |
| NOTE: | NERC Standard EOP-004-1 R3.1 requires a copy of the NERC Interconnected Reliability Operating Limit and Preliminary Disturbance Report to be submitted by the affected Operating Authority within 24 hours of the disturbance or unusual occurrence. |
| 1 | Forward the TDSP(s) report or the Director of Cyber Security’s report to ERCOT Compliance, NERC, and DOE. Ensure all three entities receive a report. (e.g. If TDSP or Director, Cyber Security sends a report to only one entity; make sure the other two entities receive a report as well.) |
| 2 | If ERCOT is required to issue a report to NERC and DOE even when the disturbance does not require a report from a TDSP (e.g. The disturbance involves two or more TDSPs area to meet the requirements for reporting.) of if a report is received from the Director, Cyber Security, then do the following: Complete required reports per NERC Attachment 1-EOP-004. Complete required reports per DOE OE-417. Forward reports to ERCOT Compliance, NERC, and DOE. |
| NOTE: | NERC Attachment 1-EOP-004 to report a disturbance can be downloaded at ftp://www.nerc.com/pub/sys/all_updl/oc/dawgstandards/rs//NERC_EOP-004-1_Form NERC IROL and Preliminary disturbance Report.doc DOE Form OE-417 to report a disturbance or cyber attack can be downloaded at http://www.eia.doe.gov/oss/forms.html. |

| 2.2.12 PUC Daily Report |
| --- |
| Step # | Procedural Steps |
| NOTE: | The PUC reports are to be generated twice per day: In winter months at 0100 and 0500 In summer months at 1100 and 1500 The timing change will be determined by the Manager, System Operations. |
| NOTE: | Be able to provide a list of unplanned generation outages for the day if requested by the PUC. |
| 1 | Complete the PUCT Daily Report template at the appropriate times. E-mail the report to the distribution list entitled “PUC-Available Generating Resources.” Do not add editorial comments to this report that reveal market sensitive data. General comments that convey overall system conditions are allowed. |
|  | Revise the last report sent and resend it if: The probability of an EECP event increases. Give reason(s) for escalation, OR Conditions change that required new notices to be issued or cancelled, such as, an OCN , Advisory, Alert, or Emergency Notice OR A shortage of generation capacity develops OR Local reliability concerns arise which include actual overloads and/or loss of load, especially the Laredo area, OR The Gibbons Creek Bryan East/Green Prairie 138 kV double circuit transmission line trips, or if there are unplanned outages of the generation units in the area. “ERCOT only” NERC and/or DOE event occurs. These events are market sensitive so provide a brief description without the market sensitive information. DCS event occurs |
| 2 | Use the following guidelines to determine the potential for EECP when completing the PUCT Daily Report: Potential for EECP 1 Low Sufficient capacity to cover peak demand An Advisory is in effect for Adjusted Responsive Reserves. Medium An Alert is in effect for Adjusted Responsive Reserves. Loss or delay of generation availability during peak demand that may diminish Physical Responsive Reserves High An Alert is in effect for Adjusted Responsive Reserves and trending downward after procuring quick-start capacity. Critical EECP Step 1 in effect |
|  | Potential for EECP 2 Low Sufficient capacity to cover peak demand An Advisory is in effect for Adjusted Responsive Reserves Medium EECP Step 1 in effect High Adjusted Responsive Reserve ≤ 2000 MW and trending downward Critical EECP Step 2 in effect |
| 3 | Potential for EECP 3 N/A – No EIL available Low Sufficient capacity to cover peak demand Medium EECP Step 2 in effect High Adjusted Responsive Reserve < 1000 MW and trending downward, OR Unable to maintain frequency ≥ 59.9 Hz Critical EECP Step 3 in effect |
| 4 | Potential for EECP 4 Low Sufficient capacity to cover peak demand Medium EECP Step 2 in effect High EECP Step 3 in effect Adjusted Responsive Reserve < 1000 MW and trending downward, OR Unable to maintain frequency ≥ 59.9 Hz Critical EECP Step 4 in effect |

3.3 Appendix 3  ERCOT EECP and NERC EEA Notifications Requirements

| Condition | Notified Entity | Notification Type | Time | How Notified | Update Requirements |
| --- | --- | --- | --- | --- | --- |
| EEA 1 | NERC | RCIS | ASAP | Via web link | As changes occur, minimum of 1 hour. |
| EECP 1 EEA 1 | TRE, NERC & DOE | Event Investigation Form RCIS | ≤ 1 Hour ASAP | E-mail Via web link | As changes occur, minimum of 1 hour. |
| EECP 2, EEA 2 | TRE, NERC & DOE | Event Investigation Form RCIS EIA-417 - Schedule 1 EIA-417 – Schedule 2 | ≤ 1 Hour ASAP 1 Hour 48 Hours | E-mail Via web link DOE web link DOE web link | As changes occur, minimum of 1 hour. |
| EECP 3, EEA 2 | TRE, NERC & DOE | Event Investigation Form RCIS EIA-417 - Schedule 1 EIA-417 – Schedule 2 | ≤ 1 Hour ASAP 1 Hour 48 Hours | E-mail Via web link DOE web link DOE web link | As changes occur, minimum of 1 hour. |
| EECP 4, EEA 3 IROL | TRE, NERC & DOE NERC | Event Investigation Form RCIS EIA-417 - Schedule 1 EIA-417 – Schedule 2 NERC Prelim. Report Final Report NERC Prelim. Report | ≤ 1 Hour ASAP 1 Hour 48 Hours 24 Hours 60 Days 72 Hours | E-mail Via web link DOE web link DOE web link | As changes occur, minimum of 1 hour. |
| Alert 0 | NERC | RCIS | ASAP | Via web link | Upon termination of EEA |

NOTE:  RCIS - Reliability Coordinator Information System

EEA – Energy Emergency Alert

LINKS:

RCIS - https://scis.nerc.net/scis.asp

NERC - ftp://www.nerc.com/pub/sys/all_updl/oc/dawgstandards/rs//NERC_EOP-004-1_Form NERC IROL and Preliminary disturbance Report.doc

DOE - ftp://ftp.eia.doe.gov/pub/electricity/eiafor417.doc

Event Investigation Form - Attachment B