## Power Operations Bulletin # 471

ERCOT has revised the Operating Period Desk Procedure Manual.

The Various Changes are shown below.

A copy of the procedure can be found at:

http://www.ercot.com/mktrules/guides/procedures/index.html

## 2.5	Monthly Testing of Satellite Phone System

Procedure Purpose: To ensure ERCOT maintains communication capability via the Satellite Phone.

| Protocol Ref. |  |  |  |  |
| --- | --- | --- | --- | --- |
| Guide Ref. |  |  |  |  |
| NERC Std. | COM-001-1 R2 | EOP-005 R5 |  |  |

| Approved by: | Effective Date: March 31, 2010 |
| --- | --- |
| Version: | 3.0 | Revision: | 4 |

| Step | Action |
| --- | --- |
|  | Primary Control Center |
| NOTE: | When a participant dials into the conference bridge before the moderator dials in, they will hear music and be placed on hold. |
| NOTE: | On the first weekend of each month, between the hours of 0000 Saturday and 0500 Monday, the Satellite Phone System Conference Bridge will be tested with Transmission Service Providers. As the Shift Supervisor makes the calls to the individual Transmission Service Provider, they will set a time that the ERCOT Operator will call the Satellite Phone System Conference Bridge and establish communication with the appropriate Transmission Service Providers. |
| NOTE: | Use the ERCOT Satellite Phone User Guide located in Section 7 of the Desktop Guide for a list of the Transmission Service Providers that will be contacted by the ERCOT Operator and instructions on how to place a Satellite Phone System Conference Bridge Call. |
| 1 | On page 11 of the MX Turret phone select the appropriate line that applies to the ERCOT Operations Desk that is making the call. These numbers are located in the bottom right of the page 11 screen. BKST Day- Day Ahead Desk BKST Freq.- Frequency Desk BKST OPD – Operating Period Desk BKST TS #1 – Transmission Desk #1 BKST TS#2 – Transmission Desk #2 If the preprogrammed number does not function correctly, refer to Attachment B of the ERCOT Satellite Phone User Guide for the Section 7 of the Desktop Guide. When prompted enter the Moderator Pass Code. If necessary wait on the line for approx. five minutes for the Participants to dial into the Conference Bridge. As each participant connects to the Conference Bridge record the name of the individual from the Transmission Service Provider making the call and any problems identified with the connection process. |
| 2 | If one or more of the Transmission Service Providers fails to connect to the Satellite Phone System Conference Bridge Call investigate the cause and log the following: Reason for inability to connect Actions taken by ERCOT Establish a time for a retest of the Transmission Service Providers not able to connect in the initial test. |
| 3 | Inform the Shift Supervisor when test is complete indicating any issues identified. |
| 4 | Log the test results in the Operations Log. |
|  | Alternate Control Center |
| 1 | When working out of the alternate Control Center during the monthly scheduled dates: Test the Satellite phone. |
| 2 | Inform the Shift Supervisor when test is complete indicating any issues identified. |
| 3 | Log the test results in the Operations Log. |