## Power Operations Bulletin # 474

ERCOT has revised the Frequency Control Desk Procedure Manual.

The Various Changes are shown below.

A copy of the procedure can be found at:

http://www.ercot.com/mktrules/guides/procedures/index.html

## 2.2.2 	Site Failover Hotline Message

Procedure Purpose: To inform the QSEs when a planed site failover is about to occur.

| Protocol Ref. |  |  |  |  |
| --- | --- | --- | --- | --- |
| Guide Ref. |  |  |  |  |
| NERC Std. | COM-001-1.1 R2 |  |  |  |

| Approved by: | Effective Date: May 12, 2010 |
| --- | --- |
| Version: | 4 | Revision: | 3 |

| Step | Action |
| --- | --- |
| 1 | Using the hotline if available notify all QSEs before the scheduled time for a planned site failover (preferably five (5) to 30 minutes). The following message should be communicated. The variable information is in brackets. When QSEs have answered the Hotline, review Hotline participants and log any issues. If necessary call participants individually. Typical script: “This call requires everyone to remain on the line until it is complete. [QSE] I will be asking you for the repeat back. This is ERCOT operator [first and last name]. At [time], ERCOT will perform a [planned, unplanned, emergency] site failover of its Energy & Market Management Systems from [Taylor, Austin] to [Austin, Taylor]. During this time, market communications will be unavailable for about 15 minutes, and real-time communications will be unavailable for about five minutes. All systems should reestablish communications automatically.” |
| 2 | As time permits, notify the Shift Supervisor of any issues during the call. |