## Power Operations Bulletin # 652

ERCOT has posted/revised the Shift Supervisor Manual.

The Various Changes are shown below.

A copy of the procedure can be found at:

http://www.ercot.com/mktrules/guides/procedures/index.html

## 3.3	Disseminating Information to System Security Response Group (SSRG)

Procedure Purpose: To communicate information concerning disturbances or unusual occurrences to appropriate parties in the Interconnection.

| Protocol Reference |  |  |  |  |
| --- | --- | --- | --- | --- |
| Guide Reference | 3.8 |  |  |  |
| NERC Standard | CIP-001-2a EA.1, EA.2, EA.3 | EOP-004-1 OE-417 |  |  |

| Version: 1 | Revision: 9 | Effective Date: December 13, 2013 |
| --- | --- | --- |

| Step | Action |
| --- | --- |
| NOTE | Threat alerts can be viewed at either of the following links: http://www.esisac.com/SitePages/Home.aspx, OR http://www.dhs.gov/files/programs/ntas.shtm The definitions for the threat alert levels are listed in the Security Alert Plan which can be found in the Operating Procedure Manual. |
| NOTE | The SSRG e-mail exploder list is used to disseminate information to the SSRG members of the ERCOT Region when an SSRG conference call is not necessary. This information is intended for use within the industry and not for public release. At the beginning of each e-mail state the follow “This information is intended for use within the industry and not for public release” At the bottom of each e-mail, be sure to include a Confidentiality Notice and your signature. The Reliability Coordinator Information System (RCIS) is used to disseminate information to other RCs in other Interconnections. Do not list the entity name on the SSRG e-mails or on the RCIS. |
| Events not Considered an Act of Suspected Sabotage |
| 1 | IF: A TO or QSE reports an event that is not considered an act of suspected sabotage, such as the following: Copper thefts Substation break-in Vandalism Malicious mischief Suspicious photos THEN: Disseminate this information using the ‘SSRG’ distribution list: State in the e-mail that the event is “currently not considered as an act of suspected sabotage”. State the region of the state the event occurred (South Texas, North Texas, etc.) |
| LOG | Log all actions. |
| Suspected Sabotage or Sabotage Events |
| Physical | For suspected physical sabotage at the ERCOT facilities, refer to ERCOT Guideline GL7.8.1 located under the “Sabotage Event Recognition” tab in each procedure manual. RCIS posting and SSRG email will also be required. |
| Cyber | When notified by Cyber Security of a reportable event at ERCOT, collect the information to post under “CIP Free Form” on the RCIS. |
| 1 | IF: A TO or QSE reports an act of suspected sabotage or a sabotage event; THEN: Verify that the FBI has been notified, Disseminate the information using the ‘SSRG’ distribution list: State in the e-mail that the event is considered “an act of suspected sabotage OR further investigation/information is needed to determine if event is an act of suspected sabotage,” State the region of the state the event occurred (South Texas, North Texas, etc.) ONCE: Enough information has been received; NOTIFY: TOs and QSEs via Hotline with information you have, Post on the RCIS using “CIP Free Form” (see Desktop Guide Shift Supervisor Section 2.2), Coordinate with the Manager, System Operations and/or Control Room Operations Manager to determine if procedure 3.4 SSRG Conference Calls is necessary and for any NERC and DOE reporting requirements. Typical Hotline Script: “This is ERCOT operator [first and last name], at [xx:xx], ERCOT notified the System Security Response Group (SSRG) of a suspected sabotage event [give information]. Please notify your SSRG representative.” |
| 2 | WHEN: Updates are received; THEN: Send an updated e-mail to the ‘SSRG’ distribution list, Update RCIS posting as needed |
| LOG | Log all actions. |

## 3.4	SSRG Conference Calls

Procedure Purpose: To communicate information concerning disturbances or unusual occurrences to appropriate parties in the ERCOT Region by making a SSRG conference call.

| Protocol Reference |  |  |  |  |
| --- | --- | --- | --- | --- |
| Guide Reference |  |  |  |  |
| NERC Standard | CIP-001-2a EA.1, EA.2, EA.3 | EOP-004-1 |  |  |

| Version: 1 | Revision: 7 | Effective Date: December 13, 2013 |
| --- | --- | --- |

| Step | Action |
| --- | --- |
| NOTE | The SSRG conference call will be used to inform the SSRG members of suspected sabotage or sabotage events, including multi-site sabotage events affecting larger portions of the Interconnection. The SSRG conference call will also be used for the following: When the Threat Alert Level has increased, To disseminate information and develop plans related to system emergencies and business continuity threats, To conduct quarterly tests with the minimum objective of reviewing and updating the contact list (test to be conducted in February, May, August and November); AND For any other events as warranted by the Manager, System Operations and/or Control Room Operations Manager Refer to Hotline and email scripts below for notifications. |
| Threat & Emergency Classifications | Threats and emergencies can be classified as, but are not limited to, the following four SSRG event-types: 1. Internal to ERCOT ISO: Physical Security: Verifiable attacks or sabotage, or threats of attacks or sabotage that could jeopardize the operation of physical equipment within the electrical boundaries of the ERCOT grid that have a direct effect on the reliability of the ERCOT grid. This could be, but is not limited to, generation equipment, transmission equipment, and communication equipment. b. Cyber Security: Verifiable loss of control of the ERCOT EMS or MMS that is identified by EMMS Production Support as an actual or probable act of sabotage or the loss of control by any of the market participants EMS Systems that is reported to ERCOT as an act of sabotage. 2. External to ERCOT ISO: a. Physical Security: Verifiable attacks or sabotage, or threats of attacks or sabotage that could jeopardize the operation of physical equipment in any electrical sector outside of the boundaries of ERCOT. b. Cyber Security: Verifiable loss of control over the EMS System of any participant in the electrical sector outside of the boundaries of ERCOT that is identified as an actual or probable act of sabotage. 3. Pandemic 4. Other unforeseen business continuity events (not to include grid instability) |
| QSE Notification | Using the Hotline, notify the QSEs of the SSRG conference call: Typical Hotline Script: “This is [first and last name] at ERCOT. There will be an SSRG conference call today at [time] Central Prevailing Time. The topic will be [quarterly test call, physical security, cyber security, pandemic or other topic]. Please notify your SSRG representative. The conference call number is 1-866-642-1665. Participants pass code is [code]. Any questions? Thank you.” |
| TO Notification | Using the Hotline, notify the TOs of the SSRG conference call: Typical Hotline Script: “This is [first and last name] at ERCOT. There will be an SSRG conference call today at [time] Central Prevailing Time. The topic will be [quarterly test call, physical security, cyber security, pandemic or other topic]. Please notify your SSRG representative. The conference call number is 1-866-642-1665. Participants pass code is [code]. Any questions? Thank you.” |
| Send E-mail | Send an e-mail to “1 SSRG” to make notification of the SSRG conference call. Typical Subject line for e-mail: SSRG conference call Typical Script for e-mail: An SSRG conference call has been schedule for today at [time] Central Prevailing Time (CPT). The topic will be [quarterly test call, physical security, cyber security, pandemic or other topic]. The conference call number is 1-866-642-1665. Participant pass code is [code]. Participation is mandatory. Include signature on email. |
| Log | Log all actions. |

## 3.5	Review Outage List

Procedure Purpose:  Verify known outages for the current day.

| Protocol Reference |  |  |  |  |
| --- | --- | --- | --- | --- |
| Guide Reference |  |  |  |  |
| NERC Standard |  |  |  |  |

| Version: 1 | Revision: 1 | Effective Date: March 1, 2013 |
| --- | --- | --- |

| Step | Action |
| --- | --- |
| 1 | Navigate to the Outage Scheduler or associated RUC displays in the MMS. Outage Scheduler>Outage Overview>OS Today’s Outages Market Operation>Reliability Unit Commitment>*RUC Displays>NDP Displays>Outaged Equipment Summary Alternatively, navigate to the Transmission Outages in the Market Information System. MIS; Grid; Transmission; Transmission Outages; Approved and Accepted Transmission Outages MIS; Grid; Transmission; Transmission Outages; Proposed Transmission Outages MIS; Grid; Transmission; Transmission Outages; Rejected Transmission Outages |
| 2 | Open OS Today’s Outages |
| 3 | Review the list of generation and transmission outages schedule for the current operating day. |
| 4 | Using the Outage Scheduler, verify if resources or facilities reported as Forced Outages are included in the outage list. |
| 5 | If Forced Outages are not listed, notify the Transmission and Security Operator. |
| 6 | Verify with the Transmission and Security and RUC Operator the results of studies for the hours and nodes where these resources and facilities are scheduled to be out of service. |
| 7 | If errors or problems are detected, consult with the Outage Coordinator. |

## 4.1	Resource Testing and In-Service Approvals

Procedure Purpose: This procedure provides direction and guidelines for conducting various required testing and approval processes for resources and transmission elements. This procedure does not include testing for the Net Dependable Capacity (NDC) on wind generation.

| Protocol Reference | 3.3.1 | 8.1.1.2.1.1(4) | 8.5.1.1 | 8.5.1.2(1) |
| --- | --- | --- | --- | --- |
|  | 8.5.1.2(3) |  |  |  |
| Guide Reference |  |  |  |  |
| NERC Standard |  |  |  |  |

| Version: 1 | Revision: 6 | Effective Date: December 13, 2013 |
| --- | --- | --- |
| Step | Action |
| Unit Testing |
| NOTE | QSEs will submit test requests to shiftsupv@ercot.com. If e-mail is down, a fax will be accepted at (512) 248-6858. Test request forms are located on the ERCOT website under ‘Operating Procedures’. |
| 1 | As requests for unit tests are received, make every reasonable effort to accommodate testing. Reasons for not accommodating testing: Unit has best shift factor to manage congestion for an outage. Without unit, contingency may reach max shadow price and become unsolvable, The request exceeds 7 days, A pattern of repeated requests for the same unit(s) indicate that abuse of the testing privilege may be taking place. If any request is refused for this reason, notify the Manager, System Operations and/or Control Room Operations Manager. |
| CAUTION | If deployment of the testing unit is necessary to maintain system security, direct the test be canceled and deploy as needed. |
| OK to Test | If the testing can be accommodated, RESPOND via e-mail or fax to the requesting party similar to the following: “ERCOT recognizes the need of <Company Name> to test its unit on <date and time>. ERCOT intends to make system adjustments to accommodate this testing to the extent possible consistent with system security. This intent is NOT a guarantee of accommodation”. ___________________ (Shift Supervisor) |
| Not OK to Test | IF the request cannot be accommodated, RESPOND via e-mail or fax to the requesting party similar to the following: “ERCOT cannot accommodate the request of <Company Name>for a unit test on <date and time> for the following reason(s) : <List reasons>”. __________________ (Shift Supervisor) |
| Approved Resources to be ONTEST |
| Approval | As Resource tests are approved, update “Approved Unit Tests” spreadsheet located on the System Operations SharePoint. All operators will be able to view the list to determine which resources are approved to be ONTEST. |
| Turbine Governor |
| 1 | At all times an All-Inclusive Generation Resource is on-line, its turbine governor must remain in service and be allowed to respond to all changes in system frequency. When the governor of a Generation Resource is blocked while the Resource is operating, the QSE shall promptly inform ERCOT. An All-Inclusive Generation Resource may not reduce governor response during abnormal conditions without ERCOT’s consent unless equipment damage is imminent. Each Generation Entity shall conduct applicable generating governor speed regulation tests on each of its Generation Resources. |
| In Service Approval (or Approval to Energize) |
| 1 | IF: A Market Participant makes a request to energize new or relocated equipment; THEN: Review notification provided by Operations Support Engineering, Approve the request if notification has been provided; IF: The equipment has not been approved by Operations Support Engineering, THEN: Delay the request and notify Operations Support Engineer. |
| Ancillary Service Testing Coordination |
| 1 | Ancillary Service Qualification Testing will be done in coordination with Operations Analysis and EMMS Production Support. IF: A QSE requests an Ancillary Service Qualification Test; VERIFY: A Wholesale Account Manager is in the notification or Direct the QSE representative to notify their Wholesale Account Manager to start the process. |
| 2 | The coordination of the testing times will be between System Operations, Operations Analysis and EMMS Production Support. When contacted by Operations Analysis: Wholesale Account Manager will notify QSE of scheduled test, Ensure reliable conditions exist at all times. |
| Log | Log all actions. |
| Coordinated Reactive Tests |
| NOTE | A minimum of 48 hours’ notice of the proposed test date is required. Requests shall be made between 0800 and 1700 on Business Days so that Operations Analysis is available for coordination to occur with ERCOT and the TO. ERCOT Operations and the TO confirms with the QSE the agreed upon test time and date or a rejection of the test time and date within 24 hours of the receipt of the request. |
| 1 | Coordinated Reactive Tests will be done in coordination with System Operations, Operations Analysis, the Transmission Operator (TO), and the Qualified Scheduling Entity (QSE). WHEN: A QSE makes a request for a Coordinate Reactive Test; VERIFY: Date/Time of Testing MVAR Leading and/or Lagging expected during the test CURL/D-Curve is attached Estimated MW output If all information is included in the test request, proceed to step 2. If not, reply to e-mail from QSE and request the missing information. |
| 2 | The coordination of the testing times will be between System Operations, Operations Analysis and the Transmission Operator (TO). WHEN: All information above is received; VERIFY: TO has approved the test, TO can approve verbally on a recorded line or by email Once the TO has approved and all information is accurate, approve the QSE test request. Include for following in the approval: Operations Analysis Shift Supervisors |
| OK to Test | If the testing can be accommodated, RESPOND via e-mail to the requesting party similar to the following: “ERCOT recognizes the need of <Company Name> to perform a Coordinated Reactive test with its unit <name> on <date and time>. ERCOT intends to make system adjustments to accommodate this testing to the extent possible consistent with system security. [TO] concurs with the test as long as real-time conditions allow for it. Will require Generator Operator to contact the wires company prior to test initiation. This intent is NOT a guarantee of accommodation”. ___________________ (Shift Supervisor) |
| Not OK to Test | If the request cannot be accommodated, RESPOND via e-mail to the requesting party similar to the following: “ERCOT cannot accommodate the request of <Company Name>for a unit test on <date and time> for the following reason(s) : <List reasons>”. __________________ (Shift Supervisor) |
| Approval | As Resource tests are approved, update “Approved Unit Tests” spreadsheet located on the System Operations SharePoint. All operators will be able to view the list to determine which resources are approved to be ONTEST. |
| Log | Log all actions. |

## 4.2	Unannounced Resource Testing

Procedure Purpose: This procedure provides direction and guidelines for conducting unannounced testing of resources.

| Protocol Reference | 8.1.1.2 |  |  |  |
| --- | --- | --- | --- | --- |
| Guide Reference | 3.3.1 |  |  |  |
| NERC Standard |  |  |  |  |

| Version: 1 | Revision: 10 | Effective Date: December 13, 2013 |
| --- | --- | --- |

| Step | Action |
| --- | --- |
| Unannounced Resource Testing |
| NOTE | Operations Analysis will provide the list of resources to be tested. The list of units are located at ERCOT SharePoint > System Operations – Control Center > Documents > Unannounced Unit Testing List. Use the current document. In addition, the Shift Supervisor may request at his discretion an unannounced test of any resource, other than Hydro, Wind and Nuclear-fueled Resources. Tests may be conducted as they best fit within the activities of the ERCOT Control Room, a minimum of 4 resources per week. The Resource to be tested must be On-line before beginning the test. To identify potential congestion it may be necessary to conduct a Security Analysis Study using a Powerflow Base Case or Real-time Snap shot of the System. NDCRC – Net Dependable Capability / Reactive Capability is located on the ERCOT MIS in the Applications folder Operations Analysis will complete the following items in the NDCRC: Current Seasonal HSL(Net MW) 30 Min Avg Real Time Telemetry (MW) Additional Comments Overall Test Results |
| Caution | Do not perform an unannounced test during a Watch for PRC or EEA event. Do not perform an unannounced test on a unit with an approved unit test. If an unannounced test is underway when a Watch or EEA event commences, the test may be cancelled. |
| Electronic VDI | Issue electronic VDI when test is complete so that the initiation and completion times are correct: ISSUE: VDI to QSE (see Desktop Guide Common to Multiple Desks Section 2.3) Choose “UNANNOUNCED CAPACITY TEST” as the Instruction Type from Resource level Initiation Time and Completion Time should be correct times In text, state “RETEST” if applicable |
| Testing Rules and Scripts | ISSUE an instruction to the QSE for the Resource being tested. The QSE has the following time to reach its HSL, depending on its output when the test begins: At LSL – 60 minutes to reach 90% of HSL, and an additional 20 minutes to reach HSL Between LSL and 50 % of HSL – 60 minutes to reach HSL Above 50 % of HSL – 30 minutes to reach HSL Typical script: “This is ERCOT operator [first and last name]. ERCOT is issuing a VDI at [time] to perform an Unannounced Unit Test on [Resource name]. Change the Resource status to “ONTEST” and increase the Resource output to the current telemetered HSL. The Resource will have [XXX] minutes to reach the telemetered HSL. Once the Resource has met the time requirement or reached its HSL, HOLD the Resource at its HSL or above for at least 30 minutes. [QSE] please repeat this back to me. That is correct, thank you.” The QSE will release all Ancillary Service obligations carried by the unit to be tested and change the Resource status to “ONTEST.” Combine Cycle Resources should include all units of the train. All QSEs associated with a jointly owned unit will be tested simultaneously. When the Resource reaches the time requirement or its HSL, SUSTAIN it at or above the Resources HSL for at least 30 minutes. NOTIFY the QSE that the test is complete, and RELEASE the resource from its VDI. If the Resource fails to reach its HSL within the time frame, CONTINUE TO HOLD the resource for at least 30 minutes, and LOG this in the ERCOT logs. NOTIFY the QSE that the test is complete, and RELEASE the Resource from its VDI. Typical script: “This is ERCOT operator [first and last name]. At [time], ERCOT is ending the unannounced test on [Resource name], please return to normal operation. I will be sending you the electronic VDI that you will need to acknowledge. Submit the results from the test on the NDCRC within 2 business days. [QSE] please repeat this back to me. That is correct, thank you.” COMPLETE the ERCOT values on the Unannounced Seasonal Generation Verification Test via the NDCRC application on the ERCOT MIS in a reasonable timeframe. MIS>Applications>NDCRC |
| Retest | The QSE can have the opportunity to request another test as quickly as possible (at a time determined by ERCOT) and may request a retest up to two times per month QSEs should submit retest requests to shiftsupv@ercot.com. The QSE may also demonstrate an increased value of HSL by operating the Resource at an Output Schedule for at least 30 minutes. In order to raise an output schedule above the seasonal HSL, the QSE may set the Resource telemetered HSL equal to its output temporarily for the purposes of the demonstration tests. After either a retest or a demonstration test, the MW capability of the Resource based on the average of the MW production telemetered during the test shall be the basis for the new HSL for the designated Resource for that Season. Any requested retest must take place within three Business Days after the request for retest. Any VDI issued as a result of a QSE-requested retest will be considered as an instructed deviation only for compliance purposes. ISSUE: VDI to QSE (see Desktop Guide Common to Multiple Desks Section 2.3) Choose “UNANNOUNCED CAPACITY TEST” as the Instruction Type from Resource level Initiation Time and Completion Time should be correct times In text, state “RETEST” |
| Notify | When test is complete, include the following information: Resource(s) Date Notification Time Start time of 30 Minute Hold Completion Time Send an e-mail to: Operations Analysis Shift Supervisors |
| Log | Log all actions. |

## 5.3	Notification of a Protective Relay or Equipment Failures

Procedure Purpose:  Be aware and respond if needed to protective relay system failures when notified by a QSE or TO.

| Protocol Reference |  |  |  |  |
| --- | --- | --- | --- | --- |
| Guide Reference | 6.2.3 | 6.2.4 |  |  |
| NERC Standard | PRC-001-1 R2, R2.2 |  |  |  |

| Version: 1 | Revision: 6 | Effective Date: December 13, 2013 |
| --- | --- | --- |

| Step | Action |
| --- | --- |
| Protective Relay or Equipment Failure |
| NERC | “If a protective relay or equipment failure reduces system reliability, the Transmission Operator shall notify its Reliability Coordinator and affected Transmission Operators and Balancing Authorities. The Transmission Operator shall take corrective action as soon as possible.” |
| NOTE | Protective relay systems include: relays, associated communications systems, voltage and current sensing devices, station batteries, and DC control circuitry |
| 1 | When notified by a QSE or TO that a protective relay or equipment failure reduces system reliability: Ask the QSE or TO how it reduces ERCOT Grid system reliability and if any corrective actions have been taken, Ask the QSE or TO if notifications have been made to any other affected TOs, Notify the Operations Support Engineer to verify that system reliability has been affected. If so, a corrective action must be taken within 30 minutes, Determine if other TOs are affected by this failure and make notification by phone. |
| 2 | After notification from a TO or QSE, NOTIFY by e-mail: OPS Support Engineering Operations Analysis Shift Supervisors The subject line of the e-mail should read “Protective Relay or Equipment Failure.” Include in the e-mail: Entity Name Brief description Contact information Any significant information |
| 3 | If a TO or QSE e-mails a – “Mis-Operation Relay report that has occurred in the past, forward to the above identified e-mail address. |
| 4 | Log all actions. |
| Protective Relay Outages |
| NOTE | Protective relay maintenance that ERCOT ISO has been made aware of can be found on the Outage Calendar located on the System Operations SharePoint. |
| Planned Outage | IF: Notified that a relay is going to be removed from service (Planned); THEN: Verify information is on the Outage Calendar located on the System Operations SharePoint Site; IF: Notification is posted; THEN: Notify the Market Participant they can proceed with work; IF: Notification is NOT posted; THEN: The relay can’t be removed from service unless there are secondary/back up relays that will be functional and no system degradation will occur; |
| Forced Outage | IF: Notified that a primary relay has been removed from service (forced); THEN: Ask if the secondary/back up relay is functional; IF: There is no secondary/back up relay; THEN: The equipment will need to be removed from service since it is no longer protected. |
| Log | Log all actions. |

## 5.4	Outage Coordination

Procedure Purpose:  Ensure Protocols are followed for Outage Coordination.

| Protocol Reference | 3.1 |  |  |  |
| --- | --- | --- | --- | --- |
| Guide Reference |  |  |  |  |
| NERC Standard | IRO-005-3.1a R1.9 |  |  |  |

| Version: 1 | Revision: 1 | Effective Date: December 13, 2013 |
| --- | --- | --- |

| Step | Action |
| --- | --- |
| NOTE | Real-time functional desks are not authorized to approve outages outside the timelines The Transmission Outage Approval process has been specifically designed to allow the market time to respond and achieve a market solution. Therefore, outages cannot be moved forward from one day to the next out of the approved timeframe without impacting the market solution The ERCOT Protocols clearly define the timelines for outage approval. At this time, no one (Outage Coordinator, System Operator, or Engineer) can approve a Planned Transmission Outage for the next day The only outages that are allowed for the next day are Level 1 outages and Remedial Switching Actions reported by the Transmission Operator |
| 1 | Direct any questions about scheduling of transmission outages and generation outages to the Outage Coordination personnel. |
| NOTE | Under extreme emergencies the Shift Supervisor may enter a Forced Outage for a Market Participant. |
| 2 | Navigate to the market Outage Scheduler in the Market Information System. MIS; Applications; ERCOT Applications; Outage Scheduler |
| 3 | Open Outage Scheduler |
| 4 | Select a Category of outage: Transmission Generation |
| 5 | Select the Market Participant Name: |
| 6 | Select Change User to access the Market Participants data |
| 7 | Select Create New Outage: Choose Forced |
| 8 | Select Actual Start: Enter Date and Time |
| 9 | Select Planned End: Enter Date and Time |
| 10 | Enter the Emergency Restoration in HRS Must be = or < than outage duration |
| 11 | Select the Nature of work: Choose a description from the dropdown |
| 12 | Select a Station Name: Choose a station from the dropdown |
| 13 | Select the Equipment Type: Choose the Equipment Type from the dropdown |
| 14 | Select the Equipment: Choose a piece of equipment from the dropdown |
| 15 | If known: Enter Supporting Information for outage |
| 16 | Select the Submit button. |
| 17 | If errors or problems are detected, consult with the Outage Coordinator. |
| Log | Log all actions. |

## 5.6	Equipment Limitation and Rating Changes

Procedure Purpose:  To ensure line rating changes are documented and correct.

| Protocol Reference | 6.5.3(2) |  |  |  |
| --- | --- | --- | --- | --- |
| Guide Reference |  |  |  |  |
| NERC Standard |  |  |  |  |

| Version: 1 | Revision: 4 | Effective Date: December 13, 2013 |
| --- | --- | --- |

| Step | Action |
| --- | --- |
| Line Rating Changes |
| NOTE | Normally line rating changes can only be changed when a NOMCR is received. |
| 1 | IF: Notified by a TO of an incorrect line rating; THEN: Notify the Operations Support Engineer. |
| Log | Log all actions. |
| TO Temporary Equipment Limitation Notifications |
| 1 | IF: Notified by a TO of any limitations on the Transmission Facilities that may affect Dispatch Instructions; THEN: Notify the Operations Support Engineer. |
| 2 | IF: The Operations Support Engineer confirmed the Temporary Equipment Limitation Notifications may affect Dispatch Instructions; THEN: Notify the Manager, System Operations and/or Control Room Operations Manager to post on the MIS Secure Area the Transmission Facility limitations that may affect Dispatch Instructions. |
| Log | Log all actions. |

## 5.7	Market Participant Backup Control Center Transfer

Procedure Purpose:  To provide internal notification.

| Protocol Reference |  |  |  |  |
| --- | --- | --- | --- | --- |
| Guide Reference |  |  |  |  |
| NERC Standard |  |  |  |  |

| Version: 1 | Revision: 3 | Effective Date: December 13, 2013 |
| --- | --- | --- |

| Step | Action |
| --- | --- |
| 1 | If notified by a QSE or TO that they will be transferring to their backup control center, or from their backup to primary, Identify Market Participant and if they are a [QSE] or [TO] Send e-mail to 1 ERCOT System Operators |
| 2 | If experiencing issues with communications, ICCP, etc. contact the Help Desk. |
| Log | Log all actions. |

## 6.1	Reports

Procedure Purpose: Provide reporting criteria and instructions for the daily reports sent to the PUC, the process to report certain events to the Texas Reliability Entity, posting EEA notices to RCIS and the process for reporting system disturbances to NERC and DOE.

| Protocol Reference | 22 (B) |  |  |  |
| --- | --- | --- | --- | --- |
| Guide Reference |  |  |  |  |
| NERC Standard | EOP-001-0.1b R4.1, R5 | EOP-002-3.1 R3, R6.3, R7.2 | EOP-004-1 R1, R3.1 | IRO-014-1 R1.1.2 |
|  | IRO-015-1 R15 | TOP-002-2.1b R4 | DOE OE-417 |  |

| Version: 1 | Revision: 17 | Effective Date: December 13, 2013 |
| --- | --- | --- |

| Step | Action |
| --- | --- |
| PUCT Daily Report |
| Initial Report | Complete the PUCT Daily Report template between 0300 – 0400 and again between 1400 – 1500 each day. |
| E-Mail Report | E-mail the report to the distribution list entitled “PUC-Available Generating Resources.” |
| Update Report | Update and resend report when system conditions change that cause concern. Some examples are below: The probability of an EEA event increases. Give reason(s) for concerns When Off-Line Non-Spin is deployed for capacity (provide times) A special update is not needed; provide information next time report is updated. Conditions change that required new notices to be issued or cancelled OCN , Advisory, Watch, or Emergency Notice Clarify whether Transmission Watch/Emergency is due to a planned or forced outage (state the area of the state) Do NOT update report for DAM delays or tool outages. The Gibbons Creek Bryan East/Green Prairie 138 kV double circuit transmission line trips, or if unplanned outages of generation units cause security problems in the Bryan-College Station area Localized gas curtailments, not expected to cause reliability issues (be specific, how much is derated) A DCS event Deployment of Load Resources Any Nuclear Resource issues (including trips, coming off-line, high risk activities, de-ratings, etc.) Do Not use abbreviations, spell words out. Send updated report when conditions have returned to normal. |
| Weather Information | The temperatures are automatically pulled from the EMS, however please verify temperatures from a National or Local Weather Service for each city listed and adjust as necessary. |
| Guidelines for Determining EEA Potential | Use the following guidelines to determine the potential for EEA when completing the PUCT Daily Report: Potential for EEA Level 1 Low Sufficient capacity to cover peak demand An Advisory is in effect for Physical Responsive Capability. Medium A Watch is in effect for Physical Responsive Capability. Loss or delay of generation availability during peak demand that may diminish Physical Responsive Reserves Excel MAI shows multiple hours of insufficient reserves and there is belief it is a significant threat High A Watch is in effect for Physical Responsive Capability and trending downward after procuring quick-start capacity Excel MAI shows multiple hours of insufficient reserves AND ERCOT has been unable to correct the capacity insufficiency over several hours AND ERCOT believes it is a significant threat Critical EEA Level 1 in effect Potential for EEA Level 2 Low Sufficient capacity to cover peak demand An Advisory is in effect for Physical Responsive Capability Medium EEA Level 1 in effect High Physical Responsive Reserve ≤ 1750 MW and trending downward Critical Physical Responsive Reserve ≤ 1375 MW and trending downward Potential for EEA Level 3 Low Sufficient capacity to cover peak demand High EEA Level 2 in effect Physical Responsive Reserve < 1000 MW and trending downward, OR Unable to maintain frequency ≥ 59.8 Hz Critical EEA Level 3 in effect |
| 7-Day Outlook |
| Report | Complete the 7-Day Outlook Report between 1500 – 1530 each day. |
| Open | The 7 Day Forecast file is located: P:\SYSTEM OPERATIONS drive in the “7-Day Outlook” Folder. |
| Verify | Data looks to be correct. |
| E-Mail Report | E-mail the report to the 7-Day Load and Capacity Outlook distribution list by selecting “Report” and confirming. |
| Event Analysis Reporting |
| 1 | WHEN an event occurs that is listed on the “event list” below, before shift is over: E-mail information to Manager, System Operations and Control Room Operations Manager The subject line of the e-mail should read “TRE Event.” |
| Event List | For purposes of the event analysis program, brief reports must be completed with 5 days. Most events listed are either OE-417 or EOP-004 reportable, those timelines and forms will be used in place of the EA brief report. Category 1 Events: An unexpected outage, contrary to design, of three or more elements caused by a common disturbance. For example: The sustained outage of a combination of three or more facilities The outage of an entire generation station of three or more generators (aggregate generation of 500 MW to 1,999 MW); each combined cycle unit is counted as one generator Intended and controlled system separation by the proper operation of a SPS Failure or misoperation of BPS SPS System-wide voltage reduction of 3% or more that lasts more than 15 continuous minutes due to a BPS emergency Unintended BPS system separation that results in an island of 100 MW to 999 MW. Excludes BPS radial connection, and non-BPS (distribution) level islanding Unplanned evacuation from a control center facility with BPS SCADA functionality for 30 minutes or more The loss of generation of 1,000 MW – 1,399 MW Loss of monitoring or control, at a control center, such that it significantly affects the entity’s ability to make operating decisions for 30 continuous minutes or more. Examples include, but are not limited to the following: Loss of operator ability to remotely monitor, control Bulk Electric System (BES) elements, or both. Loss of communications from SCADA RTUs Unavailability of ICCP links reducing BES visibility Loss of the ability to remotely monitor and control generating units via AGC Unacceptable State Estimator or Contingency Analysis solutions Category 2 Events: Complete loss of all BPS control center voice communication system for 30 minutes or more Complete loss of SCADA, control or monitoring functionally for 30 minutes or more Voltage excursions equal to or greater than 10% lasting more than 15 continuous minutes due to a BPS emergency Loss of off-site power (LOOP) to a nuclear generating station per the Nuclear Plant Interface Requirement Unintended system separation that results in an island of 1,000 MW to 4,999 MW Unintended loss of 300 MW or more of firm load for more than 15 minutes Interconnection Reliability Operating Limit (IROL) Violation for time greater than Tv. Category 3 Events: Unintended loss of load or generation of 1,400 MW or more Unintended system separation that results in an island of 5,000 MW to 10,000 MW Category 4 Events: Unintended loss of load or generation from 5,001 MW to 9,999 MW Unintended system separation that results in an island of more than 10,000 MW Category 5 Events: Unintended loss of load of 10,000 MW or more Loss of generation of 10,000 MW or more |
| NERC and DOE Reporting |
| NOTE | Contact the Manager, System Operations and/or Control Room Operations Manager when a NERC or DOE reporting event occurs. If available, they will be responsible to complete the required form In the body of the e-mail, type the following: "Contains Privileged Information and/or Critical Energy Infrastructure Information - Do Not Release.". NERC 24-hour Emergency Hotline (404) 446-9780), |
| OE-417 Reporting Events | DOE OE-417 forms can be downloaded at: ftp://ftp.eia.doe.gov/pub/electricity/eiafor417.doc. The items in bold must be reported within 1 hour of the incident. The others must be reported within 6 hours. All final reports must be submitted within 48 hours. OE-417 reports are required for the following events: Actual physical attack that causes major interruptions or impacts to critical infrastructure facilities or to operations Actual cyber or communications attack that causes major interruptions of electrical system operations Complete operation failure or shut-down of the transmission and/or distribution electrical system Electrical System separation (Islanding) where part or parts of a power grid remain(s) operational in an otherwise blacked out area or within the partial failure of an integrated electrical system Uncontrolled loss of 300 MW or more of firm system loads form more than 15 minutes from a single incident Load shedding of 100 MW or more implemented under emergency operational policy System-wide voltage reduction of 3 % or more Public appeal to reduce the use of electricity for purposed of maintaining the continuity of the electric power system Suspected physical attacks that could impact electric power system adequacy or reliability; or vandalism which target components of any security systems Suspected cyber or communications attacks that could impact electric power system adequacy or vulnerability Loss of electric service to more than 50,000 customers for 1 hour or more Fuel supply emergencies that could impact system adequacy or reliability |
| Event Reporting EOP-004-2 | NERC Preliminary Disturbance reports are to be completed within 24 hours. The events bolded are also DOE reportable and the OE-417 form should be used. For the other events, use the EOP-004 – Attachment 2 Event Reporting Form: Damage or destruction of a Facility that results in actions to avoid a BES Emergency Damage or destruction of a Facility that results from actual or suspected intentional human action Physical threats to a Facility excluding weather or natural disaster related threats, which has the potential to degrade the normal operation of the Facility or suspicious device or activity at a Facility. Do not report theft unless it degrades normal operation of a Facility Physical threats to a BES control center Public appeal for load reduction event System wide voltage reduction of 3% or more Manual firm load shedding 100 MW or more Automatic firm load shedding 100 MW or more (via automatic undervoltage or underfrequency load shedding schemes or SPS Voltage deviation of 10% or more of nominal voltage sustained for 15 or more continuous minutes IROL violation Loss of firm load for 15 minutes or more: 300 MW or more for entities with a previous year’s demand of 3,000 MW or more 200 MW or more for all other entities Each system separation resulting in an island 100 MW or more Loss of generation of 1,000 MW or more Complete loss of off-site power affecting a nuclear generating station per the Nuclear Plant Interface Requirement Unexpected loss within its area, contrary to design, of three or more BES Elements caused by a common disturbance (excluding successful automatic reclosing Unplanned evacuation from BES control center facility for 30 continuous minutes or more Complete loss of voice communication capability affecting a BES control center for 30 continuous minutes or more Complete loss of monitoring capability affecting a BES control center for 30 continuous minutes or more such that analysis capability (i.e., State Estimator or Contingency Analysis) is rendered inoperable |
| 1 | When required to file or forward a report the Manager, System Operations or Control Room Operations Manager will be responsible. File or forward non-cyber disturbance report to: NERC System Awareness (systemawareness@nerc.net) Fax (404) 446-9770), if internet down DOE (doehqeoc@oem.doe.gov) Fax (202) 586-8485), if internet down NERC and DOE Disturbance Reporting e-mail list For cyber disturbances, file or forward report to: NERC (esisac@nerc.com) NERC and DOE Disturbance Reporting e-mail list |
| RCIS Reporting |
| EEA Postings | There are four levels of Emergency Energy Alert (EEA). As ERCOT enters each level, postings must be made on the RCIS under “Energy Emergency Alert”: “ERCOT is declaring EEA 1” “ERCOT is declaring EEA 2” “ERCOT is declaring EEA 3” “ERCOT is in EEA 0 and back to normal operations.” |
| NXT Notification Requirements |
| Beginning of each Shift | Log into the NXT Communicator at the beginning of each shift in order to make the required notification quickly. If issues arise and you are unable to log into the NXT Communicator with your user name, notify the helpdesk and request immediate assistance. |
| NOTE | NXT notification should be coordinated with the Shift Engineer. |
| Watch | IF: A Watch for Physical Responsive Capability is initiated, THEN: Select the “SO Watch PRC below 2500” Scenario and activate notification, WHEN: A Watch for Physical Responsive Capability has been cancelled, THEN: Select the “SO Watch for PRC Cancelled” Scenario and activate notification. |
| EEA Implementation Levels | IF: ERCOT initiates EEA Level 1, THEN: Select the “SO EEA Level 1” Scenario and activate notification, IF: ERCOT initiates EEA Level 2, THEN: Select the “SO EEA Level 2” Scenario and activate notification, IF: ERCOT initiates EEA Level 3, THEN: Select the “SO EEA Level 3” Scenario and activate notification. |
| EEA Termination Levels | WHEN: EEA Level 3 is terminated, THEN: Select the “SO EEA Level 3 to EEA Level 2” Scenario and activate notification, WHEN: EEA Level 2 is terminated, THEN: Select the “SO EEA Level 2 to EEA Level 1” Scenario and activate notification, WHEN: EEA Level 1 is terminated, THEN: Select the “SO EEA Level 1 Cancellation” Scenario and activate notification. |
| Loss of Firm Load | IF: An Operator (ERCOT or TO) has issued a request for firm load shed of ≤ 100 MW, THEN: Notify the Manager, System Operations and/or Control Room Operations Manager immediately. WHEN: An Operator (ERCOT or TO) has issued a request for firm load shed of ≥ 100 MW, THEN: Notify the Manager, System Operations and/or Control Room Operations Manager immediately, Select the “SO Request Firm Load Shed” Scenario and activate notification. |
| NXT Testing | WHEN: Performing Shift Supervisor Procedure 9.2 Monthly Testing of Non-Routinely used Telecommunications Facilities, THEN: Select the “SO ENS Test” Scenario and activate notification. |
| ERCOT Morning Report |
| NOTE | This report is currently only required Monday – Friday. The Morning Report form is located on the _Operations Official Spreadsheets folder |
| 1 | Weather Information: Enter temperatures from a National or a Local Weather Service for each city listed. Enter the current day forecast conditions for each city listed. |
| 2 | Load Data: The All-Time Peak MW and Seasonal Peak MW will be provided as needed. Verify the Projected Peak MW and peak hour for the current day. Use the most reasonable forecast, which may not be the highest. Verify the Previous Day Actual MW. |
| 3 | Interchange: Verify the net flow across the DC-Ties for the peak hour. This can be obtained from the MOI under “DC Tie Scheduling” or from the Excel MAI. |
| 4 | Transmission Line Outages: Verify the number of 345 kV line segment outages for the peak hour. |
| 5 | Generation MW Totals: Verify the Generation scheduled outage MW total. Verify the Generation forced outage MW total. |
| 6 | Projected MW Reserves: Verify the Responsive Reserve requirement at the Project Peak. Verify the anticipated operating reserves available at time of peak. The anticipated operating reserves can be found by adding the “Max Cap. Room” and Responsive Reserve requirement. |
| 7 | Recent ERCOT Congestion Activity: No action needed |
| 8 | Comments: List any active OCNs, Advisories, Watches or Emergency notices. |
| 9 | Select: Create Report |
| EMAIL | The file is transferred to P:\SYSTEM OPERATIONS drive in the NERC Morning Report Folder. This report should be sent as an attachment by 0700 using the e-mail distribution list entitled “ERCOT Morning Report.” The subject line of the e-mail should read “ERCOT Morning Report for <date>” |
| RMR Unexcused Misconduct Events |
| NOTE | For a RMR unit, a “Misconduct Event” means any hour or hours during which Participant is requested to, but does not; deliver the energy at a level of at least 98% on each hour of the level shown in the Availability Plan. For a Synchronous Condenser Unit, a “Misconduct Event” means any hour or hours during which Participant is requested to, but does not, synchronize the Unit to the ERCOT Transmission Grid during any hour in which the Unit is shown in the Availability Plan |
| 1 | IF: An RMR or Synchronous Condenser fail to deliver the energy when requested to; THEN: Notify the Manager of System Operations and/or Control Room Operations Manager. The manager will gather the detailed information and send an e-mail to “Nodal Settlements and Billing” with the subject line “Action Required – RMR Unexcused Misconduct Event”. |
| Shift Schedule |
| NOTE | Shift Schedules will be posted to the MIS under GRID on the Transmission Page in the Transmission Supporting Information section. The posting of the schedule will be current at all time to be compliant with the Protocols. |
| GEO-Magnetic Disturbance (GMD) |
| NOTE | A geomagnetic disturbance (GMD) occurs when the magnetic field embedded in the solar wind is opposite that of the earth. This disturbance, which results in distortions to the earth’s magnetic field, can be of varying intensity and has in the past impacted the operation of communications systems, and electric power systems. |
| 1 | Periodically, monitor the NERC Reliability Coordinator Information System (RCIS) at https://rcis.nerc.net |
| 2 | WHEN: Alerts for GMDs are issued for K-7 or higher; THEN: Instruct the Transmission & Security and Real-Time Operators to make Hotline calls, AND Post message on MIS Public |
| 3 | WHEN: The GMD alert has expired; THEN: Instruct the Transmission Operator to make Hotline call to TOs, AND Post message on MIS Public |
| Gas Restrictions |
| 1 | Once notified by a QSE of gas restrictions Send an e-mail to “Gas Company Notifications”. This will notify all appropriate ERCOT staff. |
| 2 | Determine: If the gas restriction could impact electric power system adequacy or reliability, THEN: Proceed to “Reports” procedure for NERC/DOE reporting requirements, AND Consider fuel switching for the generation that has this capability This data can be viewed at ERCOT SharePoint > System Operations – Control Center > Quick Links > Fuel Oil Capability |
| Special Protection Systems (SPSs) |
|  | IF: A Monthly SPSs report is received by e-mail; THEN: Forward reports to: OPS Support Engineering Shift Supervisors |

## 7.6	Extreme Hot Weather

Procedure Purpose: To ensure ERCOT and Market Participants are prepared for Extreme Hot weather operations.

| Protocol Reference | 6.3.2(3)(a)(i) | 6.5.7.1.10(3)(c) | 6.5.9.2(1) | 6.5.9.3 |
| --- | --- | --- | --- | --- |
|  | 6.5.9.3.1 | 6.5.9.3.2 | 6.5.9.3.3 | 6.5.9.3.4 |
| Guide Reference | 4.2.1 | 4.2.2 | 4.2.3 | 4.2.4 |
| NERC Standard | COM-002-2 R2 | EOP-001-0.1b R4.1, R5 | IRO-005-3.1a R1.10 |  |

| Version: 1 | Revision: 5 | Effective Date: December 13, 2013 |
| --- | --- | --- |

| Step | Action |
| --- | --- |
| NOTE | Extreme Hot weather notifications are issued when: Temperatures are forecasted to be 103°F or above in the North Central and South Central weather zones. – OR – Temperatures are forecasted to be 94°F or above in the North Central and South Central weather zones during the following months (October – May). |
| OCN | When extreme hot weather is forecasted approximately 5 days away: Ensure OCN is issued Continue to monitor the weather Coordinate with Outage Coordination for the review of Planned and existing outages for the possibility of withdrawing or restoring equipment |
| Advisory | When extreme hot weather is forecasted approximately 3 days away: Ensure Advisory is issued Continue to monitor the weather Continue to coordinate with Outage Coordination for the review of Planned and existing outages to be withdrawn, rejected, or restored |
| Watch | When extreme hot weather is forecasted approximately 1 day away: Ensure Watch is issued Continue to monitor the weather Continue to coordinate with Outage Coordination for the review of Planned and existing outages to be withdrawn, rejected, or restored Contact Operations Support to run studies to determine the impact of current and future outages Review emergency operating procedures |
| Emergency Notice | When extreme hot weather has arrived and is beginning to have an adverse impact on the ERCOT System: Ensure Emergency Notice is issued Implement emergency procedures as needed |
| Issues | Notify the ERCOT Manager, System Operations or Control Room Operations Manager of any issues. |
| Log | Log all actions. |

## 8.1	Under Performing QSE

Procedure Purpose: To remedy under-performance of one or more QSE to prevent adverse effects on ERCOT ACE performance.

| Protocol Reference |  |  |  |  |
| --- | --- | --- | --- | --- |
| Guide Reference |  |  |  |  |
| NERC Standard |  |  |  |  |

| Version: 1 | Revision: 1 | Effective Date: December 13, 2013 |
| --- | --- | --- |

| Step | Action |
| --- | --- |
| 1 | IF: Under-performance by one or more QSEs is detected, THEN: VERIFY the Resource Operator has established communication with the QSE(s) to determine the cause. VERIFY that the Transmission & Security and Real-Time Desk Operators are informed of the situation. ALLOW the Transmission & Security and Real-Time Operators to RESOLVE the problem to restore ERCOT ACE performance to normal. |
| 2 | IF: QSE continues to under-perform in real time, AND ERCOT’s NERC performance requirements are not being met, THEN: ASSIGN a system operator to collect performance data on the QSE(s) affecting ERCOT’s NERC performance VERIFY data collected by system operators from the EMMS |
| NOTE | Step 3 may be done at any time. |
| 3 | RECORD the following information: QSE name Date and Time period of non-performance Type(s) of AS not provided and nature of non-performance Perceived effect on ERCOT’s NERC performance requirements Description of remediation attempts and results |
| Log | Log all actions. |

## 8.2	Dispatch Instruction Disputes

Procedure Purpose: The Shift Supervisor applies this procedure for resolving dispatch instruction disputes when the system operator and the participant fail to resolve the issue raised by the participant.

| Protocol Reference | 6.5.3(2) | 6.5.7.9 | 6.5.1.2 (4) | 6.5.7.8(3) |
| --- | --- | --- | --- | --- |
| Guide Reference |  |  |  |  |
| NERC Standard |  |  |  |  |

| Version: 1 | Revision: 1 | Effective Date: December 13, 2013 |
| --- | --- | --- |

| Step | Action |
| --- | --- |
| NOTE | Each TO and QSE shall comply fully and promptly with Dispatch Instructions, unless in the sole and reasonable judgment of the TO or QSE, such compliance would create an undue threat to safety, undue risk of bodily harm or undue damage to equipment’s, or the Dispatch Instruction is otherwise not in compliance with the Protocols. An Intermittent Renewable Resource (IRR) must comply with Dispatch Instructions requiring it to reduce output two MW or more below the Resource’s latest HSL. |
| 1 | IF: A Resource has inadequately responded to a Dispatch Instruction, THEN: Notify the QSE representing the Resource as soon as practicable. |
| 2 | IF: The dispatch instruction is deemed to be invalid, THEN: Issue a new Valid Dispatch Instruction. THEN Go to STEP 4. IF: The dispatch instruction is confirmed as a valid dispatch instruction, THEN: Clarify the issue with the participant. |
| 3 | IF: A participant(s) does not agree with the resolution: THEN: Direct the participant(s) to contact their ERCOT Wholesale Client Services representative for instructions on filing a formal dispute resolution request. OTHERWISE, Go to next step |
| 4 | WHEN: The dispatch instruction dispute is resolved THEN: Inform all participants involved in the dispute of the resolution of the dispute |
| 5 | RECORD the following information: Summary of communications with the participant Agreements reached Understood disagreements and, Reasons for proposed actions |
| Log | Log all actions. |

## 8.3	Possible Protocol or Operating Guide Violations

Procedure Purpose: Provide instructions for reporting that a QSE or TO may have violated an ERCOT Protocol or Operating Guides requirement.

| Protocol Reference | 6.5.7.9 |  |  |  |
| --- | --- | --- | --- | --- |
| Guide Reference | 3.1.2 |  |  |  |
| NERC Standard |  |  |  |  |

| Version: 1 | Revision: 3 | Effective Date: December 13, 2013 |
| --- | --- | --- |

| Step | Action |
| --- | --- |
| 1 | IF: It appears that a QSE or TO is in violation of the ERCOT Protocols or Operating Guides, THEN: Confirm the ERCOT System Operator’s finding of a possible violation and that an attempt was made to resolve issue with the QSE or TO personnel. Attempt to resolve the issue. Obtain information from Market Operations Support and/or Operations Support personnel, as needed. IF resolution is reached, then LOG the event and this procedure is complete. |
| 2 | IF: No agreement can be reached; THEN: Review the incident to establish confidence that there has been a possible violation. Submit information to Manager System Operations and/or Control Room Operations Manager |
| 3 | Log all actions. |

## 9.1	Monthly Testing of Satellite Phone System

Procedure Purpose: To test the satellite phone system between ERCOT and the Transmission Operators to ensure communication capability via the Satellite Phone System.

| Protocol Reference |  |  |  |  |
| --- | --- | --- | --- | --- |
| Guide Reference |  |  |  |  |
| NERC Standard | COM-001-1.1 R2 | EOP-005-1 R5 |  |  |

| Version: 1 | Revision: 3 | Effective Date: December 13, 2013 |
| --- | --- | --- |

| Step | Action |
| --- | --- |
| NOTE | This test is to be conducted on the first weekend of each month, between the hours of 0000 Saturday and 0500 Monday. Not all ERCOT TOs have satellite phones, so the call will be coming in on their regular landlines. Verify whether or not they are communicating via satellite phone or regular landlines while testing. Refer to Desktop Guide Common to Multiple Desks Section 2.7. When a participant dials into the conference bridge before the moderator dials in, they will hear music and be placed on hold. |
| Test | Call each ERCOT TO using the preprogrammed number on the Turret Phone. If there is no answer: Call the ERCOT TO directly using the Satellite Phone number provided in Desktop Guide Common to Multiple Desks Section 2.7.1 and inform them of the time of their respective Satellite Conference Bridge Call. |
| Forms | Complete the Monthly Satellite Testing forms located the in P:\ SYSTEM OPERATIONS/Satellite Testing Phone Testing Forms folder. |
| Email | Send the compiled results of the Satellite phone test by e-mail to: 1 ERCOT Shift Supervisors |
| File | File a hard copy in the control room daily file. |
| Log | Log all actions. |

## 9.2	Monthly Test of Non-Routinely used Telecommunications Facilities

Procedure Purpose: To ensure backup communications are tested monthly.

| Protocol Reference |  |  |  |  |
| --- | --- | --- | --- | --- |
| Guide Reference |  |  |  |  |
| NERC Standard | COM-001-1.1 R2 |  |  |  |

| Version: 1 | Revision: 7 | Effective Date: December 13, 2013 |
| --- | --- | --- |

| Step | Action |
| --- | --- |
| Primary Control Center |
| Phone Tests | On the first weekend of each month, between the hours of 0000 Saturday and 0500 Monday: Test the Control Room Cell Phone by calling the ERCOT Helpdesk Cell Phone. If any issues are found, send e-mail to “shiftsupv” and back office will follow up. Test the Standalone Satellite phone. It isn’t necessary to call a satellite number, just verify the phone is operational. Refer to Desktop Guide Common to Multiple Desks Section 2.7.4. If any issues are found, send e-mail to “shiftsupv” and back office will follow up. |
| SAT modem testing | Coordinate the following test with the DC Tie Operator at the alternate control center Using the turret, call each programmed desk SAT Phone at the alternate control center If any issues are found, send e-mail to “shiftsupv” and back office will follow up. |
| NXT Test | Test NXT Communicator by activating the “SO ENS Test” scenario between the hours of 0800-2200. If any issues are found, open help ticket and cc: “shiftsupv”. |
| Log | Log all actions. |
| Alternate Control Center |
| Phone Tests | When working out of the alternate Control Room during the monthly scheduled dates: Test Control Room Cell Phone with the ERCOT Helpdesk Cell Phone. If any issues are found, send e-mail to “shiftsupv” and back office will follow up. Test the Satellite phone associated to the Operations Desk on each turret. It isn’t necessary to call a satellite number, just verify the phones are operational. If any issues are found, send e-mail to “shiftsupv” and back office will follow up. Test the Standalone Satellite phone operation located in the Control Room. It isn’t necessary to call a satellite number, just verify the phone is operational. Refer to Desktop Guide Common to Multiple Desks Section 2.7.5. If any issues are found, send e-mail to “shiftsupv” and back office will follow up. |
| SAT modem testing | Coordinate the following test with the DC Tie Operator at the other control center Using the turret, test call each programmed SAT Desk Phone at the other control center If any issues are found, send e-mail to “shiftsupv” and back office will follow up. |
| NXT Test | Log into the Bastrop ENS link when working out of the alternate Control Room in Bastrop, Test NXT Communicator by activating the “SO ENS Test” scenario between the hours of 0800-2200. If any issues are found, open help ticket and cc: “shiftsupv”. |
| Log | Log all actions. |

## 10.2		EMMS and Interface System Failures

Procedure Purpose: Provide guidance to the Shift Supervisor for coordinating with the ERCOT IT Help Desk if critical functions or systems fail such that system operators and/or participants are precluded for performing and complying with their obligations and therefore jeopardizing the security of the system.

| Protocol Reference |  |  |  |  |
| --- | --- | --- | --- | --- |
| Guide Reference |  |  |  |  |
| NERC Standard | COM-001-1.1 R5 | EOP-008-0 R1.4 |  |  |

| Version: 1 | Revision: 7 | Effective Date: December 13, 2013 |
| --- | --- | --- |

| Step | Action |
| --- | --- |
| 1 | If any Control Room computer systems (ICCP, Web Portal, MIS, or API) events, failures, or incidents that affect normal operations occur, DETERMINE criticality and impact to the reliability to the grid, CONTACT the ERCOT Help Desk immediately from the Supervisor Help Desk button on the Turret Phone or extension 6804. If necessary, contact the on-call IT person first then contact the Help Desk. |
| NOTE | For a complete EMMS failure, see Real-Time Procedure Section 3.1 Frequency Control Operating Procedure and 3.3 System Failures. |
| 2 | IF: Any of the aforementioned systems fail and are effecting ERCOT systems or multiple Market Participants and will be unavailable for longer than 15 minutes; THEN: Notify market participants of the problem and expected duration via Hotline, Request additional assistance from other support staff. |
| 3 | When the problem is resolved, Notify all participants via Hotline of the problem resolution. |
| 4 | RECORD the following information: Date Time of event Description of system alarms, events, failures, or incident Actions taken and resolution Time of system or function restoration |
| Log | Log all actions. |
| Data and/or Voice Communication Failures |
| 1 | Notify the Help Desk of the loss and REQUEST assistance to re-establish voice and/or data communications. Telecommunications group will be responsible for voice communications. EMMS Production group will be responsible for data communications |
| 2 | Use back-up communications if needed such as the Control Room cell phone, Standalone Satellite phone or the PBX Bypass phones to maintain communications with the other control room, TOs, QSEs, SPP and any other entities as needed. The list of phone numbers is located in the Phone Book at Shift Supervisor’s Desk and also programmed into the cell phone. |
| 3 | IF the criticality and impact of events or failures is such that Market Participants are, or will be affected before the problem can be resolved, THEN: Instruct ERCOT System Operator to NOTIFY the other ERCOT Control Room and all market participants via Hotline of the problem and expected duration. If Hotline is unavailable utilize any of the following methods: Control Room cell phone, PBX Bypass phones, or Standalone Satellite phone. REQUEST additional assistance from other support staff, as needed. |
| NOTE | Steps 4 & 5 may be performed in any order. |
| 4 | RECORD the following: Date Time of event Description of events, failures, or incident Actions taken and resolution Time of system or function restoration |
| 5 | When the problem is resolved, NOTIFY all participants via Hotline of the problem resolution. |
| Log | Log all actions. |
| Dynamic Rating, SCED Status, EMBP, SE, RTCA or RLC Alarms |
| NOTE | Normal status for the Dynamic Rating, SCED Status, EMBP, SE, RTCA and RLC Status is indicated by each status box constant green on the “ERCOT & QSE Summary Page” in the PI system. Failure of the PI server is indicated by abnormal status of Dynamic Rating, SE and RLC, accompanied by the PI system “flat-lining” Dynamic Rating, SE and RLC status boxes flashing red AND PI flat-lining may indicate failure of the EMS. |
| Monitor | PERFORM the following as applicable to the indicated conditions: IF only the Dynamic Ratings status box is flashing red, CONTACT the ERCOT Help Desk TELL them the Dynamic Rating Alarm status in Processbook is flashing red and the dynamic ratings are not being sent to the SCADA in the EMS. REQUEST they notify the on-call EMMS Production person of the situation. IF only the RLC status box is flashing yellow/red, CONTACT the ERCOT Help Desk TELL them the RLC Alarm status in Processbook is not green Greater than 5 minutes but less than 10 minutes turns - Yellow Greater than 10 minutes turns - Red DIRECT them to notify the on-call EMMS Production person of the situation. IF only the SCED Status box is flashing red, Follow the Managing SCED Failures in the Real Time Desk Procedure. If SCED failure can’t be resolved CONTACT the ERCOT Help Desk and DIRECT them to notify the on-call EMMS Production person of the situation. IF only the EMBP box is flashing red, Determine the reason Emergency Base Point are being issued, Remove the Emergency Base Point flag when condition allow, If EMBP can’t be resolved CONTACT the ERCOT Help Desk and DIRECT them to notify the on-call EMMS Production person of the situation. IF only the SE status box is flashing red, CONTACT the Operations Support Engineer TELL them the SE Alarm status in Processbook is flashing red IF only the RTCA status box is flashing yellow or red, CONTACT the Operations Support Engineer RTCA executes every 5 minutes, if RTCA doesn’t complete within the desired threshold the display changes colors Greater than 7 minutes but less than 10 minutes turns - Yellow Greater than 10 minutes turns - Red TELL them the RTCA Alarm status in Processbook is flashing yellow/red Greater than 15 minutes, inform QSEs for STP and CPSES. |
| Building Security and Fire Alarms |
| NOTE | The Shift Supervisor or designee will ensure staff members adhere to emergency evacuation procedures and evacuate all team members from the Control Room if an emergency evacuation is required. |
| 1 | IF: Building security or fire alarm sounds, THEN: Contact Security’s Emergency Number if Security has not already made communications with the Control Room. |
| 2 | IF: It is determined it is a drill, THEN: Retrieve the ‘orange’ bag for the employee roster, Account for each operator by marking them present and return form to Security staff at front desk (if able). IF: If unable to return roster in a reasonable timeframe, CONTACT: Security and request them to retrieve roster during the next patrol. |
| 3 | IF: Control Room personnel are in danger or ordered to be evacuated, THEN: Transfer control of the Grid to the Alternate Control Center (see “Loss of Primary Control Center Functionality” procedure Section 4.6 in the DC Tie Desk Procedure), Request additional assistance from other support staff, Evacuate the Control Room to a safe area for Zone #1, Retrieve the ‘orange’ bag for the employee roster, Account for each employee by marking them present at the rally point. |
| 4 | Notify the Manager, System Operations and/or Control Room Operations Manager as soon as practical. |
| Failure of the Emergency Generator |
| 1 | If the Facilities emergency generator fails to start, you will be notified by the Facilities Staff. |
| 2 | If the Facilities Staff or the Shift Supervisor determines that it will be more than 20 minutes before the emergency generator can be started, the Shift Supervisor may consider initiating the “Loss of Primary Control Center Functionality” procedure. |
| 3 | The Shift Supervisor or his/her delegated representative should notify the Manager, System Operations and/or Control Room Operations Manager that the controls have been transferred to the other control center. |
| 4 | REQUEST additional assistance from other support staff as needed. |
| NOTE | See Desktop Guide Shift Supervisor Section 2.1. |

Document Control

Preparation

| Prepared by | Role | Date Completed |
| --- | --- | --- |
| Frosch, Hartmann, Stone, and Barcalow | Preparers | November 10, 2010 |
| Frosch and Hartmann | Procedure writers and editors | November 29, 2010 |
| Frosch, Hartmann, and Moore | Procedure writers and editors | January 26, 2011 |
| Frosch and Hartmann | Procedure writers and editors | March 23, 2011 |
| Frosch and Hartmann | Procedure writers and editors | April 20, 2011 |
| Frosch and Hartmann | Procedure writers and editors | June 6, 2011 |
| Frosch and Hartmann | Procedure writers and editors | July 18, 2011 |
| Frosch and Hartmann | Procedure writers and editors | August 30, 2011 |
| Frosch and Hartmann | Procedure writers and editors | September 28, 2011 |
| Frosch and Hartmann | Procedure writers and editors | October 28, 2011 |
| Frosch and Hartmann | Procedure writers and editors | December 13, 2011 |
| Frosch and Hartmann | Procedure writers and editors | January 16, 2012 |
| Frosch and Hartmann | Procedure writers and editors | February 27, 2012 |
| Frosch and Hartmann | Procedure writers and editors | April 25, 2012 |
| Frosch and Hartmann | Procedure writers and editors | May 10, 2012 |
| Frosch and Hartmann | Procedure writers and editors | May 30, 2012 |
| Frosch and Hartmann | Procedure writers and editors | July 10, 2012 |
| Frosch and Hartmann | Procedure writers and editors | August 27, 2012 |
| Frosch and Hartmann | Procedure writers and editors | October 26, 2012 |
| Frosch and Hartmann | Procedure writers and editors | February 26, 2013 |
| Frosch and Hartmann | Procedure writers and editors | May 28, 2013 |
| Frosch and Hartmann | Procedure writers and editors | July 10, 2013 |
| Frosch and Hartmann | Procedure writers and editors | August 7, 2013 |
| Frosch and Hartmann | Procedure writers and editors | August 28, 2013 |
| Frosch and Hartmann | Procedure writers and editors | December 11, 2013 |

Manual Change History

| Procedure | Ver/Rev | Reason for Issue | Effective Date |
| --- | --- | --- | --- |
| All Sections | 1.0 / 0 | New procedures for all sections for Nodal implementation | November 28, 2010 |
| 3.1 4.2 6.1 10.2 | 1.0 / 1 1.0 / 1 1.0 / 1 1.0 / 1 | Updated steps 1 and 5, deleted steps 6, 7 and 8 Updated VDI, Testing Rules and Retest Updated PUCT Daily Report step “Update Report”. Updated all steps of Texas RE Event Reporting. Updated Title (Dynamic Rating, SCED Status, EMBP, SE, RTCA or RLC Alarms), 1st Note and Monitor | December 1, 2010 |
| 3.2 3.3 3.7 4.2 6.1 10.2 | 1.0 / 1 1.0 / 1 1.0 / 1 1.0 / 2 1.0 / 2 / 2 | Updated step 1,3 and added step 4 in “Capacity Monitoring” Updated step 4 Updated step No SCED Solution Updated VDI, Retest, and Notify, added Completion Updated step OE-417 Reporting Events in NERC, DOE Reporting and step 2 on GEO-Magnetic Disturbance (GMD) Updated step Monitor on “Dynamic Rating, SCED Status, EMBP, SE, RTCA or RLC Alarms” | January 31, 2011 |
| 3.2 5.3 5.5 6.1 7.2 7.3 9.2 | 1.0 / 2 1.0 / 1 1.0 / 1 1.0 / 3 1.0 / 1 1.0 / 1 1.0 / 1 | Updated step 3 “Capacity Monitoring” Updated step 1 & 3 Updated 1st note & step 2 Updated PUCT Daily Report, Texas RE Event Reporting & NXT Notification Updated EEA Checklist Updated EEA Restoration Checklist Added new steps “SAT modem testing” & updated NXT Tests | March 25, 2011 |
| 4.2 5.1 7.1 7.3 | 1.0 / 3 1.0 / 1 1.0 / 1 1.0 / 1 | Updated “Unannounced Resource Testing” 1st note Updated 2nd & 6th paragraphs Updated “System Disturbance” NERC, step 2 and “Degraded Weather” step 3 Updated Table | April 22, 2011 |
| 5.3 5.7 6.1 7.1 7.4 7.5 7.6 8.3 | 1.0 / 2 1.0 / 1 1.0 / 4 1.0 / 2 1.0 / 1 1.0 / 0 1.0 / 1 1.0 / 1 | Updated step 2 Updated all steps Updated all steps in Texas RE Event Reporting and NERC and DOE Reporting Updated steps in Degraded Weather Updated all steps Added new procedure Updated all steps Updated step 2 and deleted step 3 | June 8, 2011 |
| 3.6 4.1 4.2 6.1 7.2 7.3 9.2 | 1.0 / 1 1.0 / 1 1.0 / 4 1.0 / 5 1.0 / 1 1.0 / 1 1.0 / 2 | Updated step 3 Removed Initial Synchronization of New Resource Updated Testing Rules Updated step Event List Updated EEA Implementation Checklist Updated EEA Restoration Checklist Added Notice Builder test in Primary Control Center section | July 20, 2011 |
| 4.2 5.5 6.1 7.2 7.3 7.7 9.2 10.1 | 1.0 / 5 1.0 / 2 1.0 / 6 1.0 / 2 1.0 / 3 1.0 / 0 1.0 / 3 1.0 / 1 | Updated step Caution Updated 1st Note Updated step 1 in Texas RE Event Reporting and NXT Testing in NXT Notification Requirements Updated EEA Implementation checklist Updated EEA Restoration checklist Added Extreme Hot Weather Updated NXT Test in Alternate Control Center Updated step 3 | September 1, 2011 |
| 3.4 6.1 7.2 7.3 9.2 | 1.0 / 1 1.0 / 7 1.0 / 2 1.0 / 3 1.0 / 4 | Grammar changes Combined EEA 2A & B per NPRR 379 Updated to implement NPRR 379 Updated to implement NPRR 379 Updated Phone Test in Alternate Control Center | October 1, 2011 |
| 3.7 7.2 10.2 | 1.0 / 2 1.0 / 3 1.0 / 3 | Changed title & all steps Updated EEA checklist Updated 1st Note | November 1, 2011 |
| 3.3 6.2 6.3 | 1.0 / 2 1.0 / 1 1.0 / 1 | Updated all steps Updated step 2 Updated step 1 & 2 All procedures in this manual have been reviewed. | December 15, 2011 |
| 1.2 4.2 5.7 | / 1 / 6 / 2 | Updated Scope Updated all steps of procedure Updated Market Participant Backup Control Center Transfer | January 19, 2012 |
| 2.1 3.3 3.4 3.7 3.8 4.1 4.2 5.3 5.6 5.8 6.1 7.1 9.1 9.2 10.2 | 1.0 / 1 1.0 / 3 1.0 / 2 1.0 / 3 1.0 / 1 1.0 / 2 1.0 / 7 1.0 / 3 1.0 / 1 1.0 / 1 1.0 / 8 1.0 / 3 1.0 / 1 1.0 / 5 1.0 / 4 | Updated paragraph 4 Updated Step 3 Updated Threat & Emergency Classifications & Desktop Guide reference Changed Shift Engineer to Operations Support Corrected grammar on step 1 Changed Shift Engineer to Operations Support Updated procedure Changed Shift Engineer to Operations Support Corrected grammar on step 2 Updated step 2 Updated Texas RE Event Reporting, OE-417 reporting & Desktop Guide reference Updated Desktop Guide reference Updated Desktop Guide reference Updated Desktop Guide reference Changed Shift Engineer to Operations Support and updated Desktop Guide reference | March 1, 2012 |
| 2.1 3.3 3.6 5.6 6.1 7.1 7.4 7.5 7.6 | 1.0 / 2 1.0 / 4 1.0 / 2 1.0 / 2 1.0 / 9 1.0 / 4 1.0 / 2 1.0 / 2 1.0 / 2 | Changed TSP/DSP to TO Updated 3rd Note Updated purpose Changed TSP to TO and Transmission Facility Updated step Update Report & changed ARR to PRC and ERCOT Morning Report Updated step NERC and Degraded Weather Updated OCN, Advisory, & Watch steps Deleted Cold Weather, not Extreme Cold Weather Section number changed, Added OCN, Advisory and Emergency Notice | May 1, 2012 |
| 3.2 | 1.0 / 3 | Updated to reflect changes in the TAC approved Non-Spin document | May 14, 2012 |
| 7.2 7.3 | 1.0 / 3 1.0 / 4 | Updated EILS to ERS per NPRR 451 & added TO load management program Updated EILS to ERS per NPRR 451 & added TO load management program | June 1, 2012 |
| 3.3 4.2 6.1 | 1.0 / 5 1.0 / 8 1.0 / 10 | Updated step 3 Added Desktop Guide to VDI reference Updated PUCT Daily Report, NERC and DOE Reporting and RCIS Posting | July 16, 2012 |
| 3.4 4.2 5.9 6.1 7.2 | 1.0 / 3 1.0 / 9 1.0 / 1 1.0 / 11 1.0 / 4 | Added CPT to procedure and Typical Subject line for e-mail Added Log to procedure Deleted Procedure Updated NERC and DOE Reporting Added 30 MIN ERS deployed to EEA 1 | August 29, 2012 |
| 2.2 3.1 5.3 6.1 7.6 9.1 | 1.0 / 1 1.0 / 2 1.0 / 4 1.0 / 12 1.0 / 3 1.0 / 2 | Added Hotline Call Communication Updated step 5 Updated and added Planned and Forced Outage sections. Added Weather Information section to PUCT Daily Report. Updated step 1 in NERC and DOE Reporting and ERCOT Morning Report section. Updated OCN, Advisory, & Watch Updated step E-mail All procedures in this manual have been reviewed. | November 1, 2012 |
| 3.2 3.3 3.4 3.5 3.6 3.7 3.8 4.1 5.2 5.3 5.5 5.6 5.8 6.1 6.2 6.3 7.4 7.5 7.6 8.3 8.6 9.2 10.1 10.2 11.0 | 1.0 / 4 1.0 / 6 1.0 / 4 1.0 / 1 1.0 / 3 1.0 / 4 1.0 / 2 1.0 / 3 1.0 / 1 1.0 / 5 1.0 / 3 1.0 / 3 1.0 / 2 1.0 / 13 1.0 / 2 1.0 / 2 1.0 / 3 1.0 / 3 1.0 / 4 1.0 / 2 1.0 / 1 1.0 / 6 1.0 / 2 1.0 / 5 1.0 / 1 | Updated step 1, Capacity Monitoring and deleted Reserve Monitoring Updated step 3 Updated notes and Management Notifications Updated purpose and step 1 Updated step 2 Updated step TCM & renamed LMP Map Delete procedure for large wind ramp events Updated step 1 Grammatical correction Updated step 3 Protective Relay or Equipment Failure Added MISO Reliability Coordinator Updated step 2 TO Temporary Equipment Limitation Notifications Updated purpose Updated step 1 Texas RE Event Reporting, Note and step 1 NERC and DOE Reporting, Loss of Firm Load NXT Notification Requirements, step 1 Weather Information section to ERCOT Morning Report, step 1 RMR Unexcused Misconduct Events, GMD, step 2 Gas Restrictions and added Special Protection Systems (SPSs) Deleted procedure Renamed to 6.2 and updated procedure Updated step Reporting Updated step Reporting Updated Log Updated step 2 Updated procedure Deleted Notice Builder Updated step 3 Updated step monitor, step 4 Building Security and Fire Alarms and step 3 Failure of the Emergency Generator Updated procedure Review New Communications from Manager and/or Control Room Operations Manager and step 4 Implement ERCOT Personnel and Company Standards | March 1, 2013 |
| 3.3 3.4 6.1 | 1.0 / 7 1.0 / 5 1.0 / 14 | Updated all steps Added 1st Note, deleted 2nd & 3rd Notes, Management Notification, updated QSE Notification, TO Notification Updated step Update Report | June 1, 2013 |
| 4.1 5.1 6.1 10.2 | 1.0 / 4 1.0 / 2 1.0 / 15 1.0 / 6 | Updated Ancillary Service Testing Coordination and added Coordinated Reactive Tests Added MISO Updated PUCT Daily Report & step 1 on NERC and DOE Reporting and added Note to NXT Notification Requirements Updated 1st Note and step #3 on Building Security and Fire Alarms | July 15, 2013 |
| 3.4 4.1 6.1 7.3 | 1.0 / 6 1.0 / 5 1.0 / 16 1.0 / 5 | Updated QSE Notification, TO Notification & Send E-mail Updated Coordinated Reactive Tests Added 7-Day Outlook, updated Event List on Texas RE Event Reporting & step 2 on GEO-Magnetic Disturbance (GMD) Updated table | August 9, 2013 |
| 3.3 | 1.0 / 8 | Removed HHGT TO reference | August 30, 2013 |
| 3.3 3.4 4.1 4.2 5.3 5.4 5.6 5.7 6.1 7.6 8.1 8.2 8.3 9.1 9.2 10.2 | 1.0 / 9 1.0 / 7 1.0 / 6 1.0 / 10 1.0 / 6 1.0 / 1 1.0 / 4 1.0 / 3 1.0 / 17 1.0 / 5 1.0 / 1 1.0 / 1 1.0 / 3 1.0 / 3 1.0 / 7 1.0 / 7 | Updated step 1 and Log Updated step Log Updated step Log Updated step Log Updated step 4, Planned Outage, Forced Outage and added Log Updated step Log Updated step Log Updated step 1 and added Log Updated step Update Report, TRE Event Reporting changed to Event Analysis Report and event list updated, and NERC and DOE Reporting updated Added step Issues and updated Log Updated step 3 and added Log Updated step 3, 5 and added Log Updated step 3 Updated step Log Updated steps Log Added step 4 and updated Log All procedures in this manual have been reviewed. | December 13, 2013 |